## Slide 1
MADMAX: A new Road to Axion Dark Matter Detection
OUTLINE:
MADMAX collaboration
The magnet
First results from seed setup
20 disc setup
Simulations
Outlook

## Slide 2
MADMAX @ MPP

## Slide 3
MADMAX MAgnetized Disc and Mirror Axion eXperiment
Collaboration forming on 18th Oct. 2017

## Slide 4
MADMAX MAgnetized Disc and Mirror Axion eXperiment
Collaboration forming on 18th Oct. 2017

## Slide 5
MADMAX:DESY as site!

## Slide 6
MADMAX MAgnetized Disc and Mirror Axion eXperiment
Mirror
Parabolic Mirror
10 T dipole magnet
Horn antenna (+ receiver)
80 adjustable dielectric discs
⊘: ~1m
Separate cryogenic volume
~2m

## Slide 7
Innovation partnership: First in MPG
Tedious 16 months EU tendering process: Aug. 2016 – Dec 2017
Two innovation partners: CEA-IRFU Saclay Bilfinger Babcock Noell, Würzburg
B2·A ≳100 T2m2 over 2m
MADMAX Magnet
100 T²m² dipole magnet: first ever
 Design Study  Prototype  Full scale magnet
One tender for whole magnet project!

## Slide 8
MADMAX Magnet
Design studies: investigate options

## Slide 9
MADMAX Magnet
Design studies: investigate options

## Slide 10
Fake axion
Signal analyzer (4 samplers, 1.4% dead time)
LHe bath → 4K THe + 5.5K TAmp = 9.5K TSys
Front end mixers and amps
Heterodyne detection:
MADMAX Receiver

## Slide 11
Inject fake 18GHz axion signal with 10-22 W power
Measurement for 28 hours (integrate signal): Receiver at LHe temp.
Cross correlation analysis (8kHz Lorentz shaped)
found ~5σ signal succesfully
For 1 week measurement: Sensitivity at the level of ~ few 10-23 W
Low noise preamp:
MADMAX Receiver: 1st measurements

## Slide 12
Inject fake 18GHz axion signal with 10-22 W power
Measurement for 28 hours (integrate signal): Receiver at LHe temp.
Cross correlation analysis (8kHz Lorentz shaped)
found ~5σ signal succesfully
For 1 week measurement: Sensitivity at the level of ~ few 10-23 W
Low noise preamp:
  s: Signal T: Testfunction (Lorentz, Gauss, …)
MADMAX Receiver: 1st measurements

## Slide 13
„Ab-sorber“
Dielectric discs (Saphire)
Horn antenna
Removable copper mirror
Mirror
Reflectivity measurement:
MADMAX Booster: Proof of Principle

## Slide 14
Reflectivity measurement:
MADMAX Booster: proof of principle

## Slide 15
Position reproducibility:
MADMAX Booster: proof of principle

## Slide 16
20 disc setup:
MADMAX Booster: proof of principle
Now available:
Reflectivity measurements with up to 20 discs
First results: Reproducibility of positioning without algorithm: ~ µm

## Slide 17
MADMAX 3D simulations
So far: boost factor vs. reflectivity correlation known only from 1D calculations
Need 3D simulation for “arbitrary geometries”
Test for non symmetric effects from
Geometries
Losses in materials
Tilting of discs
Surface roughness
…
using ELMER

## Slide 19
OUTLOOK:
Sensitivty for QCD dark matter axions with A=1m², B||=10T, Tsys= 8K, β2=5·104

## Slide 20
OUTLOOK:
Sensitivty for hidden photons with A=1m², Tsys= 8K, β2=5·104
tan δ ≲ 10-4 (???)

## Slide 21
Collaboration officially founded
DESY wants to host MADMX
Magnet innovation partnership with Bilfinger Babcock Noell CEA IRFU
First results from proof of principle setup promising
20 disc proof of principle setup available
Started 3D simulations
Goal: Build prototype until 2021  first physics results
OUTLOOK:

## Slide 22
Low noise preamp:
InP HEMT preamplifier from LowNoiseFactory
Frequency range: 6-20 GHz detector noise: T~7K (measured, quick and dirty) Tds~ 6K (data sheet)
First measurements:
22

## Slide 23
  → Sapphire (Al2O3) @ 300K, 10 GHz:
Chose dielectric material:
  High dielectric constant (for large boost & conversion)
  Low loss → low tan δ (reduce photon losses)
  Stable
  Cheap
  → Lanthanide Aluminate (LaAlO3) @ 77K
  → Titanium dioxide – Rutil (TiO2)
0.001(?)
MADMAX Booster: Dielectric plates