## Slide 1
LMU München - Excellence Cluster Universe
UPDATE on Services and PS
Stefan Rummel

## Slide 2
Services
Stefan Rummel
2
Kapton-Flex development
  Test production @ Taiyo submitted on 20.1.11
  Flex length from 30cm to 50cm
  Realistic designs including power & TML
  Realistic design with washer
   Testing of signal integrity and power distribution
New design for cable – incorporating:
  Our findings regarding wire diameter  AWG14/18 instead of AWG12
  Forward service space required to limit diameter
  Radiation hard till 50MRad (according to company)
  Double cable with 14.5mm diameter each
Patch panel design assuming Vienna’s mounting concept
  Space for PP seems to fit including decoupling on PP-level
  Further design iteration necessary for KEK SVD-Layer 1 design

## Slide 3
PS Development – Organisation
Stefan Rummel
2
Group from Krakow interested to join the PS development effort
  Already started with hardware tests
  Will look into Overvoltage protection / Hardware safety system
Firmware development together with TUM/Fortiss is ongoing
  Collecting requirements on Firmware and PS-Slowcontrol interface
  First preselection of microcontrollers done
  Safety analysis of PS-system ongoing

## Slide 4
PS Development
Stefan Rummel
3
Design of multichannel prototype finished – “Analog Prototype”
  Digital interface via DAC-PCI card and ADC
  Organized in 4 modules with 4 channels
  Flexible design:
    With/without remote sensing
    Positive- or Negative Output, sink or source
    Flexible over current protection
    Monitoring of currents and voltages
    Status outputs
  Will allow to verify the analog building blocks and multi channel operation
Design of micro controller card for steering has started (“MCU-Card”)
Next steps / outlook
  Finish MCU-Card
  Integration of ADC/DAC into “Analog Prototype”
   Full scale prototype till end of this year