## Slide 1
CO2 Cooling of PXD Endflange:
Results from Karlsruhe
T. Barvich, S. Heindl, Th. Müller, H.J. Simonis and Th. Weiler Belle II General Meeting (via EVO) 07.04.2011

## Slide 2: Overview
Three slides specially prepared:
Cooling tests in Karlsruhe
Results
Test at CERN
+ Backup Slides from Bonn DEPFET workshop
Belle II PXD (by MPI)

## Slide 3: CO2 Cooling Tests in Karlsruhe
Open CO2 system
Endflange prototype (DLMS) from MPI
Silicon with resistors as module dummies
Several Pt1000s for temperature monitoring
Fully equipped flange in test setup
CO2 bottle in freezer to save gas
Flow and pressure control
Pt1000

## Slide 4: Results
Temperature difference (@ 100 W): ca. 20°C
Target reached (stay below 0°C) and even 120 W possible
0
60
80
100
120
Power load: (in Watts)
Max. power for ¼ of PXD:
Cooldown: 3 mins
Temperature [°C]
Time [s]
Milestone: first proof of working cooling solution für Belle II PXD!

## Slide 5: Closed CO2 system at CERN
Closed CO2 system built by the group of B. Verlaat and H. Postema
Based on experience with AMS and LHCb systems
Test same endflange prototype under „real“ operating conditions
Testing is currently underway (April 04 to April 08)
(CERN)

## Slide 6: Backup Slides from Bonn
Unchanged!

## Slide 7: 1. Open CO2 system in Karlsruhe
Built for CMS Tracker Upgrade
Now used for Belle II PXD cooling tests
Manual operation  limited runtime
3. flow control
2. endflange
1. CO2 bottle
readout PC

## Slide 8: 1. Open CO2 system in Karlsruhe
Components of the system:
1. CO2 bottle with pressure regulator, precooled to -32°C (saves CO2)
2. endflange prototype in air-flushed box to prevent condensation
steel tube
dry air
Armaflex insulation

## Slide 9: 1. Open CO2 system in Karlsruhe
Components of the system (cont‘d):
3. electric heater (temp. controlled) to prevent liquid CO2 from reaching the gas flow meters
from flange
3. gas flow meters (combined) and pressure gauge for controlling operating values
outlet (window)

## Slide 10: 3. Results with heat load
First test in December:
Large oscillations related to leaky connection
Temperature difference (@ 100 W): about 19°C
Power loads: (in Watts)
0
60
20
40
110
120
100
80
90
70

## Slide 11: 3. Results with heat load
Second test in January: leaky connection fixed
Temperature difference (@ 100 W): about 20°C
Remaining oscillations common to open CO2 systems
0
60
80
100
120
Power loads: (in Watts)

## Slide 12: 3. Results with heat load
now: closer look at different areas of flange
1. connection side:
all probes within a range of 5°C
0
60
80
100
120
Power loads: (in Watts)
A1
A4
A6
connection

## Slide 13: 3. Results with heat load
2. front side:
much larger deviation of 24°C
probe A2: bad contact (without: 11°C)
0
60
80
100
120
Power loads: (in Watts)
front
A3
A2
A5
A7

## Slide 14: 4. Conclusion
Cooling and Mechanics workpackages have passed a milestone: first proof of working cooling solution for Belle II PXD!
Minor problems identified: quality of flange surfaces and threads needs to be improved in next iteration  even better results expected
Next steps: - test with closed CO2 system - how to get a working system for Belle II?