## Slide 1: Belle II SVD/PXD Installation Procedure
Mockup Meeting Munich

## Slide 2: SVD Skeleton

## Slide 3
The heavy metal masks are completed.
Crotch Piece
Beam Pipe
Beam Masks
Beam Mask Support
Assembly Support Stand
Beam Masks
QCS Decouple Ring

## Slide 4
PXD is assembled to two halves in another stage and put together to the beam pipe. Cables and tubes will go to the slot in the masks.
PXD
Kapton
Patch Panel

## Slide 5
SVD is also assembled in another stage. The forward and backward support cones are then fixed with the outer cover, made of CFRP.
Then they are put together around the beam pipe.
SVD half shells will be attached from the side
SVD will be preassembled before joined with the BP-PXD assembly

## Slide 6: Endflange
Schematic draft
Constraint:
Acting as shielding BG
CDC connection
SVD connection
BP conection
Assembly work will be perform for SVD and BP in parallel
SVD flange
BP flange

## Slide 7
SVD has to be self-supporting. SVD is pushed in by the cryostat.
Cabling and tubing is pre-installed and routed along the QCSR and resting in the tray.
This procedure is proposed by KEK and will be tested with a mockup.
Tray
SVD
QCSR
cryostat
koike
Conceptual view

## Slide 8
Side view
After move-in of the QCSR cryostat
After the installation of SVD, this junction must be decoupled so that a shift of the cryostat after exciting every magnet does not interfere with the SVD.
koike
koike
koike
This ring fixes the SVD

## Slide 9
Support point
2.5m