## Slide 1: HLT → PXD
T. Higuchi

## Slide 2: 0th Version Sketch
Boundary conditions
  HLT rate ~ 10kHz (design = 6kHz)
  Track multiplicity ~ 15 (Belle = 10)
  PXD: (768 rows) x (250 cols) x (40 half-ladders)
HLT #01
HLT #02
HLT #10
…
HLT→ATCA
ATCA #01
ATCA #02
ATCA #40
…
Switch
1kHz / HLT
inbound
outbound

## Slide 3: 0th Version Inbound Packet
Header
Trailer
Exp#
Event # [31-0]
TT tag
Word #
Checksum
Run#
0
31
16 15
Track-#01 helix params.
Track-#02 helix params.
Track-#nn helix params.
…
x5 double precision floating points
= 40 bytes
Pivot = (0,0,0) is assumed.
16 bytes
~400 bytes
4 bytes
~800bytes x 1.0kHz x 10HLT = 800kB/link x 10 HLT
Safety factor = (800/420) * (10k/6k) = 3.2

## Slide 4: 0th Version Outbound Packet
Header
Trailer
Exp#
Event # [31-0]
TT tag
Word #
Checksum
Run#
0
31
16 15
Track-#01 RoI
Track-#02 RoI
Track-#nn RoI
…
16 bytes
4 bytes

## Slide 5: RoI
Suppose RoI is rectangular shape.
(φ₀,z₀)
φ … 0 to 249 = 8 bits
z … 0 to 767 = 10 bits
δφ = 16 cols? … 4 bit
δz = 32 rows? … 5 bit
Half ladder ID … 0 to 39 = 6 bits
(φ₁,z₁)
6 + 8 + 10 + 4 + 5 = 33 bits → 64 bit (48 bit possible?)
NOTE: every track has at least 2 associated PXD associated (layer-1 and layer-2).

## Slide 6: RoI Across Ladders
Case (A)
Case (B)
Case (C)
  Combination of (A) + (B).
Need to survey for the fraction of the across-ladder RoI.
But let’s say
50% of tracks have 2 RoIs (usual case).
Remaining 50% have 4 RoIs.
3 RoIs / track in average

## Slide 7: 0th Version Outbound Packet
Header
Trailer
Exp#
Event # [31-0]
TT tag
Word #
Checksum
Run#
0
31
16 15
Track-#01 RoI
Track-#02 RoI
Track-#nn RoI
…
16 bytes
4 bytes
3 RoIs x 64 bits = 24 bytes
~240 bytes
~400bytes x 10kHz / 40ATCA = 100kB/link
Safety factor = (400/260) * (10k/6k) = 2.6