## Slide 1: Calorimetry of the Future & the T3B Experiment
Young Scientist Workshop – July 25th 2012
Christian Soldner, Lars Weuste, Marco Szalay
Max-Planck-Institute for Physics
Pirate Lecture Session 2012
( Arrrrrrrrrrrr!!! )

## Slide 2: Outline
Look for the Superlative:
Let’s hunt for the best future calorimeter
(for the future linear e+e- collider CLIC with 3TeV CM Energy)
Faster?
More?
Bigger?
Perfect Calorimeter

## Slide 3: What’s a calorimeter?
At a collider:
  Many particles created at collision
  What is their energy? How do we measure it?
Avast! Cut ye landlubber particle in pieces and scavenge them to see how many ye get!
Force particle into a series of hard interactions: Shower
  Using dense absorber material (steel, tungsten, …)
  Each reaction creates secondary particles (e.g. electrons, pions)
  If no energy left: Shower is stopped
   Number of secondaries N ∝ energy of initial particle E
  Works for and hadrons
Statistical Error:
Resolution:
2

## Slide 4: State of the Art Technology (At lhc)

## Slide 5: State of the Art Technology (Hadron Collider)
ATLAS: Readout:
ECAL: - Liquid Argon + Lead Absorber Plates  Cu/Kapton Electrode
HCAL: - Plastic Scintillator + Steel Absorber  Photo Multiplier Tubes
Calorimeters located outside of the Solenoid
 | 45 GeV | 500 GeV
 | 15% | 4%
 | 45 GeV | 500 GeV
 | 15% | 4%
10%/
45%/

## Slide 6: State of the Art Technology (Hadron Collider)
CMS: Readout:
Ecal: - Lead Tungstenate Crystals  Avalanche Photodiodes
HCAL: - Plastic Scintillator + Brass Absorber  Hybrid Photodiodes
Calorimeters located inside of the Solenoid
 | 45 GeV | 500 GeV
 | 19% or 12% | 5%
 | 45 GeV | 500 GeV
 | 19% or 12% | 5%
3%/
100%/

## Slide 7: How to Design a Future Calorimeter? (for a E+E- COLLIDEr)
???

## Slide 8: Big?
Let’s look for Superlatives:
Why don’t we build the biggest Calorimeter in the world?
Compare: ATLAS: 12m in beam direction, 8m diameter
Look at what’s important:
Would be nice if we could find someone to pay for it at some point!
Hermitic  leakage deteriorates the jet energy measurement
 needed to reconstruct missing E
ρ(CAL) determines size
Atlas: ~25 , ~10
 Bigger is not better
Steel | Tungsten | Gold
~ 8 | ~ 19 | ~ 19
~ 5-10 €/kg | ~ 100 €/kg | ~ 40000 €/kg
Steel | Tungsten | Gold
~ 5-10 €/kg | ~ 100 €/kg | ~ 40000 €/kg
Compare: CMS: 2.95m in diameter
What about “small”?
Advantage: CAL fits inside the solenoid  no dead material between trackers and CAL
But: most dense material to consider: Tungsten
Let’s try that

## Slide 9: More?
How about millions of readout channels in the CAL?
Compare: ATLAS: ~10.000 in the Hcal (TileCal)
Energy depositions in Cal combined to towers
 space requirements
 cost efficiency
 reduce no of readout channels (data transfer)

## Slide 10: More?
How about millions of readout channels in the CAL?
Compare: ATLAS: ~10.000 in the Hcal (TileCal)
Energy depositions in Cal combined to towers
 space requirements
 cost efficiency
 reduce no of readout channels (data transfer)
With say 8 million readout channels (HCAL):
Note: This just makes sense in the clean environment of a e+e- collider

## Slide 11: More?
How about millions of readout channels in the CAL?
Realize this with millions of PMTs?  hardly
Need to exploit
new technologies!
Use novel Silicon Photomultipliers:
Small
Insensitive to B-Fields
Low Voltage operation (~30-70V)
At last:
Photo Sensor, Scintillator Tile and Readout Electronics integrated in active layer
(other approaches: (Semi-)Digital HCAL…)

## Slide 12: More?
How about millions of readout channels in the CAL?
Why did we want this again?
Momentum measurement of tracking system better (for particles whose track is bent enough
~100GeV in case of ILD)
 | Average Jet Composition(LEP)
Charged particles | 62%
Photons | 27%
Neutral Hadrons (long lived) | 10%
The Particle Flow Idea:
Reconstruct each particle in a jet in the subdetector which can provide the best energy measurement
Calorimeters need to categorize and assign energy depositions
Ultra fine segmentation and
Intelligent clustering algorithms necessary
It certainly looks nice!
But main reason:
Try to build the best possible calorimeter
to minimize its usage
because calorimeters are bad.

## Slide 13: Particle Flow
Calorimeters need to categorize and assign energy depositions to incoming particles
ECAL  Photons HCAL  Neutral Hadrons
Unprecedented Jet Energy Resolution:
 3x better than LEP
2x better than
conventional
 5.2% using raw calo energy
45 GeV | 3.7%
100 GeV | 2.9%
180 GeV | 2.8%
250 GeV | 2.8%
375 GeV | 3.2%
500 GeV | 3.5%
45 GeV | 3.7%
100 GeV | 2.9%
180 GeV | 2.8%
250 GeV | 2.8%
375 GeV | 3.2%
500 GeV | 3.5%
For Jets >100GeV: JER dominated by confusion not by the Energy Res of Calorimeters!

## Slide 14: Faster?
Could the calorimeter be so fast that we can observe the time development of e.g. hadronic showers?
But:
Equip every calorimeter channel with a TDC (Time to Digital Converter)
Assign a time stamp to every energy deposition
A next generation HCAL prototype is on the way equipped with such TDCs
(time resolution ~100ps)
The question is: Why should we care?
Not directly.
Energy depositions cannot be sampled (like on an oscilloscope)  too much data
 more later
13

## Slide 15: Faster?
1. Because of the design of CLIC
CMS Energy | 3TeV
Bunch Separation | 0.5ns (25ns@LHC)
Bunch Train Length | 156ns
CMS Energy | 3TeV
Bunch Separation | 0.5ns (25ns@LHC)
Bunch Train Length | 156ns
Clean environment of a e+e- collider?
 Detector activity when integrating over half a bunch train
150 BXs (75 ns) in ILD-like detector
High rate background: γγ
Origin: Beam Focusing  Bremsstrahlung
Occurrence: ~13 particles/BX
Interesting Physics: << 1/Bunch Train
Time stamping can clean up the detector

## Slide 16: Faster?
2. Hadronic showers are not instantaneous
Process:
Heavy absorber nuclei get struck inelastically
Nucleus can be excited
Relaxation
  emission of a late neutron / photon
Inelastic scattering within the active layers
Ignoring late energy depositions deteriorates the JER (like leakage)
Compromise necessary:
Good Jet Energy Resolution Efficient Background Rejection
Are those timing studies true?
 Rely heavily on correctness of GEANT4 simulations (i.e. its physics lists)
Timing properties of hadronic showers in a tungsten calorimeter so far untested
This is where the Tungsten Timing TestBeam experiment (T3B) comes in!

## Slide 17: T3B
The journey to measure shower timing

## Slide 18: The T3B Experiment within the CALICE AHCAL
CALICE
(calorimeter for the linear collider experiment)
Prototype for a future highly granular HCAL
38 layers of scintillator and tungsten absorber
1x1x1 with about 8000 channels and 5
+ 3D reconstruction of hadronic shower shapes
- No timing information on the showers
Test Beams: PS 10/2011, SPS 6,7,9,10/2011
Absorber: Tungsten and Steel (for comparison)
Particles: Hadrons from 10 to 300 GeV
CALICE AHCAL
T3B Layer
Shower Shape of a 300GeV pion Event

## Slide 19: What is T3B?
What is T3B?
One layer of 15 scintillator tiles
Tile dimensions: 3 x 3 x 0.5 cm3
Light Readout by SiPMs
Data Acquisition: 4 fast USB Oscilloscopes
Setup optimized to observe the time development of hadron showers
3cm

## Slide 20: SiPMs
1mm
Hamamatsu SiPM: 1600 pixels  each pixel can measure single photons
 # fired pixels # measured Photons Energy deposition in Scintillator
Average
Typical waveform of 1 pixel firing
19

## Slide 21: Data Analysis
Waveform of Total
Acquisition window
T3B Waveforms:
Appearance of a typical event at one T3B channel  @ 10GeV
High short energy deposition, followed by potential late Edeps

## Slide 22: Novel Data Processing Method
Waveform Decomposition:
Iteratively substract 1 pixel waveform from the local maximum till nothing is left
Obtain time of energy deposition with sub-nanosecond precision
http://www.mpp.mpg.de/~soldner/WaveformDecomposition.gif

## Slide 23: Data Analysis: Waveform Decomposition
Verify the success of the procedure:
Build up the original waveform from the 1p.e. hit histogram  good agreement

## Slide 24: Data Analysis: Waveform Decomposition
Verify the success of the procedure:
Build up the original waveform from the 1p.e. hit histogram  good agreement
Analysis of the time of first hit within the tiles of the T3B layer
The time of first hit is a good measure for the intrinsic time stamping possibilities in the calorimeter

## Slide 25: Data Analysis: Waveform Decomposition
Verify the success of the procedure:
Build up the original waveform from the 1p.e. hit histogram  good agreement
Analysis of the time of hit within the tiles of the T3B layer
The time of hit is a good measure for the intrinsic timing properties of hadronic showers

## Slide 26: Analysis: The Time of the first Hit

## Slide 27: Time of First Hit
Analysis:
Consider a hit if > 8 p.e. are deposited within 9.6 ns
Take the time of the second fired SiPM Pixel as the TofH
(reduced bias through thermal darkrate  on average 1 pixel per waveform of 2.4 microsec)
Sum the number of pixels fired within the identified hit to determine its energy deposition
Tungsten Data
60GeV
All Tiles
[MIP]
Muon Data
180GeV
All Tiles
[MIP]
Steel Data
60GeV
All Tiles
[MIP]

## Slide 28: Time of First Hit
Analysis:
Consider a hit if > 8 p.e. are deposited within 9.6 ns
Take the time of the second fired SiPM Pixel as the TofH
(reduced bias through thermal darkrate  on average 1 pixel per waveform of 2.4 microsec)
Analysis of the time of first energy deposition within the tiles of the T3B layer for hadronic showers
Striking difference between Tungsten and Steel data
Sum the number of pixels fired within the identified hit to determine its energy deposition

## Slide 29: Time of First Hit
Determine binwise mean time of first hit:
First hit on average later for Steel and Tungsten
Steel: Late hits deposit few energy
Tungsten: Late hits can deposit few or much energy
No significant energy dependence observed
Analysis:
Consider a hit if > 8 p.e. are deposited within 9.6 ns
Take the time of the second fired SiPM Pixel as the TofH
(reduced bias through thermal darkrate  on average 1 pixel per waveform of 2.4 microsec)
Sum the number of pixels fired within the identified hit to determine its energy deposition

## Slide 30: Analysis: The Time of the hit

## Slide 31: Time of Hit Analysis
Analysis Steps (All plots for Hadron Data, 60GeV, Tungsten, 4mio Events):
Fill the time of every single fired pixel into one timing histogram (per E and tile)
Typical T3B event for hadron data
Pedestal
Gaussian smearing  width of 1.7ns
Fast energy depositions
Various late contributions
Correct for Detector Effects: Pedestal sub., substract SiPM afterpulsing…

## Slide 32: Time of Hit Analysis
Analysis Steps (All plots for Hadron Data, 60GeV, Tungsten, 4mio Events):
Fill the time of every single fired pixel into one timing histogram (per E and tile)
Correct for Detector Effects: Pedestal sub., substract SiPM afterpulsing…

## Slide 33: Time of Hit Analysis
Now we can determine the
Mean Time of Hit
http://www.mpp.mpg.de/~soldner/Shinshu2012/SummedTimeOf1pe.gif
Tile Position
Mean Time of Hit [ns]
http://www.mpp.mpg.de/~soldner/Shinshu2012/SummedTimeOf1pe-EnergyScan.gif
Energy Scan
Tungsten Data 60,80,180GeV
 No differences in terms of ToH
Analysis Steps (All plots for Hadron Data, 60GeV, Tungsten, 4mio Events):
Fill the time of every single fired pixel into one timing histogram (per E and tile)
Correct for Detector Effects: Pedestal sub., substract SiPM afterpulsing…

## Slide 34: Time of Hit Analysis
Analysis Steps (All plots for Hadron Data, 60GeV, ~4mio Events):
Which fraction of the total Energy is deposited at which time?
Compare Muon, Steel And Tungsten Data
Time [ns] | Fraction Mu [T3B] | Fraction Steel [T3B] | Fraction W [T3B]
5 | 77% | 69% | 56%
10 | 88% | 83% | 74%
24.5 | 94% | 91% | 88%
Edep takes longer for Tu than for Steel absorber (than for Muon data)
Compare Hadron Data to MC for Tungsten
Monte Carlo Comp.:
High precision physics lists reproduce shower timing of Tungsten reasonably well
 Discrepancies in late shower timing observable

## Slide 35: Analysis: Recovery of the third Dimension

## Slide 36: Recovery of the 3rd dimension
T3B is a single strip detector
  1D: Shower center  border
  One time dimension
   2 dimensions
We are interested in full 4D description of hadronic showers!
  Assume rotation symmetry
    Recovery of 1D
  But: Longitudinal component still missing
Reminder: T3B is parasitic to A-HCal
  3D “imaging” calorimeter in x/y/z
  Maybe 4D = 3D + 2D?
CALICE AHCAL
T3B Layer

## Slide 37: Synchronisation: Calice to T3B
T3B and CALICE A-HCal use the same trigger signal
Data can be synchronized offline
T3B Tile Geometry
Energy Depositions within Calice Scintillator Tiles
Beam Direction
T3B Tile Geometry
Shower start relative to T3B
First hadronic interaction
Happens in a certain depth
Can be identified in CALICE A-HCal
Ordering of T3B Hits relative to the shower start
Recovery of longitudinal dimension
Eventdisplay:
Hadron Data @ 60GeV (Tungsten)

## Slide 38: Synchronization Crosscheck: Hit probability per layer
If shower starts late, only central T3B tiles are hit
If shower starts in front of HCal, all T3B tiles are hit
38
A-HCal
T3B
1
38
A-HCal
T3B
1
1
15
 Sync is ok

## Slide 39: Mean time of first Hit
Time of Flight: ≈3.3ns
Mean shower development of first hits:
On shower axis: fast (few ns)
Off shower axis up to 10 ns
38
A-HCal
T3B
1
1
15
T3B can really show the average development of hadronic showers!
(by using AHCal information)
38

## Slide 40: A hadronic shower in “4D”
Passing particle can be clearly seen
Response only slowly wears off

## Slide 41: Summary

## Slide 42: Summary
We saw how a calorimeter of the future could look like
Using the Particle Flow concept an unprecedented jet energy resolution of is achievable
CALICE is a prototype of a highly granular calorimeter with 8000 channels
  Testing if the performance requirements can be met
T3B is a new experiment testing the time development in hadronic showers
  First results manifest that the standard GEANT4 physics list QGSP_BERT does not reproduce shower timing correctly
  A high precision extension to the list is needed to fit the data
There is still a lot of potential in the taken test beam data  analysis ongoing

## Slide 43: Backup

## Slide 44: Results: Data vs. MC
First Robust Comparison of Data vs. MC with a timing key parameter:
Determine the mean time of first hit cell by cell
Note:
Beam axis through T3B tile 0
Tile 10 is 30cm from beam axis
Data very well reproduced with QGSP_BERT_HP
QGSP_BERT overestimates late contributions at large radii
First Data vs. MC comparison delivers valuable information:
 The GEANT4 physics list QGSP_BERT (standard for ILC, LHC simulations) does not reproduce the timing properties of hadron showers correctly, but the High Precision extension does!

## Slide 45: Summary
We presented preliminary results on the time structure of hadronic showers
  Setup: Investigated π- events at 10 GeV in the CALICE WHCAL at 3 lambda depth
  using the T3B Timing Layer
  In the presented analysis we used the time of first hit as key parameter for the time structure of hadronic showers
  Data vs. MC comparison shows excellent agreement for QGSP_BERT_HP and large discrepancies for QGSP_BERT
  More timing analyses from the T3B group will follow…