## Slide 1: Update on FOS monitor Ringberg Castle, 13th DEPFET Workshop
E. Currás, D. Moya, I. Vila, A. L. Virto.,J.González
Instituto de Física de Cantabria (CSIC-UC)
G. Carrión, M. Frövel.
Instituto Nacional de Técnica Aeronautica (INTA)

## Slide 2: Outline
FOS-based L-shape
Calibration of L-shapes
  Temperature calibration
  Displacement calibration: Stability, Reproducibility, linearity.
  Other issues: fixation and improved contact.
Outlook

## Slide 3: L-shape basics
Temperature & strain to displacement transducer with custom geometry for integration in PXD
Readout speed from zero to 1KHz (vibrations)
Currently three demonstrators manufactured
Contact surface
Contact ball
Locked part
FBG sensors

## Slide 4: L-Shape Demostrators
One millimiter Diameter Quartz contact ball
L-shape tip
ball glued
Clamping system

## Slide 5: FOS Monitor Timeline
2009 Oct FOS Monitor proposal
2010 Jan Omega-shape proposal
2010 Oct. FOS radiation hardness study (1.5 GRads ,3.3 1015 p/cm2)
2011 January First omega mechanical dummies
2011 Sept. FOS radiation hardness study ( 10 Mrads )
2011 Dec Proof-of-concept-prototype omega
2012 Feb Omega calibration.
2012 March New transducer design L-shape
2012 May Test in depfet mock-up at IFIC
2012 October L –shape calibration
(resolution less 1 um ,accuracy≈10 um )
2013 May Test in mock-up at IFIC (N2 atmosphere)
2013 June-July Omegas and L-s irradiation ELSA
2014 January commissioning at PXD-SVD common test beam
,
Notes: Poner primero el año
Poner omega-shape
Test in first Depfet mock-up
Poner punto de la calibración

## Slide 6: Thermal calibrations & temperature compensation
Calibration using a SIKA thermocouples calibrator.
The sensitivity of three sensors was constant and near the same (difference<0.6%)
Maximum deviation < 3 pm (0.3 ºC)
Error X 10
Error X 10
Error X 10
Trivial approach to temperature compensation

## Slide 7: Displacement Calibration
D.Moya, LC2013 Tracking-Vertex session, Desy May. 30th 2013
Contact ball
Contact
surface
Micrometric stage
L-shape
Displacement measured with Michelson interferometer for high precision calibration (tenth of a micron)
Readout of L-shape compared with true position (interferometer)

## Slide 8: L-shape Output Stability
Short term studies (temperature constant ± 0.1° )
Continuous readout of the sensor output.
Stabilities below or about 1um (convolution with mechanics stability)
RMS ≈ 0.6 um
RMS ≈ 1.1 um

## Slide 9: L-shape Linearity vs. Displacement
Calibration over a range of 1mm
Resolution (readout resolution) 0.5 um.
Accuracy (diff. Between inter & L-shape) ≈ 2 um
Sensitivity 1.2 pm/um

## Slide 10: L-shape Linearity (2)
L-shape sensibility presents a small dependence depending of the direction of movement (L-shape specific effect due to its shape)
Sensitivity reproducibility
0.4 %
Difference load-unload cycle
2 %

## Slide 11: L-Shape Linearity (3)
Investigate the effect of the roughness of the contact surface on the asymmetric load-unload behavior.
POLISHING
OF CONTACT SURFACE
Still sensitivity asymmetry 2 %
More studies in progress
(harder materials than Al)
Still sensitivity asymmetry 2 %
More studies in progress
(harder materials than Al)

## Slide 12: L-Shape sensitivity to enviromental conditions: HR%, T, N2
No sensitivity to environmental conditions

## Slide 13: Outlook
In-depth calibration of L-shapes
Accuracy of few tenths of degree and few microns demonstrated
Short term and in progress activities:
  Asymmetric linearity (2%) for loading and unloading movements (improve the ball-surface contact).
  Radiation tolerance of the L-shape as a whole (ESLA irradiation).

## Slide 14
BACK UP