## Slide 1: The Belle II Vertex Pixel Detector
fmu@mpp.mpg.de
IMPRS Young
Scientist Workshop
July 16 - 19, 2014
Ringberg Castle
Kreuth, Germany
Felix Mueller

## Slide 2: Outline
SuperKEKB and Belle II
Vertex Detector (VXD)
Pixel Detector (PXD) and its characteristics
DEPFET technology and working principle
The readout electronics
Gated Mode Operation
Production / Technology Issues
Lab Measurements and TestBeam with PXD6
Summary and future plans

## Slide 3: SuperKEKB upgrade
Belle II
Nano beam scheme  smaller beam size (~nm) & increased beam currents (x2)
L = 8 x 1035 cm-2 s-1 (40 times larger than in KEKB)
Ee- = 7 (8) GeV & Ee+ = 4 (3.5) GeV
(bg = 0.42 (KEK)  0.28 (SuperKEK))
Ecm = 10.58 GeV - Y(4S)
positron (4 GeV)
electron (7 GeV)
5.0 m
7.4 m
Changes involving the Vertex Detector (VXD):
Four layers of Double Sided Si-Strip Detector (DSSD) with a larger radius
Two layers of DEPFET pixel detector (PXD)
see Martin‘s talk

## Slide 4: Vertex Detector (VXD)
Tasks of the vertex detector:
reconstruction of primary, secondary, … vertices of short-lived particles
  decay of particles is typical in the order of 100 µm from the IP
detect tracks of low momentum particles (in high B field) which cannot make it to the main tracker
  Innermost detector system as close as possible to IP
  highly granular pixel sensors; provide most accurate 2D position information
  should be massless and still provide a large enough S/N
  Design and specifications to a larger extent driven by machine/beam characteristics
    Beam background, radiation
    damage, occupancy …

## Slide 5: Vertex Detector (VXD)
Silicon Vertex Detector (SVD)
4 layers of double sided silicon strip detector
R= 3.8 cm, 8.0 cm, 11.5 cm, 14 cm
Pixel Detector (PXD)
2 layers of DEPFET pixels
R = 1.4 cm, 2.2 cm
Beam pipe: R=10mm

## Slide 6: PXD detector requirements
Occupancy | 0.1 hits/µm²/s
Frame time | 20 µs (rolling shutter mode)
Momentum range | Low momentum (<1GeV)
Acceptance | 17°-150°
Radiation | ~20 kGy/year, 11010 n/ab-1cm²
Belle II is dominated by low momentum tracks
Modest intrinsic resolution (15 μm), dominated by multiple scattering → Moderate pixel size (50 x 75 μm²)
Lowest possible material budget (0.2% X0/layer) [including ASICs]
due to higher background (20x-40x): Radiation damage and occupancy, fake hits and pile-up noise
10x higher event rate => higher trigger rate
Replace inner layers of SVD with PXD

## Slide 7: Mockup of the Belle II PXD Detector
Beam pipe radius:
10 mm (inner), 12.5 mm (outer)
Half Ladder

## Slide 8: Half Ladder of DEPFET PXD
 | Inner layer (L1) | Outer layer (L2)
# modules | 8 | 12
Distance from IP (cm) | 1.4 | 2.2
Thickness (µm) | 75 | 75
Total # pixels | 3.072 x 106 | 4.608 x 106
Pixel size (µm2) | 55, 60 x 50 | 70, 85 x 50
Sensitive area (mm2) | 44.8 x 12.5 | 61.44 x 12.5
Sensor length (mm) | 90 | 123
Frame/Row rate | 50 kHz / 10 MHz | 50 kHz / 10 MHz
256 x 250 pixels
55 x 50 µm² (L1)
70 x 50 µm² (L2)
512 x 250 pixels
60 x 50 µm² (L1)
85 x 50 µm² (L2)
~0.2%X0 per layer

## Slide 9
impinging
particle
Clear
Turn on DEPFET
source
Gate
DEPFET (DEPleted p-channel Field Effect Transistor)

## Slide 10: DEPFET (DEPleted p-channel Field Effect Transistor)
A DEPFET is a MOSFET onto a sideward depleted silicon bulk
Impinging
particle
→ Low noise
→ Low power
→ High signal/noise-ratio
→ Non-destructive readout
Cross-section of a DEPFET
internal amplification:
gq0.5 nA/e-
90 steps fabrication process
9 Implantations
19 Lithographies
2 Polysilicon layers
2 Aluminum layers
1 Copper layer
Back side processing

## Slide 11: Control and readout electronics
SWITCHER
Fast voltage pulses up to 20 V to activate gate rows and to clear the internal gate
JTAG for interconnectivity tests
64 output drivers for both gate and clear channels  address 32 matrix segments
768 rows  192 electrical rows  6 ASICs needed per module
Drain Current Digitizer (DCD)
Keeps the columns line potential constant
8 bit ADCs
Compensates for pedestal current variation (2bit DAC)
Programmable gain and BW
256 input channels (4 per module)
Data Handling Processor (DHP)
Pedestal correction
Common mode correction
Data reduction using the zero suppression
Triggered readout scheme introduces
further data reduction
Controls the Switcher sequence
Kapton Flex cable
Power Supply via soldered contacts and bond wires
Data transmission via bond wires
4 layers, 48 cm
DEPFET

## Slide 12: Rolling Shutter Mode - Readout
Rolling Shutter Mode
Low power consumption; only one row is active; all are sensitive
Single Sampling (pedestal subtraction and common mode correction)
Readout time: 20 µs for entire frame (50 kHz)
Read-Clear cycle: 100 ns
one ADC per column

## Slide 13: Gated-Mode Operation
Continuous injection scheme; total rate: 50 Hz
Due to Liouville theorem injected bunches need to cool (4ms); results in „noisy“ particles
Very large occupancy („junk charge“)
If similar damping is assumed for SuperKEKB => 20% deadtime for PXD

## Slide 14: Processing
Phase I – before metal
Implantations
Polysilicon
Dielectric depositions
Phase II – Aluminum
Metal 1
Isolation
Metal 2
Phase III – Thinning & Copper
Handle Wafer Removal
Dielectric deposition
Metal 3
Passivation
front end of line
back end of line

## Slide 15: Thinning Technology
450 mm
50 mm
Etched grooves
Perforated frame

## Slide 16: Lab measurements and Beam Test
Switcher
B-18v1.0
DCDBv2
DHP0.2
seed charge
Laser scan 5x6 pixels
Test Beam,
2013
gq ~ 450 pA/e-
cluster charge
Laser scan 5x6 pixels
Homogeneous charge collection
PXD6
50x75µm²
50µm

## Slide 17: Large PXD6 Prototype Matrix – fully populated module
DCD-Bv2
Switcher-B18v2.0
DEPFET
DHP
DCD
SW
Belle II pixel cell design
640x192 pixels matrix
50x75x50 µm³ pixel cells
66 mm
16 mm

## Slide 18: Testbeam 2014 at DESY (Hamburg, GER)
Glue (between PCB and PXD6 module): Epotek 920 EL, cure at 120°C
Due to different coefficients of thermal expansion
⇒ Bowing of matrix (crest & valley: 80 µm at a distance of 1 cm)

## Slide 19: Vertex Detector and AIDA Telescope – Testbeam 2014
Telescope
Telescope
SVD
PXD
1 Tesla Solenoid Field
beam

## Slide 20: Setup – Testeam 2014 – DESY
Solenoid
BlackBox
PXD, SVD
Fibres
Power, Data cables, cooling pipe
BEAM
Telescope

## Slide 21: Results – Testbeam 2014 - DESY
Pedestal distribution
(dominated by induced stress)
non irradiated devices
Zero suppressed
frame
Zero suppressed
frame – laser spot
alignment
laser

## Slide 22: Results – Testbeam 2014 - DESY
DEPFET PXD6 HitMap
Beam Spot: 11 x 6 mm²
Cluster Signal
MPV ~ 15ADU

## Slide 23: DEPFET Collaboration
CNM/IFAE, Barcelona
Charles University, Prague
DESY, Hamburg
HLL, Munich
IFCA, Santander
IFIC, Valencia
IFJ PAN, Krakow
IHEP, Beijing
KEK-PF, Tsukuba
KIT, Karlsruhe
LMU Munich
MPI for Physics, Munich
TU, Munich
University of Barcelona
University of Bonn
University of Heidelberg
University of Giessen
University of Göttingen

## Slide 24: Summary
To fully exploit the high luminosity (increase by factor 40), the detector is currently upgraded
Excellent spatial resolution of ~ 15 mm; occupancy ~ 1%, fast readout (50 kHz frame rate), huge number of pixels (~ 8 Mpix) => fits all the requirements for Belle II
Complex DEPFET technology; fully functional; successful demonstration in lab and beam tests
Thinning of sensitive area down to 50µm / 75 mm (0.2% X0), minimizing multiple scattering;
Low power consumption ~ 18 W per ladder
ASICs and Sensors close to final version
Signal to Noise: ~ 40 (including noise from ASICs)
Many aspects not covered in this talk; though in development by the Collaboration

## Slide 25
Backup

## Slide 26: Radiation Tolerance
Gate Dielectrics: ~ 200nm
Radiation field at Belle II dominated by ~MeV electrons/positrons from QED beam background
Ionizing Radiation - Total Ionizing Dose (TID)
(~2Mrad/a at Belle II)
Positive fixed oxide positive charge  ∆VT
interface trap density 
  reduced mobility (gm)
  higher 1/f noise
Non Ionizing Energy Loss (NIEL)
(1012 neq/cm²/year at Belle II)
leakage current increase  shot noise
trapping not considered to be critical
Type inversion expected after 1014 neq/cm²

## Slide 27: Radiation Tolerance
R&D since 2008:
Reduce tox
Optimize gate dielectric layer
Vt(10Mrad): ~15V  3 V
The remaining small threshold
voltage shift can easily be
compensated by a shift of
the operating voltages
of the DEPFET!
 Safe operation for about 10 years in Belle II

## Slide 28: Belle II – Pixel Detector – Inner Layer
Inner layer
Kapton cables
Inner layer close to the IP (14mm)
Additional carbon fibers capillaries to cool the Switchers, if needed (not tested yet)

## Slide 29: Belle II – Pixel Detector – OuterLayer
Outer layer
PXD fully armored
Low material budget cooling
  Massive structures outside the acceptance to cool down the readout chips
  The center of the ladder rely on cold air

## Slide 30: Gated Mode – Simulations – trajectories of electrons
Clear
Internal Gate
VClear = 18V
VClear = 3V
Collection Mode
Blind Mode

## Slide 31: GM: Generation of Junk Charge – CCG dependance
1ADU
=
2.61 electrons
Generated charge:
185 000 e/h pairs
<1‰ of the generated charge accumulate in the internal gate
for ClearHigh ≥ 12V

## Slide 32: Generation of Junk Charge-Laser intensity dependence
1ADU
=
2.61 electrons
Generated charge
185 000,
370 000
555 000
e/h pairs

## Slide 33: Four Fold Readout
Gate
row 1
row 2
row 3
row 4
Drain
column 1
column 2
column 3
geometrically speaking
row 1
row 1
row 1
row 1
row 1
column 1 2 3 4 5 6 7 8 9 10 11 12
electrically speaking

## Slide 34: Cooling Issues

## Slide 35: Telescope HitMap – Testbeam 2014 - DESY
Beam: 5GeV, 1T Magnetic Field

## Slide 36: Further Talks related to Belle & Belle II
“The Belle/Belle II Experiment“
by Martin Ritter
“The Neutral Z-Vertex Trigger for Belle II”
by Fernando Abudinen

## Slide 37: Abbreviations
DCD = Drain Current Digitizer
DHP = Data Handling Processor
DEPFET = DEPleted p-channel Field Effect Transistor
IP = Interaction Point
MIP = Minimum Ionizing Particle
MPV = Most probable value
PXD = Pixel Detector
S/N = Signal to Noise Ratio
SVD = Silicon Vertex Detector (historivally based, meaning: silicon strip detector)
X0 = Radiation length = electron loses all but 1/e of itsenergy
VXD = Vertex Detector