## Slide 1
DCD 2bit DAC
Florian Lütticke
University of Bonn

## Slide 2: DCD DACs: what for?
Pedestal Distribution of Hybrid 6
Unirradiated

## Slide 3: DCD Channel Layout

## Slide 4: Issues with Data aquisition
DHP steers 2Bit DAC settings (640 Mbyte/sec)
LSB width steered by one DCD DAC
Design Issues in DHP02:
  Steering only works in ACQUISITION mode (not in AQUISITON TO MEM)
  Data acquisition in DHP stops synchronously
  2 Bit DAC output from DHP stops asynchronously
  Last written DAC Data stays on output line when DAC output is switched off

## Slide 5: DAC output: DACs switched off

## Slide 6: DAC output: DACs switched on – Acquisition to Mem

## Slide 7: DAC output: Normal acquisition
Leaving acquisition mode: DAC output gets static
Acquisition continues until the specified “last row” from DHP Settings

## Slide 8: DAC output: programmed Memory
Programmed pattern
Last row set to 0 (not good for normal acquisition)
Data acquisition will work with some tricks:
  DHH Memory bigger than matrix - if switching to static occurs after that we don’t have a Problem.
  Try often, do intelligent logic to sort out bad events.
Update DAC optimization algorithm
DAC Value = 3
DAC Value = 2
DAC = 0
DAC Pattern

## Slide 9: DAC outputs
Acquisition stopped somewhere here
Timing needs to be optimized