## Slide 1: Rad damage in direct detection
Real-space imaging:
1e8 electrons, 100% occup., 4e6 e-/cm2, “homogenous” on 25cm2  0.64 rad/shot
80kHz repetition rate  51 krad/s (on sensor)
Diffraction imaging:
1e6 electrons in 100(???) pixel, “in-homogenous”, 1 reflex in 4 pixel  1e4 e/1e-4 cm2
1e8 e-/cm2  16 rad/shot
1kHz repetition rate  16 krad/s (local)
TID: Oxide/interface damage  Vth -> more negative  need to compensate
(NIST)

## Slide 2: NIEL Damage
:- NIEL  leakage current increase
:- Normalize NIEL Damage to 1MeV Neutrons
:- Andreas Ritter:
Hardness factor for 10 MeV electrons ~1/100
:- ~100 keV even smaller, but non-zero
:- measure!!!

## Slide 3: Irradiation plan
:- irradiate with lowE electrons, few 100keV, as a function of fluence
:- first approach
:- MOS caps under bias
:- non-biased PiN diodes
:- 1cm² chips mounted on ceramic carriers
TID and NIEL Damage without uncertainty of conversion to rad and neq
High-temp annealing studies
:- a nice Master Thesis or so
:- details on irradiation facility at MPSD?
:- space??
:- how to bias?

## Slide 4: Applications (info from Sascha)
1000 Hz +/- full frame rate
10 % of the Pixels are >90 % filled
90 % of the Pixels are <10% filled
Primary electrons 60 -300 KeV and 1-5 MeV
1E5-1E8 electrons within < 1ps, (1000 Hz rep. Rate)
80 kHz +/- full frame rate
100 % of the Pixels are 50 % filled on avarage all values within the dynamic range exist. Normally distributed around 50% .
Primary electrons 100 -300 KeV
1E8 electrons within < 10ns, (80 kHz rep. Rate)
Diffraction imaging
Real-space imaging