## Slide 1: SVD Environmental Monitoring and VXD Radiation Monitoring
L.Lanceri & L.Vitale
INFN and Univ. Trieste

## Slide 2: Outline + news since last B2GM
Radiation monitoring:
  single crystal diamonds sensors
Temperature monitoring
  NTC sensors
  FOS Fibers
Plan for humidity
  Sniffing pipes plus chilled mirror hygrometer outside
  FOS Fibers
Total service space for cables

## Slide 3: Radiation Monitoring and Beam Abort
6 + 6 sensors (was 8+8)
on SVD support cone
(close to L3 rings)
4 + 4 sensors
PXD-beam pipe
Shielded
diamond
sensors
Voltage sources
(150÷500 V)
picoAmmeters
Sensors: scCVD, 4.5x4.5x0.5 mm3
Readout electronics and
Beam Abort Trigger:
In collaboration with
Elettra – Electronics Division

## Slide 4: Radiation Monitoring: Mechanics, cabling
Compact packages:
  1) 12 x 20 x 3.1 mm3
  multi-layer package, Rogers laminate ok for SVD (we already have 28 pc)
  2) 12 x 15 x 3.1 mm3
  Same material, with perpendicular mounting (for discussion, it can still be modified) we need input from simulation (M. Ritter and C. Marinas working on it).
Cabling
  3 m coaxial thin (HS SM47LSFH) from sensors to DOCKs
  + 15 m (or more) HS S_04162-B60, double shield

## Slide 5: Characterization of scCVD sensors
Single electrons, from Sr90 1-2 MeV (MIP): Landau peak vs HV
MPV vs HV
Current measurements studies with Sr90 point-like source, 3.2 MBq, at different distances, compared to FLUKA simulations, + long term studies for stability and reproducibility
d [mm]

## Slide 6: Radiation Monitoring Electronics
For each of the 4 input channels (diamond sensors)
  Individual HV supply
  Effective bandwidth: 100 kHz (matched to 1 revolution = 10 μs)
  Selectable current range: 0-50 μA or 0-2 mA
  16 (24?) - bit ADC; over-sampling possible with freq > 100 kHz
  4 circular data buffers, updated every 10 μs:
    “Raw data” and 3 levels of "sliding sums” over programmable numbers of cycles
    digital filtering levels and time responses, from "immediate" (10 us) to "very slow" (typically 1 s)
  4 levels of abort signals
    from the comparison of raw data and sliding sums with the programmable thresholds, selected according to a “SuperKEKB Status Register”
  Approach similar to FermiLab Beam Loss Monitor (BLM) and CERN LHC BLM systems
  Specifications discussed within Belle II and with SuperKEKB
  In collaboration with G.Cautero, D.Giuressi, and R.H.Menk from Elettra - Sincrotrone Trieste S.C.p.A.
First FPGA based evaluation board implementing the required features for the beam monitoring and abort now in preparation.

## Slide 7: Temperature 1: NTC Thermistors
System now foresees up to 96 NTC thermistors (Betatherm 100kΩ)
  24=12 pairs: 12 half-rings supporting the SVD ladders
  32=16 pairs: inlets and outlets of the CO2 cooling pipes
  6: near FOS fibers for cross-calibration
  34 still available
Readout based on ELMB (Embedded Local Monitor Board)
  1 power supply board, 3 motherboards with ELMB and CANbus adapter, 3 x 2 current source boards, 3 x 2 x 16-channel connectors

## Slide 8: NTC Interconnections
detector
docks
up to
6x16 NTC
sensors
counting room
PC
CANbus
ELMB
ELMB
ELMB
Power supply
≈ 3÷4 m
single
twisted
pairs
(no shield)
shielded
twisted
pairs
(shield
grounded
at docks)
current
sources

## Slide 9: Temperature 2 and Humidity 1 – FOS
FOS R&D completed by the IFIC group for PXD,
successfully tested at the DESY beam test Jan 2014
We adopt a similar approach for SVD:
one fiber per ladder, inserted in the Airex foam,
with several temperature sensing points per fiber
(one per DSSD in layers 4, 5, 6)
Total: 38 fibers and 120 temperature sensing points
Read-out of up to 40 fibers:
One rack-type sm225-800 interrogation unit (16 ch), 0.5Hz
10 (4 x 1) passive couplers.
=> Read-out available for 8-18 additional fibers (with humidity-sensitive coating?)
Moreover, humidity (to avoid condensation issues, from CO2 cooling at -20oC): interlock (Dew point < - 30 oC): sniffing pipes e Chilled Mirror Hygrometers
Model | description | cost | quantity | total
sm225-800 | FBG interrogator | 26,000€+VAT | 1 | 31,720€
CP-W-P-1X4-1550-250 | 1x4 passive coupler | 180/45€+VAT | 10 | ~800€

## Slide 10: FOS fibers
Layer 6: 16 ladders
16 fibers x 4 (+1) sensors
DOCKs
(4x1)couplers
…
…
Layer 5: 12 ladders
12 fibers x 3 (+1) sensors
…
…
Layer 4: 10 ladders
10 fibers x 2 (+1) sensors
…
…
Layer 6
4 couplers
Layer 5
3 couplers
Layer 4
3 couplers
Interrogator
(16 inputs)
…

## Slide 11: Humidity 2: CMS “sniffer” approach
Vaisala dew point sensors:
  Vaisala DMT242A for the [-80, +20] C dewpoint range
  Vaisala DMT242B for the [-60, +60] C dewpoint range
Chilled mirror:
  Edgetech Dewmaster Chilled Mirror Hygrometer

## Slide 12: Cabling space from DOCKs to E-hut
We will have to interconnect (distribution in DOCKs to be optimized!):
a) diamond sensors:
20 coaxial cables (FW) + 20 coaxial cables (BW)
b) NTC sensors:
minimum 4 (maximum 6) multi-conductor cables to individual twisted pairs
(symmetric FW-BW sharing?)
c) FOS fibers
38, all BW + 2? Humidity
Assuming pessimistically a pi/4 filling factor for packed cylindrical cables:
TOTAL (approximately equally shared FW/BW):
from a minimum 1734 mm^2 to a maximum of 1976 mm^2,
corresponding to less than half a 4000 mm^2 slot (one quarter FW, one quarter BW)
Sensors type | #Sensors | #cables | Cable ⌀ mm2 | FW/BW sharing | Total Section mm2
Diamond | 20 | 40 | 5.5 | = | 605+605
NTC | 64-96 | 4-6 | 11 | ~ | 482 to 726
FOS | 38+2(120) | 38+2 | All BW | All BW | 40
Total |  |  |  |  | 1734 to 1976

## Slide 13: Conclusions + news since last B2GM
Radiation monitoring:
  single crystal diamonds sensors
    number of sensors, package for PXD
    simulation, current measurements (in progress)
Temperature monitoring
  NTC sensors
    design of system for readout 96 NTC
    location and fixing (in progress)
  FOS Fibers
    fixing of the fibers
    location of the sensors (in progress)
Plan for humidity
  Sniffing pipes plus chilled mirror hygrometer outside
  FOS Fibers
Total service space for cables
+ Discussions in Slow Control meeting

## Slide 14: Back-up

## Slide 15: News, issues and details to be clarified
NTC sensors: total proposed number 24+32+6.
  we already purchased 100 (1000€) Betatherm (Radhard certified by CMS). Are these really too bulky? 2.4mm ⌀
  Final position and mounting on the 12 half-rings (24 sensors)
  Final position and mounting on inlets and outlets of the CO2 cooling pipes (32 sensors)
  Reference for FOS cross-calibration: we propose 2 sensors per Layer (6 sensors)
FOS: total proposed number, 38 fibers, 158 sensors:
  1 sensor per DSSD both for origami and BW DSSD (inside Airex channel), where exactly?
  1 sensor close to the clamp (outside Airex channel), precise distance?
  Note that test and calibration takes 1 day per 9 sensors in Santander!
  Note that procurements takes >~2 months
  + Humidity with different coating. 2 per layer (?) + 2 outer cylinder (?)

## Slide 16: Location of Temperature Sensors on the fibers
Sensor dimension 10mm
Coating: acrylate (almost insensitive to humidity)
Unbuffered (just 250 um ⌀) from clamp to all airex channel
Buffered (~900 um ⌀) from clamp to DOCKs with SC/PC connector?
Airex channel
500 um ⌀
Yellow: buffer tube
Orange: coating
Blue: core

## Slide 17: Humidity: CMS approach (reinforced after condensation problems)

## Slide 18: CMS approach (reinforced after condensation problems)

## Slide 19: CMS approach (reinforced after condensation problems)

## Slide 20: Sensor location test at Gemba
For SVD the package seems already ok (on support cones of L3).
Also first 3m of small (⌀1.6mm) coax cables to DOCKS ok.
Only issue is the path to HUT (under discussion) for standard coax.
For PXD more issues:
this package may be too long (needs to rework it or new one)
The first 3m of coax need grooves along the heavy metal

## Slide 21: First dosimetry tests with AH501 and 90Sr beta source
Point-like 90Sr beta source (~2MBq) on a movable stage in front of diamond sensor.
Full setup with AH501 and 3+15m.
Measured current from pA to nA.

## Slide 22: NTC temperature sensors
At least 28 x 2 = 56 NTC thermistors
  12 sensor pairs attached to the 12 half-rings supporting the SVD ladders
  16 sensor pairs on the inlets and outlets of the CO2 cooling pipes
  A few positioned near fibers for cross-calibration
We adopted rad-hard sensors and readout, largely used by LHC experiments
  One ELMB board + 2 Betatherm NTC thermistors: borrowed from CMS
  2 motherboards and 10 adapter mini-cards procured (public CERN design)
  Read-out via CAN bus interface, implemented
  Now purchasing 100 Betatherm thermistors

## Slide 23: Feasibility test in Vienna
Christian successfully made a mechanical test of this solution in April
a prototype “sandwich” consisting of an Airex sheet with an impressed groove (⌀ ~500µm) and an Origami CE flex;
a commercial optical fiber from which they removed the cover (coating). Section of uncovered fiber ~200µm
A groove impressed on all Airex sheets.
Now a functional test is also needed!
The plan: feed in the fibers after the ladder mount on the end rings.

## Slide 24: Cabling space from DOCKs to to E-hut
Numbers for calculatiion of required Cross Sections:
diamond sensors: initially based on (4+8)+(4+8) sensors in total, two coaxial cables per sensor, 24 coaxial cables (FW) + 24 coaxial cables (BW), 5.5 mm diameter each (June written request by Lorenzo)
reduced (after July 21st discussion) to (4+6)+(4+6) sensors:
20 coaxial cables (FW) + 20 coaxial cables (BW), 5.5 mm diameter each
b) NTC sensors: minimum request based on 64 NTC thermistors in total (*)
  (= 12x2 NTC on half rings + 16x2 NTC on CO2 inlets and outlets + 8 cross-reference on FOS fibers) from DOCK to E-hut: 4 = (2+2) (**) screened multi-conductor twisted pairs, 11 mm diameter each
  (*) The system with 96 channels allows for one full spare ELMB (32 channels) always available
or additional NTC sensors requests (thermal screen, beam pipe, ...) that however would imply to increase the number of cables from 4 to a maximum of 6 in total
(**) The exact location of sensors has to be decided,
as a consequence the FW-BW sharing may not be symmetric
c) FOS fibers
38 fibers (10(L4)+12(L5)+16(L6)), about 1mm diameter each, all BW; (bundled together?)

## Slide 25: Approximate schedule
Temperature & humidity | 2014 |  |  |  | 2015 |  |  |  | 2016 | 
What | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2
T&H Specifications, sign up |  |  |  |  |  |  |  |  |  | 
Fibers, mechanical layout |  |  |  |  |  |  |  |  |  | 
Fibers, assembly tests (SVD) |  |  |  |  |  |  |  |  |  | 
Fibers, multiplexing scheme |  |  |  |  |  |  |  |  |  | 
Fibers design sign up |  |  |  |  |  |  |  |  |  | 
Procurement, assembly |  |  |  |  |  |  |  |  |  | 
installation (PXD & SVD) |  |  |  |  |  |  |  |  |  | 
Thermistors, lab tests |  |  |  |  |  |  |  |  |  | 
Mechanics & cabling design |  |  |  |  |  |  |  |  |  | 
Procurement |  |  |  |  |  |  |  |  |  | 
assembly, installation |  |  |  |  |  |  |  |  |  | 
Radiation | 2014 |  |  |  | 2015 |  |  |  | 2016 | 
What | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2
Specifications, sign up |  |  |  |  |  |  |  |  |  | 
Simulations |  |  |  |  |  |  |  |  |  | 
Dosimetry, characterization |  |  |  |  |  |  |  |  |  | 
Diamond sensors choice |  |  |  |  |  |  |  |  |  | 
Mechanics & cabling design |  |  |  |  |  |  |  |  |  | 
Electronics specifications |  |  |  |  |  |  |  |  |  | 
Electronics design & proto. |  |  |  |  |  |  |  |  |  | 
Overall design, sign up |  |  |  |  |  |  |  |  |  | 
Components, procurement |  |  |  |  |  |  |  |  |  | 
"final" prototypes (4 ch.) |  |  |  |  |  |  |  |  |  | 
BEAST, 1 preliminary tests |  |  |  |  |  |  |  |  |  | 
BEAST, 2 complete test (4 ch) |  |  |  |  |  |  |  |  |  | 
electronics production & test |  |  |  |  |  |  |  |  |  | 
sensors installation & cabling |  |  |  |  |  |  |  |  |  | 
electronics installation |  |  |  |  |  |  |  |  |  |