## Slide 1: Online-Cluster-Analysis on FPGAs for recovery of slow pions
Steffen Bähr

## Slide 2: D* Decay in VXD
Particles with low impuls experience high stopping power
D* decays produce pions with low transversal momentum
  Below 60 MeV majority of the pions attributed to to this decay

## Slide 3: Momentum Distribution of Slow Pions
Pt < 60 MeV may already be insufficient to reach all SVD Layers
PXD Hits of slow pions will get lost since no RoI is built
Recovery mechanism necessary

## Slide 4: Charge of slow Pions with PXD
Use charge deposit in PXD for different momenta tracks to separate pi from mip
Charge deposit for different momentum

## Slide 5: Algorithm for Recovery of slow pions
Usage of the NeuroBayes Algorithm to predict Slow Pions by using cluster features
Training
  Usage of Simulated Clusters
  Conducted Offline
Prediction
  Usage of Detector Data

## Slide 6: Cluster Data used for Recovery
Charge deposition of Clusters can be supplemented by additional Information
  Additional information about the charge in a cluster
  Spreading of clusters in the PXD
  Features have different impacts on the result
Cluster Feature | Importance
Total Charge | 1st
Standard Deviation | 8th
Maximum Pixel Charge | 5th
Minimum Pixel Charge | 3rd
Length in Z | 4th
Length in Phi | 6th
Total Length | 2nd
Number of Pixels | 9th
PXD Layer | 7th

## Slide 7: Sample used for NeuroBayes Training
The Pion Sample covers the transversal impuls of pions not reaching the outer Layers
Background includes QED, Touschek and Coulomb

## Slide 8: NeuroBayes Performance
NeuroBayes achieves good Signal Efficiency and Background Rejection Ratios for pions with Pt < 65 MeV

## Slide 9: Using the NeuroBayes at the PXD
Algortihm needs to handle the data rates
  Usage of FPGAs with guaranteed Throughput
Needs to be placed close to the readout of PXD
  FPGAs of DHH has free resources

## Slide 10: Challenges for the Implementation on FPGA
Performance
  Interface is clocked with 200 MHz
  1 Cluster / Clock Cycle has to be able to be achieved
Resources
  30 % of the CLBs available
  50 % of the DSPs available
Quality
  Output of FPGA Implementation cannot differ to much from Software

## Slide 11: Cluster Processing Pipeline
Incoming Clusters are passing through a processing pipeline
  Protocol Handling for the Interface to the DHH‘s Clustering
  Computation of Cluster Features for the NeuroBayes
  NeuroBayes Expert makes the decision and passes it to the output interface

## Slide 12: Overview of NeuroBayes on FPGA
The NeuroBayes Expert consists of 4 major components
  Binning of the Cluster Features
  Preprocessing by using CDF
  Zero-Iteration done by vector multiplication
  Cut on the Ouput

## Slide 13: Conversion to Fixpoint
Original NeuroBayes Algorithm uses Floating Point
  Usage on FPGA requires more ressources and impacts latencies
  Transformation to fixpoint is more efficient, but impacts the quality
Quality of a Fixpoint implementation‘s Output depends on the used bitwidth
  Higher Bitwidth equals higher consumption of Ressources, while increasing Quality
  DSPs have 25*18 Bit Inputs

## Slide 14: Evaluation of Fixpoint Implementation
Usage of 25*25 Bitwidth results in no difference of output to floating point implemenation
Difference is small for 25*18
  Most resource efficient configuration for multiplication
  Difference is at 1.5 * 10^-5

## Slide 15: Evaluation of Performance
Computation of the Algorithm takes several clock cycles
  Performance requirements cannot be met
Usage of Pipelining throughout the implemenation
Fixpoint Vector Multiplication is the critical path
  High Frequency through usage of cascading DSPs
Component | Latency | Frequency
Cluster Feature | 1 cycle | 446 MHz
Preprocessing & Binning | 1 cycle | 446 MHz
Vector multiplication | 9 cycles | 350 MHz
Cut | 1 cycle | 446 MHz
Total | 12 cycles | 350 MHz

## Slide 16: Ressource Consumption
Critical Path for CLBs in the implemenation is the Binning and Preprocessing
  Mostly Usage of Look Up Tables
Usage of DSPs for vector multiplication makes life easier
  50 % of DSPs are still available
  Each multiplication needs one DSP
Ressource | Demand | Constraint
DSP | 3,125 % | < 50 %
CLB | ~ 2 % | < 30 %

## Slide 17: Simulation
Cluster Feature | Value
Total Charge | 425
Standard Deviation | 49
Maximum Pixel Charge | 135
Minimum Pixel Charge | 23
Length in Z | 2
Length in Phi | 2
Total Length | 1
Number of Pixels | 4
PXD Layer | 2
Result of Software is:
0000001110100011110010001 -> slow Pion Cluster
(S)DDD,DDDDDDDDDDDDDD

## Slide 18: Summary
Recover slow Pions using FPGAs near PXD
FPGA-Implementation is sufficient
  Quality : Difference < 1.5 * 10 ^ -5
  Throughput : 350 Mio Cluster per secons
  Resources : ~ 2 % CLBs , ~3 % DSPs
Integration into DHH

## Slide 19
Demo