## Slide 1: ASIC Discussion
H-.G. Moser, 18th B2GM, June 2014
DCD status and plans (information from Ivan)
DCD summary
Switcher status and plans
Schedule
ASIC review

## Slide 2: DCD status (measurements by Edi Prinker)
D ~ 50 ADU
Actually quite ok, s ~ 0.6 ADU
Few with noise > 2 s
O(10%) channels with large non-linearity due to missing codes
Not bad, spread could be smaller
Ivan: understood, due to transistor mismatch, can be fixed

## Slide 3: Chip #1 Test all ADCs (measurements by Ivan Peric)
ADC characteristics
Gain (nA/LSB)
Average noise
INL
DNL

## Slide 4: Chip #1 Test all ADCs
…
ADC gain 73nA/LSB (~112e @ gq 650pA/e)
Noise floor: ~0.58LSB (64e @ gq 650pA/e)
336e
3LSBs
Noise of a bad ADC: ~1.3LSB (145e @ gq 650pA/e)
INL of a bad ADC: ~5.3LSB

## Slide 5: DCD Status & Plans (Ivan Peric)
Status
DCDBv4 pipeline and standard versions submitted in 2013
Single chip and the tests on EMCM are ongoing (see talk E. Prinker)
The first results are good – all circuits tested and work
Similarly as in previous chips, we have several sensitive ADCs pro chip which are distinguished by small missing code regions and higher noise
The problem can be related to transistor mismatch and a poor ROUT of current sources – can be fixed on the next chip
Irradiation of DCDBv4 (pipeline) is planned at KIT-Karlsruhe
Plans
A few things in DCD can be improved – we are planning a new DCD submission for November 2014 or February 2015
Improvements:
Fix JTAG DIN sampling moment to rising CLK edge (to be conform with the standard)
Enlarge several transistors in ADC (comparator) for better matching, improve the ROUT of the current sources
Further changes will be determined from measurement results

## Slide 6: DCD Summary
Documentation: Description of new registers
Schematics (updated of DCD manual)
List of known good settings
BSDL file for boundary scan test
Description of digital test pattern
Proposed Tests:
Digital test: write in all registers and read back
Power test: all currents as expected (@ 305 MHz)
JTAG boundary scan ok?
Pedestal control (VNSubIn, VNSubOut,)
Functionality of calibration circuit (internal & external)
  Tuning of optimal settings……
Pedestal spread (rms, peak-to-peak), without sensor
Gain and linearity (with internal or external current source?)
Dynamic range
RMS noise without sensor: @ 305 MHz dependence on
Number of defect channels:
    Large pedestal offset (criteria)
    ( ) Excessive noise (> 2 x rms?)
    Missing codes / excessive non-linearities
Link DCD-DHP: stability @ 305 MHz
Analogue common mode subtraction (with internal current source)
DACs for pedestal correction
Tests should be performed on hybrid 4/5 and on EMCM.
Test with matrix: average noise (increase with respect to measurements without matrix).
LOW STATISTICS!

## Slide 7: SWITCHER Status & Plans (Ivan Peric)
Irradiation of latest SWITCHER has been done at KIT (dose 30 MRad)
The chip works after the irradiation
Bumping issue: bumping so far done in HD-lab, this works well for prototyping but is slow for production
Bumping with the required pitch (150 μm) is not offered by the vendor (AMS/IBM)
Solution: Company Pactec can place underbump metallization (ENIG) and solder bumps on single dies (price < 66 Eur/chip + 7.3 kEUR ~ 16k EUR)
=> see Laci’s talk
Backup solution: ordering of wafers from AMS MPW runs and bumping at IZM (probably possible in 2015 – still to be confirmed)
SWITCHER submission planned in 2015
Improvements: faster clear driver
Separated control of the termination resistance for serial input (should be always on) and for the other fast inputs

## Slide 8: Schedule
DHPT roadmap by Leo
New DHPTs available end of April 2015
Test modules from pilot run ready end of March 2015
More or less in time
What about DCD and switcher (with bumping)?
need them at the same time
=> Submission as early as possible !

## Slide 9: ASIC Review
Design Review of all ASICs to give green light for next iteration
Results of the EMCN tests need to be evaluated as well
Scheduled: October 27/28 at MPP
External reviewer: Gary Warner
It might well be the case that the information we have till then is incomplete and we decide that more tests are needed.
Then the review should result in
  a list of missing measurements
  a plan of actions (milestones)
  criteria for acceptance
  an evaluation of the impact on the schedule