## Slide 1: Project Meeting at MPI/HLL
Status of the Readout ASIC
Timing Test Concept
Test Set-up
Next Steps

## Slide 2: Status Readout ASIC
Submission Date: 19. May 2014 at MOSIS
Preliminary delivery Date: 18. July 2014 at CERN
Components
  16-by-16 Matrix of Pixel Readout Electronics
    Active Quenching and Recharging Circuit
    Hit-Counting and -Serializing
  Fast Trigger with Wired-OR Configuration of every row and subsequent of every column
  Slow Trigger for Validation
    Only for 1 row (until now)
    4 adjustable Reference Voltages as Threshold Condition
  Control Register for Static Signals
    Pixel Masking
    Counting Depth (1 or 2 Bit)
    Reference Voltage for Slow Trigger
    Switches of 2 Pixels to extra Test Pad
  Pad Ring

## Slide 3: Layout Readout ASIC
16x16 Pixel Matrix
Bump-Pads to Sensor
Control Register
for static Signals
Wire-Bond
Pads
Wire-Bond Pads for Testing
Slow Trigger
Fast Trigger

## Slide 4: Pixel Electronics
SiMPI-Modell (simplified)
Cg=65f
Cq=10f
Rq=1.2k
Vbias=VBD+VOV=36V+3.3V
Anode
Anode
Out
Out
Recharge
Recharge

## Slide 5: Pixel Electronics
SiMPI-Modell (simplified)
Cg=65f
Cq=10f
Rq=1.2k
Vbias=VBD+VOV=36V+3.3V
Anode
Out
Recharge

## Slide 6: Fast Trigger Concept
Wired-OR Connection:
Step: of every Row
Step: of every row-wise Wired-OR Connection (final)
Trigger
1.
2.

## Slide 7: Delay Times – Fast Trigger
Chart: Number of Pixels active inside 16x16 Matrix
| 1 | 2 | 4 | 8 | 16
td_Rows | 1.4696 | 1.4708 | 1.4553 | 1.4473 | 1.4597
td_final | 1.5419 | 1.5209 | 1.494 | 1.4738 | 1.4673
Time Delay from Event
until Output triggers
Decision: 1 TDC for Matrix or for every Row

## Slide 8: Slow Trigger Concept
Realization for 1st Row in Matrix
Adjustable Threshold for Trigger Condition (1-4 Pixel)
Comp_In
Comp_Out
Ref: 1 Pixel
Ref: 2 Pixel
Ref: 3 Pixel
Ref: 4 Pixel

## Slide 9: Timing Test Concept

## Slide 10: Pixel Electronics – with Test Input
Timing Test of every Pixel possible due to Masking

## Slide 11: Timing Test
Trigger
Latch
Reset
FF Out
FF Out Dummy
TestIn
FF
FF-
Dummy
DUT
TestIn
Latch
Trigger
Latch
n∙∆t
td
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
 | 0.00023263 | 0.0013499 | 0.0062097 | 0.02275 | 0.066807 | 0.15866 | 0.30854 | 0.5 | 0.69146 | 0.84134 | 0.93319 | 0.97725 | 0.99379 | 0.99865 | 0.99977 | 0.99997 | 1 | 1 | 1 | 1 | 1
 | 9.8659e-10 | 1.899e-08 | 2.8665e-07 | 3.3977e-06 | 3.1671e-05 | 0.00023263 | 0.0013499 | 0.0062097 | 0.02275 | 0.066807 | 0.15866 | 0.30854 | 0.5 | 0.69146 | 0.84134 | 0.93319 | 0.97725 | 0.99379 | 0.99865 | 0.99977 | 0.99997
td
∆t
N∙∆t
0.5
1
0
Frequency distribution of FF Out and FF Out Dummy

## Slide 12: Test Set-up
Usage of an existing Testboard
Hybrid removable
1. Hybrid-Version only with Test ASIC
2. Hybrid-Version with Sensor and ASIC
Installation of Test Set-up will be done by the summer student Alessio Borgheresi (22.07.-11.09.)
Oscilloscope is ordered
DTG and Logic Analyzer exist

## Slide 13: 1. Hybrid-Version
PCB Layout designed
  Costs: ≈800 €
  Delivery Date: End of July
  4-Layer Design

## Slide 14: Interconnection with Sensor
20 ASICs will be send to PacTech
  For UBM and solder balling of 30-µm balls
  PacTech needs at least 10 setup chips
  Costs: ≈10k €
    ≈5300 € for electroless Ni/Pd/Au under bump metallization
    ≈4500 € for single chip solder balling SB2 on Ni/Pd/Au UBM
  For connecting with an Interposer or Sensor
max. 10 ASICs with solder balls would be available for Flip-Chip Bonding with Sensor chips at HLL

## Slide 15: 2. Hybrid-Version
Layout Design can start when we have detailed Sensor Information

## Slide 16: Questions
Sensor Schedule
Detailed mechanical Structure of the Sensor
Sensor Connnection
Sensor Tests
Status: Design of Teststructures (Dummies with Daisy-chain structure) for Pac Tech and Flip-Chip-Bonding (Assembly at HLL)
Future Plans for analog and digital SiMPIs

## Slide 17: Next Steps
ASIC Test
Design of 2. Hybrid
ASIC + Sensor Test
Hiring of PostDoc
Further Design Activities
  TDC
  Validation Logic for total Matrix
  Multiplexing of Hit Matrix
  Sequencer
2nd ASIC Submission in May 2015

## Slide 18: End
Thank you!
Project Wiki-Page: fec-sipm.desy.de