## Slide 1: DHPT Architecture & Implementation
Tomasz Hemperek

## Slide 2: Outline
Overview of DHP chip iterations
DHP overview
DHPT Overview
SEU tests
Slow control/synchronization/reset
Data processing
Sequencer
Offset correction
RTL & verification
Implementation

## Slide 3: Data Handling Processor – Design History
Started with IBM 90nm technology in 2010
DHP 0.1
  Half size prototype, 2 x 4 mm2, C4 bumps
  Basic digital data processing
  PLL (1.6 GHz) + High speed serial link
   Successful verification
DHP 0.2 (sub. mid of 2011)
  Full size chip, 3.2 x 4.3 mm2
  Full data processing, added switcher sequencer and bias generators
  Improvements in link performance (pre-emphasis), buffer size, and data format
  Successful tests & system operation (some issues with max. speed of CMOS clock output)

## Slide 4: Data Handling Processor – Design History
Forced to abandon 90nm IBM process  chosen 65nm TSMC, started with small prototype chips to verify full custom blocks and rad. hardness performance
DHPT 0.1 (Oct. 2011)
  PLL (1.6 GHz)
  High speed TX (CML driver)
  Bias generators (U Barcelona)
  Memory SEU test structures
DHPT 0.2 (June 2012)
  LVDS RX & TX
  Temperature sensor (U Barcelona)

## Slide 5: DHPT 0.1 - SEU Test
Memory blocks
  compiled TS1N65 low power, 1024x72bits
  compiled TS1N65 low power, low leakage, 1072x72bits
  full custom register file, 64x72bits
JTAG interface
TCK
TMC
TRST
TDI
TDO
JTAG tap
JTAG memory configure
Data in
Data out
Data enable
Add enable
Data [71:0]
En
A
D
En
A
D
En
A
D
Add [11:10]
Select
Add [9:0]
Mem1
Mem2
Mem3
Add [11:0]
M. Lemarenko, T. Hemperek

## Slide 6: SEU Tolerance
Cross section measured at 24 GeV pion beam line
Results agrees with other data published for 65nm memory cells
SUE rate extrapolated by assuming 104 neutrons s-1 cm-2

## Slide 7: Data Handling Processor – Design History
First full size 65nm chip submission (DHPT 1.0) after internal design review
DHPT 1.0 (Aug. 2013)
  Full size chip
  Includes all pre-verified full custom blocks
  Footprint & electrical compatible to DHP 0.2
  Improved memory & processing resources wrt. DHP 0.2
  12 mm2 area, C4 bumps, 200µm pitch
  >300k Gates, >3MB SRAM
  PLL, 1.6Gb/s serial link, CML preamhasis
  >100 LVDS and HSTL IO
  DACs, ADC
  core voltage 1.2, i/o voltage 1.8

## Slide 8: DHP
One 1.6GB output link per chip
81.29Gbps
(320Mbps output data x 256 lines)
10MHz read-out frequency
Per DHP chip:
8x8 bit wide data inputs
8x2 bit wide offset correction outputs
To SWITCHERS

## Slide 9: General Overview

## Slide 10: Hard Macros
PLL/SER/CML Driver
LVDS RX
LVDS TX
HSTL RX
SRAM MEMORY (3 types)
IREF
DACS
ADC
PROGRAMABLE DELAY (on all inputs/outputs to and from DCD and switcher)
Will be covered in next talks

## Slide 11: Block Diagram
CORE
JTAG
AURORA FRAMER
PLL/SER/CML
IREF/DACs/ADC
CMD DECODER
OFFSET CORRECTION
DATA BUFFERING
ZERO SUPPRESION
COMMON MODE CORRECTION
SORTING
FRAMING
SEQUENCER
LVDS I/O
HSTL I/O
CMOS I/O
SYNC

## Slide 12: Clocking
DIGITAL CORE runs mostly on 80MHz
One full DEPFET row takes 10MHz (8 clock cycles)
DIGITAL CORE
AURORA FRAMER
SRIALIZER
20 to 1
CML
DRIVER
PLL
320M
80M
1.6G
80M
1.6Gbit/s
32bit frame based interface (clock-domain-crossing)
20bit@80M
DESERIALIZERS
:4

## Slide 13: Command decoder
One control word per row period is send synchronized to the DHP clock GCK (76.35 MHz)
The control word (8 bits) transmits four independent commands: <RST|VTO|TRG|FSYNC>
  RST: Reset, level sensitive, pulse width selects different reset modes
  TRG: Physics trigger, level sensitive, pulse width selects raw data frame size
  VTO: Veto (gated mode), level sensitive, selects veto sequence while on
  FSYNC: Frame sync, edge sensitive
The state of every command is encoded in two bits (Manchester code)
  <10> = on
  <01> = off
Two additional control words are accepted (broken Manchester code)
  <00 01 11 01> synchronization sequence, should be used as IDLE
  <11 10 00 FSYNC> CALTRG (mem_dump): calibration data trigger, edge sensitive, allows simultaneous FSYNC command transmission
The command latency in the DHP core is in the order of a few GCK cycles

## Slide 14: Reset
Power on Reset (CRESET)
  Reset configuration ONLY (JTAG REGISTERS)
    mainly used to set default values for DACs to bias LVDS RX
    asynchronous
Reset command/signal is level sensitive
  Short reset -> resynchronize output link
  Long reset -> reset all state machines
  Synchronous
  Recommended reset when possible
FRAME SYNC (FS)
  Every 20us resets almost all state machines and pointers

## Slide 15: Synchronization
All signal synchronized to external frame sync
Send on trigger line

## Slide 16: Slow Control / Configuration
User Registers:
Memory access (self incrementing address pointer):
TAP Controller:
Synopsys BSD Compiler
jtag_conf_reg
reset_n, clk_conf, enable,
capture, shift, update, si
so
[SIZE-1:0] out
[SIZE-1:0] in
read, write
data_reg
reset_n, clk_conf,
capture, shift, update, si
so
[SIZE-1:0] data_out
write_data
addr_reg
en_addr
en_data
[15:0] addr
write_addr
[SIZE-1:0] data_in

## Slide 17: Data taking
Data taking with zero suppression
  Data are buffered (programmable size of matrix)
  Triggering after latency (programmable)
  Pedestal subtraction on/off (+ offset)
  Common mode correction on/off
  Hits recognition
  Formatting
  Sending out
Memory dump
  Activate by fast command
  Dump raw data from beginning of memory (programmable amount)
  Trigger need to be disabled before

## Slide 18: Data Buffering
desterilizing and sorting (x32@320MHz)
DCD data 8x8bit
256x8bit
16x128bit
memory
1024x(128+16 parity)
X16
256x8bit data
256x8bit pedestal
pedestal correction
256x8bit data
0-255: (data)
256-511: (data*)
512-767: pedestal A
768-1023: pedestal B
1024 rows
8 clock cycles for 1 row processing (256x8 bit)
  MEM_CONF_RD
  MEM_CONF_WR
  MEM_DATA_WR
  MEM_DATA_RD
  MEM_PED_ACTIVE_RD
  MEM_PED_ACTIVE_WR
  MEM_PED_NACTIVE_RD
  MEM_PED_NACTIVE_WR
pixel masking when pedestal = 255
concurrent JTAG access
Overall memory size: 4 full (1024 rows) frames (1x data + 2x pedestal)
Double buffer for pedestals:
Memory protected by Hamming code
Can be entirely used for raw data taking
memory physical organization
1024x128+parity

## Slide 19: Common mode correction
256x8bit data
256x8bit data
average
apply threshold
input – average > threshold ? input : common mode
average
apply threshold
input – average > threshold ? input : 0
There is probably something wrong with masking!
256bit mask

## Slide 20: Hit finder
256x8bit data
memory 256x20
frame_id[2],row_id[10],data_in[8]
X64
64x8bit data (x4 in time)
memory 512x16
cm, frame_id[2], row_id[8]
6bit common mode
8x8x20bit
sort fifo
X8
sort fifo
8x(20+3 column) bit
(20+6 column) bit
sort/hit find
hit data

## Slide 21: Output data buffering
hit data
mux
active memory dump
/ calibration data
cdc_fifo
memory 4096x(32+2)+ parity
data[32], sof, eof, 2/4byte
aurora framing
raw data
20bit
to serializer

## Slide 22
If CM = 63 – there was some loss in this row
CM = 62 – common mode overflow
TYPE (3)
FLAGS (13)
FFRAMEID (16)
TYPE (1)
ROW (9)
CM(6)
COLUMN (7)
VALUE(8)
VALUE(8)
VALUE(8)
FRAME HEADER
ZERO SUPPRESED DATA
RAW DATA
flags: overflow ,offset_mem_active, active_ped_mem

## Slide 23: Expected DHPT 1.0 Data Losses
FIFO 1: 64 FIFOs in front of the hit finder  256 words deep (DHP 0.2  16)
FIFO 2: between hit finder and serializer  4096 word deep (DHP 0.2  512)
Chart: 
| 0.49727700000000002 | 0.58678900000000001 | 0.68934499999999999 | 0.78525699999999998 | 0.87515500000000002 | 0.97245400000000004 | 1.0670999999999999 | 1.1625700000000001 | 1.2559499999999999 | 1.3494699999999999 | 1.4499500000000001 | 1.54758 | 1.63208 | 1.7336499999999999 | 1.8317600000000001 | 1.9309700000000001 | 2.0133100000000002 | 2.1198600000000001 | 2.2167300000000001 | 2.3194499999999998 | 2.4071199999999999 | 2.4971800000000002 | 2.5967199999999999 | 2.7018 | 2.7925399999999998 | 2.88273 | 2.9926699999999999 | 3.08168 | 3.1778599999999999 | 3.2673399999999999 | 3.3741099999999999 | 3.4644200000000001 | 3.5444399999999998 | 3.6415899999999999 | 3.7469199999999998 | 3.8442500000000002 | 3.9341499999999998 | 4.0379300000000002 | 4.1361499999999998 | 4.2432299999999996 | 4.3116700000000003 | 4.4145000000000003 | 4.5297799999999997 | 4.6053600000000001
HF=16, OUT=4096 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0014199 | 0.01143 | 0.029468 | 0.071281 | 0.16131 | 0.36393 | 0.57818 | 0.8993 | 1.4455 | 1.9449 | 2.6628 | 3.5652 | 4.5706 | 5.6002 | 6.5102 | 7.659 | 9.1526
Chart: 
| 1.9660899999999999 | 2.1032700000000002 | 2.2417899999999999 | 2.3746900000000002 | 2.512 | 2.6485500000000002 | 2.7842099999999999
Bandwidth limit untriggered | 0 | 0 | 0 | 0 | 0.47771 | 5.6087 | 10.2079
DHPT1.0 triggered @ 30kHz | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00049604 | 0.0021601 | 0.020184 | 0.021973 | 0.037737 | 0.077311 | 0.14387 | 0.24047 | 0.4296 | 0.59373 | 0.93167 | 1.273 | 1.4626 | 1.8146 | 2.1756 | 2.3894 | 2.9788 | 3.7645 | 4.628 | 5.2811 | 6.1448 | 7.2495 | 8.2084 | 9.3882
Bandwidth Limit triggered @ 30kHz | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.28206 | 2.3678 | 4.4563 | 6.3059 | 8.1433
Data loss [%]
Occupancy [%]

## Slide 24: Sequencer
0-255: switcher seq.
256-511: unused
512-767: gated mod seq.
768-1023: unused
8 clock cycles for 1 row processing
SW_MEM_RD
SW_MEM_WR
SW_MEM_GATE_UP_RD
SW_MEM_GATE_UP_WR
SW_MEM_GATE_RD
SW_MEM_GATE_WR
SW_MEM_CONF_RD
SW_MEM_CONF_WR
read sequence memory
256 rows
clock
data/new frame
clear
gate
concurrent JTAG access
gated mode sequence memory
clock
clear
gate
mux
serializer
(x32@320MHz)
3x32 bit
3x32 bit
32 bit
memory physical organization
1024x128+parity
veto
run
Fully programmable sequencer (length and bits)
Gated mode started by veto command (at given row) stopped after programmable time

## Slide 25: Offset correction
memory
1024x(128+16 parity)
2x128 bit
memory
1024x(128+16 parity)
serialization (x16@320MHz)
8x2bit DCD offset data
4 clock cycles -> 4 states
  OFFSET_MEM_CONF_RD
  OFFSET_MEM_CONF_WR
  OFFSET_MEM_DATA_WR
  OFFSET_MEM_DATA_RD
0-511: offset A
512-1023: offset B
1024 word/2x256 rows
2 bits per pixel
concurrent JTAG access
concurrent JTAG access
memory physical organization
1024x128+parity

## Slide 26: Explanation of the Timing Diagrams
Raw data frame
Physics trigger on
Raw data frame
Rolling shutter cycle
Event data frame
20µs
latency
Calibration trigger
Calibration data frame
~400µs
Data buffer write inhibit
20µs – latency
40µs - latency
Injection
Inhibit physics trigger
Physics trigger off
DHP Internal Data Processing
DHP Data Transmission
DHHDHP Commands
External Events
Physics event

## Slide 27: DHP timing for triggered data taking
Raw data frame (n)
Physics trigger on
Raw data frame (n+1)
Raw data frame (n+2)
Event data frame
Latency
The transmitted Event data frame starts with hits from [rowm, raw data framen] and ends with [rowm-1, raw data framen+1]
The row index m is a function of the phase between trigger and frame sync
The trigger command is level sensitive and its width selects the size of the raw data frame to be processed
The default width is 1536 GCK cycles (8 GCK cycles/row · 192 rows/frame)
Frame sync
Physics trigger off
Frame sync
Frame sync
Frame sync
Physics event
Depending on FIFO fill level data transmission can extend the trigger width
20µs
20µs

## Slide 28: DHP timing for calibration data taking
Raw data frame (n)
Calibration data and event data frames may overlap
Raw data frame (n+1)
Raw data frame (n+2)
Calibration trigger
Calibration data frame
The calibration trigger can be send any time within a frame period
If the previous event data transmission is not yet finished (case B), the calibration data transmission will be put on hold until the FIFOs are flushed. In some cases remaining event data still might be send after the calibration data frame (not recommended).
The transmitted Calibration Data Frame is re-sorted and always starts with [row0, raw data framen+1] and ends with [rowmax, raw data framen]
Programmable rowmax and defines the raw data buffer size to transmit (default m=255)
Data buffer write inhibit
Event data frame
Physics trigger off
Calibration data frame
Event data frame
B) Transfer overlaps cal. trigger
A) Transfer finishes before cal. trigger
~400µs
For better readability periodic frame sync commands are omitted in this and the following drawing s

## Slide 29: DHP timing for injection sequence w/o calibration data taking
Raw data frame (n)
Raw data frame (n+1)
Raw data frame (n+2)
Event data frame
Latency
Injection
Inhibit physics trigger
Physics trigger on
Physics trigger off
Physics event
The suppression of physics triggers should start 20µs – latency before the injection starts.
20µs – latency

## Slide 30: DHP timing for injection sequence with calibration data taking
Raw data frame (n)
Physics trigger on
Raw data frame (n+1)
Rolling shutter cycle (n+2)
Event data frame
latency
Calibration trigger
Calibration data frame
Data buffer write inhibit
40µs - latency
Injection
Inhibit physics trigger
Allow a few row clock periods (~0.5µs) delay between calibration trigger and injection to allow for command processing latency compensation
Physics trigger off
Physics event
The suppression of physics triggers should start 40µs – latency before the injection starts.
Calibration trigger should only be send if the previous event data transmission has finished
20µs
~400µs
20µs – latency

## Slide 31: DHP timing for injection sequence with calibration data taking
Raw data frame (n)
Physics trigger on
Raw data frame (n+1)
Rolling shutter cycle (n+2)
Event data frame
latency
Physics trigger off
Calibration data frame
Data buffer write inhibit
Injection
Inhibit physics trigger
Allow a few row clock periods (~0.5µs) delay between calibration trigger and injection to allow for command processing latency compensation
Minimum timing requirements for sequence of Physics trigger – Calibration trigger – Injection
Physics event
Calibration data and event data frames overlap
Calibration trigger
&
The suppression of physics triggers should start 20µs before the injection starts.
20µs
~400µs

## Slide 32: Verification Plan
You should be able to use this for chip testing too

## Slide 33: RTL & Verification
RTL and verification based on SystemVerilog (DVT & Eclipse)
UVM for verification
Use linting and simulation (Questa)
Clock Domain Crossing formal analysis (Questa)
RTL code statistics:
  Chip code lines : ~6000
  UVM code lines: ~7000

## Slide 34: Testbech organization
Original DCD HDL code is used for DCD
Original Xilinx Aurora core receiver used for receiver
OVC Components:
  Command/Sync
  JTAG
  DCD/Switcher
  Aurora RX
DHP
DCD
Aurora RX
JTAG
CMD

## Slide 35: PDK Preparation
Based on default 65nm OA version
Marge technology files (LEF and tf) to achieve full integration on between tools on single oa database
Standard ARM cells/io/memory
Migrate all libraries to OA to be able to automate from virtuoso and encounter same time
  Layout (from gds)
  Abstract (from lef)
  Schematics (form netlist)
Netlist for LVS is generated from Verilog netlist (need lot of magic here so that this work)

## Slide 36: IP Design and Modeling
For all custom IP needed to generate
  Abstract
  Verilog model
  Liberty file
  Proper netlist for LVS

## Slide 37: Flow (Digital on Top)
One full cycle ~20h

## Slide 38: Timing Corners
 | ff | ss | tt | ff_max | ss_min
corner | ff | ss | tt | ff | ss
Voltage [V] | 1.32 | 1.08 | 1.2 | 1.32 | 1.08
Temperature [C] | -40 | 125 | 25 | -40 | 125
rc | best | worst | typical | worst | best
derate early | 1.0 | 0.9 | 0.9 | 1.0 | 0.9
derate late | 1.15 | 1.0 | 1.1 | 1.15 | 1
clock uncertainty: 0.1ns
this is quite pessimistic -> radiation

## Slide 39: Florplan
vertical M6 and M8
horizontal M7 (and M1)

## Slide 40: Place & Route

## Slide 41: Timing Report
also with PrimeTimeSI

## Slide 42: Mixed signal verification
Simulation on spice level critical blocs together with digital
Gate level
Digital (verilog)
PLL/SER
(spice)

## Slide 43: LVS & DRC
Bumps and RDL added on top
Deep n-well added
No Layout view for all SRAMs
Manage to get Assura DRC “clean”
Small metal fixes

## Slide 44
Thank you