## Slide 1
APVDAQ Status
Markus Friedl
22 January 2015

## Slide 2
Introduction
What APVDAQ Can Do
What APVDAQ Cannot Yet Do
What APVDAQ Cannot Do
Summary

## Slide 3
Introduction
What APVDAQ Can Do
What APVDAQ Cannot Yet Do
What APVDAQ Cannot Do
Summary

## Slide 4: Introduction
APVDAQ is a modular readout system for the APV25
Predecessor of the Belle II SVD readout system (“FADC”)
6U VME module
Repeater board
APV25 hybrid
30m
2m

## Slide 5: Electrical QA During Ladder Assembly
Identical setups built for all ladder assembly sites
  To obtain comparable results
  Results are stored in the database
Measurements:
  Bare hybrids or Origamis
  Ladders during construction
  Final ladders (source/laser scan)
  Only one sensor (2 hybrids/ Origamis) at a time can be measured
Melbourne
IPMU
Pisa
Vienna
About one year ago before shipping; KEK already had an APVDAQ system

## Slide 6
Introduction
What APVDAQ Can Do
What APVDAQ Cannot Yet Do
What APVDAQ Cannot Do
Summary

## Slide 7: What APVDAQ Can Do
Different run types (tests):
  Pedestal/Noise (software run)
  Internal Calibration Scan
  IntCal vs. Vsep Scan
  Source/Laser (hardware run)
Run-dependent
  Online analysis
  Export to CSV file for database
Bare hybrid,
Origami
With sensor during production
Final module/ ladder

## Slide 8: Recently Added Features (1/3)
DAC add-on board
  Allows to apply separation voltage in the range -5…+5V between bias and APV ground
  Supported on p-side from software version 0.96
  Hardware is being distributed
  Installation instructions available in Twiki:
    https://belle2.cc.kek.jp/~twiki/bin/ view/Detector/SVD/ApvDaqPage

## Slide 9: Recently Added Features (2/3)
Typical IntCal vs. Vsep plots for APV with pinholes
SFW993 p-side, APV#1, channel 30
Distinct Vsep dependence of pinhole channels for both polarities
Mean
RMS

## Slide 10: Recently Added Features (3/3)
Correlation scatter plots and coefficients between neighbors
SFW993 p-side, APV#0, pulled channels (61,73,74) are obvious
  High anti-correlation to neighbors
Raw data
CMC data

## Slide 11
Introduction
What APVDAQ Can Do
What APVDAQ Cannot Yet Do
What APVDAQ Cannot Do
Summary

## Slide 12: What APVDAQ Cannot Yet Do
Additional features for next software release:
  DAC support also for n-side
  Correlation coefficient shown for scatter plot on display
What else?
  Maybe more sophisticated analysis/export for source/laser run?
  Please let me know any requests

## Slide 13
Introduction
What APVDAQ Can Do
What APVDAQ Cannot Yet Do
What APVDAQ Cannot Do
Summary

## Slide 14: What APVDAQ Cannot Do
Software does not
  Interpret/judge measurement results
  Grade the device under test
Human intelligence is required for those tasks
  It’s not very complicated  student’s job
  Instructions: https://belle2.cc.kek.jp/~twiki/bin/view/Detector/SVD/ModuleElectricalTest

## Slide 15
Introduction
What APVDAQ Can Do
What APVDAQ Cannot Yet Do
What APVDAQ Cannot Do
Summary

## Slide 16: Summary
APVDAQ is a powerful tool for electrical tests
  Before (hybrids, Origamis)
  During
  After (full ladder test)
Ladder assembly
System well matured
  Few more features to be added in software

## Slide 17
Backup Slides

## Slide 18: APVDAQ in Vienna, Pisa, IPMU, Melbourne
Systems installed at all assembly sites (plus KEK)
Vienna
IPMU

## Slide 19: Measurements are Stored in the Database
APVDAQ software
Construction database

## Slide 20: HEPHY Clean Room Installation
Linear LV power supplies
VME Crate
2 x Keithley 2410
HV power supplies
(software controlled)
PC
Metal box with repeater boards
Device under test
(here: SFW993 wrapped in cloth)
Barcode scanner

## Slide 21: Closeup
DAC board

## Slide 22: Power Supplies etc.
HV: 2 x Keithley 2410 SMU
  Operated by a dedicated software
LV: 2 x GW Instek GPS-3303 (linear, 3 channels each)
  Works well also with bias (floating LV)
  (Had noise troubles before with switching LV PS under bias)
Barcode Scanner: 2D Imager KD-1000-OP
  Reads 1D and 2D codes
Label Printer: Brother QL-720NW
  Produces rad-hard, self-adhesive labels

## Slide 23: APVDAQ Stability
Data of >640 APV25 chips tested on hybrid level
Example plots shown here:
  Noise
  IntCal Peak
More plots:
  http://www.hephy.at/project/belle/belle2svd/apvdaq/pa_dh.pdf