## Slide 1: Power supplies
Twiki page available:
  https://belle2.cc.kek.jp/~twiki/bin/edit/Detector/SVD/PowerSupplies
  Including technical specifications
Tender process started in August 2014, concluded in December.
  Several companies invited:
    CAEN
    WIENER
    ISEG
    TDK-LAMBDA
    TEXIO
    MATSUSADA
  CAEN and WIENER/ISEG (combined) responded
  CAEN was awarded the contract
Expected delivery:
  Second half of 2015

## Slide 2: Power Supplies Overall schematics
It turns out that maybe separation voltage is useful also on N-side ! Require some extra boards

## Slide 3: Numers
Required numbers of channels
Purchased products:
Layer | Num Ladders | FW Hybrid/ ladder | BW Hybrid/ ladder | N FW groups | N BW groups | TOTAL
3 | 7 | 2 | 2 | 2 | 2 | 
4 | 10 | 2 | 4 | 4 | 6 | 
5 | 12 | 2 | 6 | 4 | 10 | 
6 | 16 | 4 | 6 | 8 | 12 | 
 |  |  | Total groups | 18 | 30 | 48
 |  |  | LV channels | 36 | 60 | 96
 |  |  | SEP channels | 18 | 30 | 48
 |  |  | HV channels | 18 | 30 | 48
Product | Description | Nch/ board | Qty base | Spare | Total boards | Total ch
SY4527 | Universal multichannel Power supply system - Basic 600W |  | 2 | 1 | 3 | 
A4533 | Optional double power supply unit 1200W |  | 2 | 1 | 3 | 
A2519A | (LV) LV Channels 15V 5A (50W) - DB37 conn - Individually floating (8ch) | 8 | 12 | 3 | 15 | 120
A1510 | (SEP) HV Channels 100V 10mA floating (12ch) | 12 | 2 | 0 | 2 | 24
A1519B | (HV) HV Channels 250V 0.1/1mA floating (12ch) | 12 | 4 | 1 | 5 | 60