## Slide 1: DCD submission plan
Changes in design (present status):
Change sampling of TDI for global and pixel register to positive edge
Add fast parallel sampling mode for easier needle card tests (maybe)
Improve test DAC resolution (?) by adding additional DAC
Programmable LVDS output current (or just larger)
Protection diodes should be on VDDD for digital
Investigate power up problem
Add transmission switch to monitor (now only PMOS)
Check the voltage drop on power rail – connect gate of the NMOS sources only in one point
Reduce RefIn current
Try to connect DAC Dump and SF VDDA to RefIn
Separated bias DACs for up and down bias
Spare ADCs
Alternative - Current through bias line
Redo protection diode, current drain/split nwell
Ipdac 60uA full range
SubIn 4 times or additional DAC
Introduce 15k Feedback resistor setting – low gain mode
Variable digital test patterns (?)

## Slide 2: DCD submission plan
Simulations:
ADC full/CMC+Comparator corner, mismatch, drop
Measurements:
RefIn/ALow vary whole chip
Current mismatch
Repeat after irradiation

## Slide 3: JTAG and slow controll
3
Global Register
G_Shift, G_Rb, G_Ld
Address
Pixel Register
P_Shift, P_Rb, P_Ld
Data Register
ShiftDR, CaptureDR, UpdateDR
Instruction Register
ShiftIR, CaptureIR, UpdateIR
ID Register
ShiftDR&IDSel
In
i
CaptureIn
LatchOut
PreLoad
Out
ExtTest
CaptureIn
LatchOut
o
Digital Block
ShiftDR, CaptureDR, UpdateDR
GlobalSel
TDI
FF
FF
FF
FF
ShiftDR, CaptureDR, UpdateDR
PixelSel
PixelSel
GlobalSel
ExtTest OR PreLoad
ShiftIR
The other if not ShiftIR
IDSel
Bypass
TDO
Pads
Commands
State M.
Cont. Signals
TMS
DO0(7:0),DI0(1:0),…,DI3(1:0),SYNC_RES,CLK,RetCLK,TestInjEn,DO4(7:0),…,DI7(1:0)
Readout Reg
CaptureIn
Full custom latches
Ld
TCK
o
Readout
CaptureIn
i
TestMode
Bitck
Res
Res!
TestMode
TestPads

## Slide 4: DCD Measurements
…

## Slide 5: DCD Measurements
….

## Slide 6: DCD submission plan
…
RefIn
Source
Source
240uA max
~300uA
~60uA
GNDA
VDDA
SF
AmpOut
VDDA
AmpIn
AmpInCM
RefIn
VDDA
Gate
This makes NMOS scs independent on GNDA noise
This makes current GNDA constant always
RefIn Current isn‘t constant
RefIn
RefIn

## Slide 7: DCD submission plan
…
DAC
Mirror
d
d

## Slide 8: DCD submission plan
…
DAC
DAC

## Slide 9: Origin of offset
Possibility: transistor mismatch – fix in the next chip: make the layout in a better way e.g. the transistors bigger
Additionally, there may be a systematic offset in comparator that adds to the mismatch
Notice also: two output nodes are not on perfectly same potential
Original UI converter connected to amplifier input, copy UI converter to RefIn – this explains RefIn dependence
Reduce RefIn voltage drop!
PFB
RefFB
Sc2
RefIn
Sc2
Sc2
RefIn
Sc2
RefFB
PFB
TooLow
24u
24u
24u
24u
26u
24u
Low

## Slide 10: SWITCHER Status
SWITCHER
Irradiation of latest SWITCHER has been done at KIT (dose 31 MRad)
The chip works after the irradiation
Bumping: bumping so far done in HD-lab, this works well for prototyping but is slow for production
Bumping with the required pitch (150 μm) is not offered by the vendor (AMS/IBM)
Solution: Company Pactec can place underbump metallization (ENIG) and solder bumps on single dies
SWITCHER submission planned for end of May 2015
Improvements: faster clear driver
Separated control of the termination resistance for serial input (should be always on) and for the other fast inputs

## Slide 11: Rise Time Measurements – irradiated chip
Irradiation to 21MRad – 150pF load
We need to increase size of the power transistors
Can be done, but the chip size will increase by 100um

## Slide 12: Simulation
Simulation of clear pulse with 150pF load
Output transistors 3 time wider
20ns

## Slide 13: Backup Slides

## Slide 14: DCDBPip
ADC
TIA
200 µm
5 mm

## Slide 15: ASICs Ivan Peric

## Slide 16: DCD

## Slide 17: KIT
The development/production of DCD and SWITCHER chips will be done from middle of 2015 at KIT
ASIC and detector laboratory (ADL) at the Institute for Data Processing and Electronics (IPE)

## Slide 18: DCDBPip
ADC
TIA
200 µm
5 mm

## Slide 19: DCD
DCD chip contains 256 channels, each channel has a DEPFET current receiver (trans-impedance amplifier) and an eight bit ADC
DCD specifications:
  Required number of channels (256)
  Sampling rate of about 100ns
  Radiation tolerance up to a dose of about 20MRad
  Noise which should allow good detection efficiency (~ 200e – SNR ~ 25)
  Power consumption not too high, current consumption ~ 1A
Resolution 10 bits (2-bit offset correction DAC and 8-bit ADC)
Dynamic range of up to 90uA (low gain mode 115nA/LSB) which should be enough to cope with DEPFET current that has signal and mismatch part
Non-standard fabrication process. After fabrication of standard layers (FEOL, BEOL) the chips are sent to another company which adds one extra layer, bump pads and bumps.

## Slide 20: DCD
Testing of these single dies is difficult
Due to space constrains if was not possible to implement standard differential pads – the chip’s IOs are not compatible with FPGA
Since the chip does not have wire bonds, it must be mounted onto adapter
Another ASIC must be used to convert DCD IO format to the standard one
Difficult characterization

## Slide 21: DCD
Different tests setups
To FPGA
DCD
DCDRO
Sensor
DCD
Tests on probe station
Tests on hybrid4 with DCDRO
Test with DEPFET or with test signal sources
adapter
PCB

## Slide 22: DCD
Different tests setups
DCD
DHP
Sensor
Tests on hybrid5 with DHP
Test with DEPFET or with test signal sources
Irradiation tests
adapter
PCB

## Slide 23: DCD
EMCM

## Slide 24: DCD tests on single chip PCB

## Slide 25: Chip #1 Test all ADCs

## Slide 26: Chip #1 Test all ADCs
…
ADC characteristics
Noise of the first ADC
Deviation from mean for every input
INL of the first ADC
Deviation from linear fit for every input
DNL: code difference for two consecutive inputs
(first ADC)
All ADCs:
Gain (nA/LSB)
Average noise (LSB)
INL (peak to peak for all inputs)
DNL (peak to peak for all inputs)
Gain vs. ADC position
Noise vs. ADC position
INL vs. ADC position
DNL vs. ADC position

## Slide 27: Chip #1 Test all ADCs
Several ADCs show higher noise (out of 128 tested)
Bad ADCs

## Slide 28: Chip #1 Test all ADCs
…
ADC gain 73nA/LSB
Noise floor: ~0.58LSB (92e @ gq 450pA/e)
3LSB
3LSBs
Noise of the ADC: ~1.3LSB (210e @ gq 450pA/e)
INL the „bad“ ADC: ~5.3LSB

## Slide 29: Chip #2 test all ADCs – fit (-100 to 125)
…

## Slide 30: Chip #2 Test all ADCs
Another chip: no bad ADCs – probably due to more careful optimization of bias parameters
ADC gain 72nA/LSB
Noise: ~0.55LSB
2.5LSB

## Slide 31: DCD tests on EMCM

## Slide 32: DCD
EMCM
All ASICs can be configured and read out, Switcher outputs ok
Small PXD6 matrix connected to DCDPipeline

## Slide 33: EMCM Tests
Digital test pattern has been used to tests the digital blocks and the communication DCD - DHP
bit | 29 | 30 | 31 | 0 | 1 | 2 | 3
7 | 0 | 0 | 0 | 1 | 0 | 0 | 0
6 | 1 | 1 | 0 | 0 | 0 | 1 | 1
5 | 1 | 1 | 0 | 0 | 0 | 1 | 1
4 | 1 | 1 | 0 | 0 | 0 | 1 | 1
3 | 1 | 1 | 0 | 0 | 0 | 1 | 1
2 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1 | 1
DCD digital block
Test pattern
ADCs
mux
DHP

## Slide 34: EMCM Tests
Digital test pattern has been used to tests the digital blocks and the communication DCD - DHP
~/TIMING/15_12_22_DCDpp0_1/test_pattern_of_dhpdcd0_bit61_SLDY_0.pdf
~/TIMING/15_12_22_DCDpp0_3/test_pattern_of_dhpdcd0_bit15_SLDY_0.pdf
305MHz, DCD1, VDDD=1.8V
250MHz, DCD1, VDDD=1.8V
column 223
(128ADU 160ADU)

## Slide 35: EMCM Tests
Digital test pattern has been used to tests the digital blocks and the communication DCD - DHP
~/TIMING/15_01_07_DCDpp0_1/test_pattern_of_dhpdcd0_bit0_SLDY_0.pdf
~/TIMING/15_01_08_DCDpp3_2/test_pattern_of_dhpdcd3_dcd_cmos_clk_dly_0_pll_ser_clk_dly_1.pdf
305MHz, DCD1, VDDD=1.9V
305MHz, DCD4, VDDD=1.9V
PLL_SER_
CLK_DLY=1
column 191
(128ADU 132ADU)
✔

## Slide 36: DCD Measurements
Test pattern
bit | 29 | 30 | 31 | 0 | 1 | 2 | 3
7 | 0 | 0 | 0 | 1 | 0 | 0 | 0
6 | 1 | 1 | 0 | 0 | 0 | 1 | 1
5 | 1 | 1 | 0 | 0 | 0 | 1 | 1
4 | 1 | 1 | 0 | 0 | 0 | 1 | 1
3 | 1 | 1 | 0 | 0 | 0 | 1 | 1
2 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1 | 1
Channel 191

## Slide 37: DCD Measurements
Test pattern
DCD ck
DCD data
Seen by DHP
Delayed data DHP
Synchronized by DHP
DCD digital block
VDD
Channel 191
DCD ck
Bias block
DCD
DHP
Duty cycle

## Slide 38: DCD Measurements
Digital communication works for ~ 99.5% channels
Can be improved (next submissions) by slight resizing of bias currents, delay elements in DHP and DCD
RLC models of DEPFET needed
bit | 29 | 30 | 31 | 0 | 1 | 2 | 3
7 | 0 | 0 | 0 | 1 | 0 | 0 | 0
6 | 1 | 1 | 0 | 0 | 0 | 1 | 1
5 | 1 | 1 | 0 | 0 | 0 | 1 | 1
4 | 1 | 1 | 0 | 0 | 0 | 1 | 1
3 | 1 | 1 | 0 | 0 | 0 | 1 | 1
2 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1 | 1
127
0
-127
127
0
-127
0
127
0
127
Channel 191
Ideal
Realistic
In DHP - CMOS
Reduced sampling window

## Slide 39: EMCM Tests
ADC readout – only one channel has unstable bit 6 (64) (digital problem?)
305MHz, DCD1, VDDD=1.9V
Column 209
ADU: 30, 31, 32, 33 & 63

## Slide 40: EMCM Tests
ADC characterization
ADCs have been measured using internal- and DHE current source
Only 3 ADCs with slightly higher noise – unstable bit (e.g. bit 5)
Column 52
ADU: 94, 95, 96, 126, 127

## Slide 41: EMCM Tests
ADC characterization
Noise measurement with LMU power supply on EMCN
Noise 0.5LSB < 100e
Only one ADC with noise ~ 1.5 LSB
4 DCDs on
daciampbias = 66
dacifbpbias = 80
dacipsource = 88
dacipsource2 = 77

## Slide 42: EMCM Tests
ADC characterization
Sw1
Sw2
Sw4
A
TC
DAC
24 μA
SF
Sub
Add
WrB*
WrB
NotRd
AmpLow
24 μA
12 μA
Logic
Cmp1
Cmp2
ThHi
ThLo
Rd
3
1
Iin
RefFB
RefIn
Cf
2
En
RefIn
4
Wr*
VFBPBias
VFBNBias (VPSource2)
VFBNCasc
VPSource
VAmpPBias
VPSourceCasc
Sw3
NotWr
NotRd AND Not Wr
Sw5
RefIn
RefNWELL
To Next Cell

## Slide 43: Operation of Matrix
Light sensitive
Still not optimized
/home/hybrid5/ADC_curves/DCD_noise/15_01_19_parser_DCD3_71th/dcdpp_3_dacvnsubin_7
/home/hybrid5/ADC_curves/DCD_noise/15_01_15_parser_DCD3_70th/dcdpp_3_dacvnsubin_7
18 rows
14 rows

## Slide 44: EMCM Tests
Different gain settings

## Slide 45: EMCM Tests
Missing code
„missing code“

## Slide 46: Missing Codes

## Slide 47: ADC unit-cell
The ADC-unit has two current-memory cells based on two U-I converters A and B
Depending on the input current amplitude (too low or too high), a reference current (4 μA per cell) will be added or subtracted
The comparison is done in the following way:
Two copies of the current stored in A are made – this is done with the two, layout-identical, UI converters CL and CH that are connected to the same voltage as A
The goal of this preprocessing is “to compress” the input signal so that it occupies 2x smaller range.
14u
A
CH
12u+/-4u
TooLow
TooHi
10u
12u+/-4u
CL
B

## Slide 48: Unit-cell characteristics
The purpose of the comparators is to assure that the reference currents are subtracted/added in the way so that the result current occupies two times smaller range
Only so, the error in algorithm is small
IIn
IOut
-2u
-4u
-8u
8u

## Slide 49: Unit-cell characteristics with offset
Imagine now that the ThHi threshold is shifted by Ref/4 (2uA) +Delta.
Imagine also that the signal is about Ref/2 (=64) In this case the result of the first comparison is zero. The result of all other comparisons is TooHigh. This leads to the binary code 64.
Imagine now that signals are within range Ref/2 and Ref/2+Delta. Obviously the binary code are always 64. This leads to the long code 64.
IIn
IOut
-2u
-4u
-8u
8u

## Slide 50: Bad characteristics causes missing codes
Missing codes around 64
IIn
IOut
-2u
-4u
-8u
8u

## Slide 51: Origin of offset
Why does the current offset happen?
Possibility: transistor mismatch – fix in the next chip: make the layout in a better way e.g. the transistors bigger
Additionally, there may be a systematic offset in comparator that adds to the mismatch
Notice also: two output nodes are not on perfectly same potential
Original UI converter connected to amplifier input, copy UI converter to RefIn – this explains RefIn dependence
We will verify our theory by measurements of the transistor currents. It is possible to access the output of one transconductor in every channel from outside.
PFB
RefFB
Sc2
RefIn
Sc2
Sc2
RefIn
Sc2
RefFB
PFB
TooLow
24u
24u
24u
24u
26u
24u
Low

## Slide 52: Monte-Carlo Simulation
We have started Monte Carlo simulations – according to first simulations mismatch is up to 1.5uA – which is still smaller than 2uA which produces missing codes.
However, the use of enclosed gates and mirroring can make the models not accurate.
Comparator input current for current memory cell current of 4uA (code 64)
If less than 0 we have a long code

## Slide 53: Unit-cell characteristics
The purpose of the comparators is to assure that the reference currents are subtracted/added in the way so that the result current occupies two times smaller range
Only so, the error in algorithm is small
IIn
IOut
-2u
-4u
-8u
8u

## Slide 54: Layout
The NMOS current source has a complicated structure
It is based on enclosed NMOS and a PMOS that should compensate for voltage drops (the simple version with only NMOS behaved worse on DCD1)
The layout is dense
Original cell
TooLow
TooHigh

## Slide 55: Layout
…
11u
18u
Old
New

## Slide 56: Layout
ADC
TIA
200 µm

## Slide 57: Missing codes
The problem can be solved by changing of layout, which can be done within one-two weeks.
Question: Is the long code problem worth of this effort
It reduces dynamic range by ¾
Dynamic range is still 20u which should be ok
„missing code“
20uA

## Slide 58: DCD submission plan
UMC run on 18. May
Changes in design (present status):
Resize of several transistors in ADC to fix the problem of missing codes
Change sampling of TDI for global and pixel register to positive edge
Add fast parallel sampling mode for easier needle card tests
Improve test DAC resolution
Programmable LVDS output current
Add transmission switch to monitor
Check the voltage drop on power rail – connect gate of the SubIn source only in one point
Try to connect DAC Dump and SF VDDA to RefIn
Separated bias dacs for up and down bias
RefIn
Source
Source
240uA max
~300uA
~60uA
GNDA
VDDA
SF
AmpOut
VDDA
AmpIn
AmpInCM
RefIn
VDDA
Gate
This makes NMOS scs independent on GNDA noise
This makes current GNDA constant always
RefIn Current isn‘t constant

## Slide 59: DCD submission plan
UMC run on 18. May
Changes in design (present status):
Resize of several transistors in ADC to fix the problem of missing codes
Change sampling of TDI for global and pixel register to positive edge
Add fast parallel sampling mode for easier needle card tests
Improve test DAC resolution
Programmable LVDS output current
Add transmission switch to monitor
Check the voltage drop on power rail – connect gate of the SubIn source only in one point
Try to connect DAC Dump and SF VDDA to RefIn
Separated bias dacs for up and down bias
RefIn
Source
Source
240uA max
~300uA
~60uA
GNDA
VDDA
SF
AmpOut
VDDA
AmpIn
AmpInCM
RefIn
VDDA
Gate
This makes NMOS scs independent on GNDA noise
This makes current GNDA constant always
RefIn Current isn‘t constant

## Slide 60: DCD Conclusions
DCD has been testes in various ways
All circuits have been tested
Probably the only problem is that usually some number of ADCs have a long code (mostly +64 but can be -64 or zero).
Our measurements are not consistent - measurements in Heidelberg show no long codes after optimization, measurements in Munich several channels from 256 affected
Question: is the long-lode issue critical? (It only reduces the dynamic range by 25% in some channels.) Can the present chip be used for production?
The fix for the long code problem is probably easy – resize of several transistors.
All other issues that we encountered during measurements are to my opinion either not related to DCD itself or fixed in the DCD pipeline design.
The problems in some channels (unstable bits, wrong digital patterns) are probably the issue of data transfer from DCD to DHP – large capacitances, not optimized delays, slow digital IOs

## Slide 61: DCD
Do we already have enough measurement results?
 We still did not test a properly working DEPFET module with DCDs…
 Measurements with EMCM show very low noise
 Configuration of all ASICs works well
 The DCD-DHP communication has been tested at somewhat reduced speed. Tests at full speed are not possible due to PLL/VCO/Delay element issue
We do not have many measurements with long DEPFET lines (and capacitances) on DCD inputs, however additional capacitance, according to simulation, does not introduce noise; it is just making the amplifier slower. Notice, a slower amplifier is not critical, since it equally reduces noise and signal. Signal to noise ratio is the same.
We have performed irradiations of DCD2 and DCDBv2. DCDBPipeline uses exactly the same circuits, just arranged in different way.
SEU tolerance of 180nm technology with 1.8V power supply is better than the SEU tolerance of 65nm technology.
The only issue could be the NMOS leakage current in the DCD digital part for the does range 1-5MRad. We will investigate this
Analog CMC has been tested on modular hybrid

## Slide 62: SWITCHER

## Slide 63: SWITCHER
SWITCEHR chips generate fast high-voltage pulses of up to 20 V amplitude to activate gate rows and to clear the internal DEPFET gates.
SWITCHER is implemented in HV AMS 180nm technology.
32 channels with a clear- and a gate-driver each.
SWITCHER in 180nm AMS

## Slide 64: DHP

## Slide 65: Thank you!

## Slide 66: DCD Measurements
Measure

## Slide 67: DCD Measurements
Measure

## Slide 68: DCD Measurements
Noise vs. Code
Bias V.
ADC
RC

## Slide 69: Problem of low ADC end
Problem of low ADC end
M1 current too weak
Resistance Sw too high
Out too low (Amplifier A saturates)
Low VT of PMOS not produced or bad corner – do corner simulation
Try
Increase Sc2
Decrease NMWELL voltage
Increase RefFB voltage
Decrease AmpLow (better Out_low), but increase IPAmp for higher in
In next chip – increase W/L of differential PMOS
PFB
RefFB
Sc2
Sc2
RefIn
24u
24u
24u
M1
Sw
Out