Test beam results from large pxd6 detectors
B. Schwenker
For the test beam crew
DEPFET Meeting Seoon 2015

---
Test beam 22-29 March @ DESY
- 3rd beam time with a large PXD6 sensor
- DEPFET integrated into EUDET telescope
- Tests with a 2nd large PXD sensor (I00)
    - No bending of silicon from gluing
    - 2bit pedestal correction used
    - LMU power supply used
    - But: only single DHP/DCD assembled
- Time for more systematic scans
    - Scan of trigger delay settings
    - Scan of hit threshold
    - Collect data from all sensor regions

---
The prototype detector – I00
(wrong figure, sorry)
I00
48x9.6mm^2
:- 480 rows / 192 columns
:- Pixel pitch: 50x100um²
:- Thickness: 50um
:- Cap. coupled clear gate
:- Only 1x DHP/DCD assembled
:- ASICS: DCDBv2, DHP02, SwitcherB1.8G
:- Speed: 250MHz (nominal 320MHz)

---
Local coordinate system and channel numbering (TB)
(wrong figure, sorry)
V, rows [0,480]
We see hits only from here
U; columns [0,192]

---
Large data sample
:- Landau from ~6.6 million
   matched hits
=> intense beam at DESY
=> 2 days data taking
:- Overlay hits from all scans
=> Mostly hit threshold 8LSB
=> Lowest threshold 4LSB
(few runs, rather noisy)
Edge from hit threhold
(→ cutting into signal)

---
Data from whole sens. area
:- >500 hits per pixel in some
   areas.
:- moved sensor up/down to
   get all area
:- illuminate ~100 rows at one
   Position
=> small tel. acceptance
~10mm
DEPFET
M26

---
Difference in number of hits
due to illumination time.
→ not a sensor problem
No hits from these two gates
→ probably problem of switcher
→ confirm in lab

---
Large pixel level
defect
Problems with
drain lines

---
Study of pixel gains
:- mean seed signal as proxy
   for pixel gain
:- cluster attached to pixel hit
   by the tel. track
:- tel track resolution ~5mu
   (at DEPFET plane)
:- Non brocken pixel have
> 200 hits (lower part)
~600 hits (upper part)

---
Zoom in to see more details
Differences > 5LSB
form one column to next
Twofold modulation
mean seed

---
(different color scale)
 :- rather poor uniformity gains,
   but why?
→ clear performance?
→ dynamic range (→ pedestal)?
→ transistor / gq?

---
“Low” threshold operation
:- tel. tracks to disentengle signal from noise
:- hit threshold @DHP set to 6LSB
→ we believe this should be a 10xnoise cut
→ however: noise and signal overlap

---
Occupancy Estimation
Occupancy = #noise hits / # triggers
:- DHP02 pedestal and common mode
:- noise hits = hit > 6LSB && far from tel. track
Noise occupancy<0.1% level

---
Occupancy Hybrid 4
Occupancy = #noise hits / # triggers
:- noise hits = cluster Threshold > 3LSB) far away from track
:- offline pedestal and common mode
Much less noise @ 2x lower cut

---
1D residuals (perp. incidence)
Mostly 1px clusters, few two pixels when track hits pixel edge
(having much better resolution)
50um pitch
Profits from charge sharing
(threshold 6LSB)
100um pitch
Shows perfect P/sqrt(12)

---
Efficiency vs seed charge threshold
PXD9: threshold of 2000e still ok.
Good agreement with simulation
for Hybrid 4 (50 micron thick)
Extrapolation for PXD9
(75 micron thick)

---
Now, change angle of incidence
H4.1.15 beam data @ 37° tilt of sensor
→ on average more signal per seed than perp.
→ allows to go to higher thresholds
For reasonable aspect ratio, perp. incidence gives smallest signal per pixel
and defines a lower bound for hit threshold.

---
Summary
- Used the beam time to collect high statistic data sample.
  - Response from all parts of sensor
- As expected: many sensor defects observed, mostly related to metal system.
  - Gains uniformity is poor, needs to be understood
- Some benchmark numbers
  - Landau MPV: 15.5LSB
  - Noise occupancy: ~0.1% (@6LSB threshold)
  - Efficiency: please do not ask
- Setting the hit threshold for PXD9
  - For PXD6 on H4: 1200e threshold was efficient
    - Still, this number should be confirmed with large sensor.
  - For PXD9 on MC: 2000e threshod can be efficient (larger signal)

---
Thanks