## Slide 1: Module/Ladder Assembly
Receive module from flip chip, inspection
SMD assembly in base jig
Tests (needle card)
Kapton assembly (soldering, wire bonding)
Full test & characterisation
Glue two modules to a ladder
Test
Need jigs and tooling for each step
Module fixation for handling
Storage and transport
Tests (cooling)
Tooling

## Slide 2
Base jig sensor
For transport and bonding
Fits on NTC stage (vacuum)

## Slide 3
Transport base
For transport and storage

## Slide 4
Transport cover, sensor

## Slide 5
Cooling plate
(for tests)

## Slide 6
Kapton jig
- shaped, to keep bending

## Slide 7
Kapton jig fitted to base jig
Including cooling for solder joint

## Slide 8
wire bonding

## Slide 9
Finished module
Ready for testing
Lid can be opened to access Kapton

## Slide 10
With protective cover for transport and storage
All components show so far are in work
(7 base jigs are ready)

## Slide 11
Prepare for ladder gluing
open
Vacuum jig for turning and ladder gluing
Fits on top side (cut outs for switcher)
Mode from microporous plate (gentle vacuum on sensor top side)

## Slide 12
Vacuum jig on sensor
Connect kapton extension to vacuum jig
Disconnect base jig

## Slide 13
Lift off from base jig and turn over

## Slide 14
Add cover

## Slide 15
Mask for applying the glue
In order to ensure a well defined glue thickness: use shims to adjust height
Needs tests!

## Slide 16
Alignment stage

## Slide 17
Attach one module…..

## Slide 18
And the 2nd one
Old drawing: alignment screws are in wrong position

## Slide 19
Align, push together & cure

## Slide 20
Remove fixations

## Slide 21
Add base jig, ladder

## Slide 22
Take off from alignment stage

## Slide 23
turn over

## Slide 24
Remove gluing jigs

## Slide 25
Base plate for tests (cooling)
Transport and storage

## Slide 26
Basic jigs already produced (for pilot run)
5 outer backward
2 outer forward
(2 jigs will be anodized)
Other components (up to gluing jig) are in work
Stages for alignment station delivered