Heidelberg-Moscow
and Evidence for 0nubb?
experiment
Daniel Lenz
Cresst – Gerda – FMC(?) Seminar

---
Overview
Theory Introduction to 0nubb
Experimental Setup of Heidelberg Moscow Experiment
Phys. Rev. D 55, 54 (1997)
Background Reduction and Background
Phys. Rev. D 55, 54 (1997)
Latest results from the Heidelberg-Moscow double beta decay experiment
Eur. Phys. J. A 12, 147-154 (2001)
EVIDENCE FOR NEUTRINOLESS DOUBLE BETA DECAY
Mod. Phys. Lett. A16 2409-2420 (2001)	hep-ph/0201231
COMMENT ON “EVIDENCE FOR NEUTRINOLESS DOUBLE BETA DECAY“
Mod. Phys. Lett. A 17 1475-1478 (2002) hep-ex/0202018
Reply to the Comment on “Evidence for Neutrinoless Double Beta Decay“
hep-ph/0205293 v1
REPLY TO A COMMENT OF ARTICLE “EVIDENCE FOR NEUTRINOLESS DOUBLE BETA DECAY“
hep-ph/0205228 v2
Explanations?	Summary	Conclusion
nucl-ex/0704.0306v4

---
Theory Introduction to 0nubb
(A,Z)  (A, Z+2) + 2e-
L 0
happens, if    & m>0
n
e-
e-
p
n
p
R
L
W-
W-

---
Experimental Setup
5 enriched (86%) HPGe p-type detectors used
total: 11.51 kg 10.96 kg
Advantages:
excellent energy resolution at 2039 keV of 3.59 +- 0.26 keV
large size => large peak to compton ratio
source = detector => large source strength and high efficiency

---
Experimental Setup
Underground in Gran Sasso approx. 3500 m.w.e
Shielding:
Detector “enr No. 1,2,3,5“ in Pb cryostat
muon shield
boron PE shield (added later on)
air-tight steel box
with nitrogen gas
30 cm Pb shield:
outer 20 cm Boliden (standard) Pb
inner 10 cm radiopure
LC2-grade (~10Bq/kg) Pb

---
Experimental Setup
Detector “enr No. 4“ in Cu cryostat
Shielding:
air-tight steel box
with nitrogen gas
boron PE shield
47.5 cm shield:
outer 20 cm Pb
27.5 cm electrolytical Cu

---
Background Reduction
Detector “enr No. 4“
10E5 count rate reduction
After Bo-PE shield installation:
Overall decrease in count rate: (7.5 +- 0.5)%
Decrease in ROI count rate: (22.5 +- 13)%

---
Background
Phys. Rev. D 55, 54 (1997)
Phys. Rev. D 55, 54 (1997)
Backgrounds:
gammas:
cosmogenic:
anthropological
natural decay chains
U238, Th232, K40
Co60
Cs137
NO external alphas & betas due to 0.7 mm dead-layer
elastic & inelastic neutron scat
direct muon induced events
BUT slight contamination of detector 4,5 with Pb210 ~muBq/kg

---
Background Simulation
enr No. 2
enr No. 2
each detector scanned with collimated Ba133 source
detector enr No. 1,2,3 simulated
evaluation done using 4 strongest gamma lines => error of ~6 %
 Figure: Th228 data-MC:
low energy bad, 2mm uncertainty in src-position, src partially covered Pb
above 500 keV less than 10 % deviation

---
Latest Results from the HDM 0nubb...
 Eur. Phys. J. A12, 147-154 (2001)	hep-ph/0103062
Identified 142 lines in spectrum
Bkg simulated
=> 5 main locations of radioactive contamination
position estimated from least square fit of peak intensity
LC2-Pb shield,
Copper shield,
Copper+plastic parts of cryostat,
Ge-crystals
No muon induced events simulated
(too large uncertainties in GEANT3.21)
Activities of K40 and Pb210
      in LC2 Pb measured

---
Latest Results from the HDM 0nubb...
 Eur. Phys. J. A12, 147-154 (2001)	hep-ph/0103062
energy resolution(2039keV):
(4.23+-0.14)keV
expected background(2-2.080 MeV)
(0.19+-0.01) cts/(kg y keV)
expected background 3 sigma region
(110.3+-3.9) events
measured:
112 events
Result:
T1/2 >= 1.3 E25 y (90% C.L.)	53.9 kg * y
T1/2 >= 1.9 E25 y (90% C.L.)	35.5 kg * y	PSA!!!

---
Evidence for 0nubb decay
Mod. Phys. Lett. A16 2409-2420 (2001)	hep-ph/0201231
~ same dataset as before!
Eur. Phys. J. A12, 147-154 (2001)
hep-ph/0103062
energy resolution(2039keV):
(4.00+-0.39) keV
background rate (2. -2.08 MeV):
(0.17+-0.01) cts / (kg y keV)
assume all data = bkg
statistical significance:
54.981 kg * y

---
Evidence for 0nubb decay
Mod. Phys. Lett. A16 2409-2420 (2001)	hep-ph/0201231
All detectors
known Bi214 lines:
2021.8 keV
Bayesian peak detection algorithm
applied
2016.7 keV
not
expected
2052.9 keV
2010.7 keV

---
Evidence for 0nubb decay
Mod. Phys. Lett. A16 2409-2420 (2001)	hep-ph/0201231
Detectors 1,2,3,5
known Bi214 lines:
2021.8 keV
2016.7 keV
not
expected
2052.9 keV
2010.7 keV

---
Evidence for 0nubb decay
Mod. Phys. Lett. A16 2409-2420 (2001)	hep-ph/0201231
Detectors 2,3,5
with PSA
known Bi214 lines:
2021.8 keV
2016.7 keV
not
expected
2010.7 keV
2052.9 keV

---
Evidence for 0nubb decay
Mod. Phys. Lett. A16 2409-2420 (2001)	hep-ph/0201231
with probability 97.4% C.L.
line found at Q_bb
# events: 1.2 – 20.4 (95% C.L.)
best value: 14.8 events
0.11 eV < <m> < 0.56 eV
T1/2 = (0.8-18.3) E25 y (95% C.L.)
Evidence for 0nubb decay:

---
Comment on “Evidence for 0nubb...“
hep-ex/0202018v3
No null hypothesis in analysis!
No MC simulation done to confirm peak finding method!
3 unidentified peaks with greater significance than 2039 keV peak!
No discussion of sensitivity of conclusions to different mathematical models!
i.e. HDM T1/2 limits in conflict with best fit Evidence T1/2
Cross checks to be done:
How does variation of window size affect peak finding? Not shown!
No relative peak strength analysis of Bi214 peaks
No discussion of rel. peak strenght of Bi214 peaks
before and after SSE cut

---
Evidence for 0nubb decay
Mod. Phys. Lett. A16 2409-2420 (2001)	hep-ph/0201231
~ same dataset as before!
Eur. Phys. J. A12, 147-154 (2001)
hep-ph/0103062
energy resolution(2039keV):
(4.00+-0.39) keV
(4.23+-0.14) keV
background rate (2. -2.08 MeV):
(0.17+-0.01) cts / (kg y keV)
assume all data = bkg
(0.19+-0.01) cts/(kg y keV)
statistical significance:
54.981 kg * y
53.93 kg * y

---
Evidence for 0nubb decay
Mod. Phys. Lett. A16 2409-2420 (2001)	hep-ph/0201231
All detectors
known Bi214 lines:
2021.8 keV
2016.7 keV
not
expected
2052.9 keV
2010.7 keV
?
Peak finding?

---
Evidence for 0nubb decay
Mod. Phys. Lett. A16 2409-2420 (2001)	hep-ph/0201231
Detectors 1,2,3,5
known Bi214 lines:
2021.8 keV
2016.7 keV
Peak finding?
not
expected
2052.9 keV
2010.7 keV
?
?

---
Evidence for 0nubb decay
Mod. Phys. Lett. A16 2409-2420 (2001)	hep-ph/0201231
Detectors 2,3,5
with PSA
known Bi214 lines:
2021.8 keV
2016.7 keV
2052.9 keV
not
expected
2010.7 keV
?
?
?

---
Relative Strength of Bi214 Peaks
No full spectrum given in “Evidence“ paper, but in “Latest results...“ paper
Dataset similar,
give similar background values....
Estimate rate in Bi214 peaks
Table of Isotopes
Assume: peak width ~ 4 keV
0.08 cts/(kg y) * 1 / 4 keV
= 0.02 cts/(keV kg y)
in peak!!!
Remember: Bkg = 0.17 cts/(keV kg y)
After 46.5 (kg y): 4 cts in peak over bkg of ~ 32 cts

---
Replys to Comments on “Evidence...“
Harney: hep-ph/0205293v1	Klapdor-Kleingrothaus: hep-ph/0205293v1
“There is no rel. peak strength analysis of all the Bi214 peaks“
H: Analysis done under assumption that peaks showing up in (a) can be identified at least ones closest to Q_bb. Otherwise significance decreases.
Peak strength: Situation is not as bad as critics conclude for 2 reasons:
1: Exp. rate is larger by factor of ~ 9 since plot normalization is wrong!
2: Not taken into account “Coincidence Summing“ effect
    => Intensities not prop to branching ratios!
MC Simulation needed!
K: 2 reasons: see above 1,2
       simulation: lines are consistent within 2 sigma experimental errors
Comment on the Evidence
including factor 9
Firestone
H: If peaks cannot be identified by way of simulation, confidence will be lower.
     I expect from Table that this is the case because half of intensity to left and about 20% of peak at 2053 keV are predicted by simulation.

---
Replys to Comments on “Evidence...“
Harney: hep-ph/0205293v1	Klapdor-Kleingrothaus: hep-ph/0205228v2
“No discussion of how variation of size of the analysis window
would affect the significance“
H: This is not true. Impact of variation was qualetatively shown in comparison of parts (a) and (b) of figures. Still I consider the size of the analysis window the most serious part of the critisism.
K: This is not true. Figures show difference obtained for the probability of signal in large and small window. Details in forthcoming paper.
“with an appropriate window the evidence for a peak at Q_0 can reach the 3 sigma level. Both the evidence and the central value of the signal change when the size of the window is varied. There is almost no evidence when a large window is chosen; but if the backgrounds were constant, a large window would be the fairest way to estimate its level“
Feruglio et al. hep-ph/0201291v5

---
Replys to Comments on “Evidence...“
Harney: hep-ph/0205293v1	Klapdor-Kleingrothaus: hep-ph/0205293v1
“There are three unidentified peaks in the region of analysis that have greater significance than the 2039 keV peak“
H: Since they have higher significance than the significance claimed for the peak at Q_bb, even future improved analyses need not necessarily consider these peaks to be part of the background. In principle there is no reason to consider all non-identified structures as fluctuations of the background. Peaks that have a high significance may be considered a spectral line although unknown at present.
K: True, there are lines beyond 2060 keV which cannot be identified. However this is not relevant to conclusions concerning the signal at 2039 keV.
“No simulation performed to demonstrate that analysis correctly finds true peaks or none, if none exsisted “
H: This cannot be demonstrated. The randomness of data entails probabilistic conclusions.
K: Not true, simulations performed to show that programs work OK. Ensemble-tests have shown that probability to find line if none present above 95% C.L. is 4.2%

---
Replys to Comments on “Evidence...“
Harney: hep-ph/0205293v1	Klapdor-Kleingrothaus: hep-ph/0205293v1
“There is no discussion of how sensitive the conclusions are to different mathematical models[...] There is a previous HDM publication that gives lower limit of 1.9E25 y (90%C.L.). This is in conflict with “best value“ of new paper 1.5E25 y. “
H: Unfortunately any results are sensitive to the model one chooses to describe peak plus background. The comparison between (a) and (b) shows it since size of the window is part of the model.
K: This is not true. No discrepancy!
“There is no null hypothesis analysis demonstration that data requires peak“
H: Statement that there is peak with probability K implies that there may be none.
     Results are probabilistic impossible to demonstrate data requires peak.
K: This is not true. Fit allows for case: only background, line intensity zero

---
Replys to Comments on “Evidence...“
Harney: hep-ph/0205293v1	Klapdor-Kleingrothaus: hep-ph/0205293v1
“There is no discussion of the relative peak strengths before and after single-site cut.“
H: Intensitiy at Q_bb before and after cut are compatible if efficiency taken into account.
K: 90% of signal after SS cut, Bi214 lines reduced to about 25% same reduction as stronger Bi214 lines and 2614 keV Th line.
const bkg suppression:
~ 3.5/0.55
identified gammas:
~ 3.8/0.55
0nubb:
~ 3.2/0.55
Feruglio et al. hep-ph/0201291v5

---
Replys to Comments on “Evidence...“
Harney: hep-ph/0205293v1	Klapdor-Kleingrothaus: hep-ph/0205293v1
Summary:
Harney:
The critics have made a valuable point with their concern about the size of the analysis window;the simulation of the experimental setup indicates that the significance of the possible structure at Q_bb is lower than claimed by KDHK.
Klapdor:
The criticism made in the 'Comment' is, in view of the Replies given here, not justified in any of the points raised.
We think that it remains useful and inspiring to have informed the neutrino community about our evidence for a 2.2 – 3.1 sigma result on the 0nubb decay.

---
Explanations?
nucl-ex/0704.0306v4
Excited states of Pb through neutron inelastic scattering
predicted rate too low to explain peak
No peak at 3062 keV would expect ~175 cts in peak
DEP: single site event
        => Possible candidate
DEP @ 2040 keV

---
Summary
HDM sees no evidence but set lower limit
Klapdor & Co. sees evidence if peaks close to Q_bb are identified (Energy,Intensity)
Harney doubts that peak with that high significance
exists after MC simulations
Klapdor sees no problem with MC simulation of peaks
since agree within 2 sigma
Pulse shape analysis:
 H: Signal before after cut compatible
K: 90% of signal left, 25 % of gammas left
F: all peaks reduced in the same way
Other explanations failed to describe spectrum
Latest Klapdor paper sees 6 sigma evidence with same dataset !

---
Conclusions
?