## Slide 1: The Belle II Vertex Pixel Detector (PXD)
Felix Müller

## Slide 2: Outline
SuperKEKB and Belle II
Vertex Detector (VXD)
Pixel Detector (PXD) and its characteristics
DEPFET technology and working principle
The readout electronics
Gated Mode Operation
Summary and future plans

## Slide 3: SuperKEKB upgrade
Belle II
Nano beam scheme  smaller beam size (~nm) & increased beam currents (x2)
L = 8 x 1035 cm-2 s-1 (40x larger than in KEKB)
Ee- = 7 (8) GeV & Ee+ = 4 (3.5) GeV
(bg = 0.42 (KEK)  0.28 (SuperKEK))
Ecm = 10.58 GeV - Y(4S)
Changes involving the Vertex Detector (VXD):
Four layers of Double Sided Si-Strip Detector (DSSD) with a larger radius
Two layers of DEPFET pixel detector (PXD)

## Slide 4: Vertex Detector (VXD)
Tasks of the vertex detector:
Reconstruction of primary, secondary, … vertices of short-lived particles
  Decay of particles is typical in the order of 100 µm from the IP
Detect tracks of low momentum particles (in high B field) which cannot make it to the main tracker
  Innermost detector system as close as possible to IP
  highly granular pixel sensors; provide most accurate 2D position information
  should be massless and still provide a large enough S/N
  Design and specifications to a larger extent driven by machine/beam characteristics
    Beam background, radiation
    damage, occupancy …
BELLE PHYSICS II (Friday 11-12)

## Slide 5: Vertex Detector (VXD)
Silicon Vertex Detector (SVD)
4 layers of double sided silicon strip detector
R= 3.8 cm, 8.0 cm, 11.5 cm, 14 cm
Pixel Detector (PXD)
2 layers of DEPFET pixels
R = 1.4 cm, 2.2 cm

## Slide 6: PXD detector requirements
Belle II is dominated by low momentum tracks
Modest intrinsic resolution (15 μm), dominated by multiple scattering → Moderate pixel size (50 x 75 μm²)
Lowest possible material budget (0.2% X0/layer) [including ASICs]
Due to higher background (20x-40x): Radiation damage and occupancy, fake hits and pile-up noise
10x higher event rate => higher trigger rate
Replace inner layers of SVD with PXD
Occupancy | 0.1 hits/µm²/s
Frame time | 20µs (rolling shutter mode)
Momentum range | Low momentum (<1GeV)
Acceptance | 17°-150°
Radiation | ~20 kGy/year, 1·1010 n/ab-1cm²

## Slide 7: Mockup of the Belle II PXD Detector
Beam pipe radius:
10 mm (inner), 12.5 mm (outer)
Half Ladder

## Slide 8: Half Ladder of DEPFET PXD
256 x 250 pixels
55 x 50 µm² (L1)
70 x 50 µm² (L2)
512 x 250 pixels
60 x 50 µm² (L1)
85 x 50 µm² (L2)
~0.2%X0 per layer
 | Inner Layer (L1) | Outer Layer (L2)
# Modules | 8 | 12
Distance from IP (cm) | 1.4 | 2.2
Thickness (µm) | 75 | 75
Total # pixels | 3.072 x 106 | 4.608 x 106
Pixel size (µm²) | 55, 60 x 50 | 70, 85 x 50
Sensitive area (mm²) | 44.8 x 12.5 | 61.44 x 12.5
Sensor length (mm) | 90 | 123
Frame/Row rate | 50 kHz / 10MHz | 50 kHz / 10 MHz

## Slide 9: DEPFET (Depleted p-channel Field Effect Transistor)
impinging
particle
Clear
Turn on DEPFET
source
Gate

## Slide 10: DEPFET (DEPleted p-channel Field Effect Transistor)
A DEPFET is a MOSFET onto a sideward depleted silicon bulk
Impinging
particle
→ Low noise
→ Low power
→ High signal/noise-ratio
→ Non-destructive readout
Cross-section of a DEPFET
internal amplification:
gq0.5 nA/e-
90 steps fabrication process
9 Implantations
19 Lithographies
2 Polysilicon layers
2 Aluminum layers
1 Copper layer
Back side processing

## Slide 11: Rolling Shutter Mode
row1 (on/off)
Gate
Source
DCD
Drain1
row2 (on/off)
Gate
row3 (on/off)
Gate
row4 (on/off)
Gate
row5 (on/off)
Gate
row1 (on/off)
Clear
row2 (on/off)
Clear
row3 (on/off)
Clear
row4 (on/off)
Clear
row5 (on/off)
Clear

## Slide 12: Control and readout electronics
SWITCHER
Fast voltage pulses up to 20 V to activate gate rows and to clear the internal gate
JTAG for interconnectivity tests
64 output drivers for both gate and clear channels  address 32 matrix segments
768 rows  192 electrical rows  6 ASICs needed per module
Drain Current Digitizer (DCD)
Keeps the columns line potential constant
8 bit ADCs
Compensates for pedestal current variation (2bit DAC)
Programmable gain and BW
256 input channels (4 per module)
Data Handling Processor (DHP)
Pedestal correction
Common mode correction
Data reduction using the zero suppression
Triggered readout scheme introduces
further data reduction
Controls the Switcher sequence
Kapton Flex cable
Power Supply via soldered contacts and bond wires
Data transmission via bond wires
4 layers, 48 cm
DEPFET

## Slide 13: Lab Measurements and Beam Test
Switcher
B-18v1.0
DCDBv2
DHP0.2
seed charge
Laser scan 5x6 pixels
Test Beam,
2013
gq ~ 450 pA/e-
cluster charge
Laser scan 5x6 pixels
Homogeneous charge collection
PXD6
50x75µm²
50µm

## Slide 14: Injection Scheme of SuperKEKB
continuous injection every 20 ms
„noisy bunches“ create (junk) electrons within the Pixel Detector (PXD)
mask noisy bunches  PXD deadtime = 20%
best solution: gate the DEPFET during the passage of the noisy bunches
Make detector „blind“
Two questions for our Test-Set-up:
Can we protect charge in the internal Gate from being cleared?
How much of the junk charge will arrive in the internal Gate?
Applying appropriate voltages to Clear and Gate one can apply an electronic shutter:
    Clear pulse to all pixels during the noisy bunch injection
    Keep the Gate in the off state
Intensity of particle beam decreasing, cooling down takes 4ms (worst case throw away all noisy recordings)  again intriguing property of DEPFET detector

## Slide 15: Selectivity of the Clear Process
Real Clear
External Gate in on state
Suppressed Clear
External Gate in off state
Electrons can overcome the
small potential barrier (<0.5V)
by thermionic emission
The difference is due to the applied voltage at the external gate
external gate shifts the potential of the internal gate by capacitive coupling  e- stay in internal gate

## Slide 16: Hybrid 4 Setup – ASICs supporting GatedMode
SwitcherB18v2
Read-Out with DCDBpipeline
PXD6 Matrix
FPGA
Lab Setup: small matrix, i.e. 64 rows, 32 columns
(Experiment: large matrix, i.e. 768rows, 250columns)
Laser impinges from backside due to metal layers

## Slide 17: Signal Charge Restore
Frame # | Frame 1 | Frame 2 | Frame 3 | Frame 4 | Frame 5 | Frame 6 | Frame 7 | Frame 8
Normal sequence | Read No reset | Read No reset | Laser Read No Reset | Read No Reset | Gated Mode | Gated Mode | Read No Reset | Read Reset/Clear
Frame 1 2 3 4 5 6 7 8
Lab Setup: small matrix, i.e. 64 rows, 32 columns
(Experiment: large matrix, i.e. 768rows, 250columns)

## Slide 18: Gated Mode w/o Readout
1,6ms
Impinge Laser
Charge is generated
Charge is collected
Read
rolling shutter mode
Gated Mode
Gated Mode
Read

## Slide 19: Junk Charge Generation
Frame # | Frame 1 | Frame 2 | Frame 3 | Frame 4 | Frame 5 | Frame 6 | Frame 7 | Frame 8
Normal sequence | Laser Read No Reset | Read No reset | Read Reset/Clear | Gated Mode | Gated Mode | Gated Mode | Read No Reset | Read No Reset
Lab Setup: small matrix, i.e. 64 rows, 32 columns
(Experiment: large matrix, i.e. 768rows, 250columns)

## Slide 20: Gated Mode w/o ReadOut – Junk Charge Generation
Read&Clear
ReadnoClear
ReadnoClear
+ Laser
Gated &
Readout
Gated & Laser & Readout
Gated & Readout
ReadnoClear
ReadnoClear

## Slide 21: Gated Mode with ReadOut – Junk Charge Generation
Read&Clear
ReadnoClear
ReadnoClear
+ Laser
Gated
Gated
+Laser
Gated
ReadnoClear
ReadnoClear
rows sensitive for 100ns

## Slide 22: Summary and Outlook
Measurements with small matrix and one set of ASIC pair
Many beam tests to study performance
Proof of GatedMode operation to „noisy“ bunches
Future plans:
Use silicon substrate as supporting structure for ASICs and Sensor (-> next talk by Jakob Haidl)
Operate system in an experimental environment (14 ASICs, small capacitors, no surrounding PCB)
Next months: large prototype sensor („pilot-run“) equipped with latest generation of ASICs: characterization of ASICs / operation of matrix