## Slide 1
overview and introduction including plans and schedule
- need the first set of tested and understood ASICs by March 2015 
- dates:
- DHP: 26.8.  1.12., 100 chips
- DCD: 31.8.  1.1.15 (including bumping), 80-100 chips
- SWB: 24.8. ???  ???  +4-6 weeks bumping
A block of detailed presentations of measurement results from experts - the links between DCD/DHP - Leo
- findings at the recent irradiation campaign – Philipp - IDrain dispersion on sensor, including "fixed pattern“, PXD6/PXD9 comparison - Rainer - consequences for dynamic range - Florian - Gated Mode seen from the DCD/DHP and SWB perspective - Christian Koffmane
- how well is this implemented already and what measurements do we still need?
- DCD recovery after blind mode
- Missing (long codes) – Benjamin
- in what extent do we still have them? - relevance for the experiment
- ways to live with that if we cannot avoid them

## Slide 2
3. Two long talks from Hans and Ivan on DHP and DCD/SWB
- specs for ASICs
- summarizing the issues
- presenting conclusions and the planned changes with priorities
- work load
- time scale
- risk assessment.

## Slide 3: Reviewer’s comments
General remarks
For coordination reasons, it would be helpful if the management could present one, agreed-upon schedule.
Switcher
Generally in good shape:
  Concept proven
  Performance: only concern is speed of Clear signal
Required changes look modest
Recommendations:
• End users should review Reference Manual for completeness
  o Are pin table listings sufficient?
  o Interface control description adequate?
• Recommend creating Hardware Description Language description of Gating functionality
• Concern regarding radiation hardness of the HV transistors
• We endorse performing detailed tests of the Gated Mode operation
• We recommend investigating long-term burn-in/stress testing of HV operation

## Slide 4: Reviewer’s comments
Switcher
Specific charged items:
:- Comprehensive Specification document lacking.
Reference Manual is a good start, needs to be expanded to include performance requirements.
:- Additional Gated Mode testing needed.
Further radiation hardness testing likewise needed.
:- Recommend clarifying test program leading to ASIC revision.
Designer needs to clarify scope of modification, which will drive the schedule.
:- General test plan looks reasonable.
The committee expresses concern regarding the proposed ASIC modifications to
support multiplexed testing (additional HV-LV conversion, output multiplexing).

## Slide 5: Reviewer’s comments
DCD
• Basic architecture looks well suited to the requirements
• The committee expresses serious concerns about the details of the ADC implementation
  o Unclear if problems observed are sensitivities to process parameters
  o Further design work needed
:- We foresee significant additional design effort to address concerns regarding the ADC
:- A comprehensive Specification Document is lacking.
:- Strongly recommend further testing to understand variety of pathologies observed.
Further ASIC/channel testing statistics are needed.
:- Matching of observation with simulation is mandatory.
:- More an issue of understanding results observed that missing measurements.
Encourage further, cross-checked analyses.
:- Highly important that before next submission these problems are fully understood
Given the above concerns, a February submission seems very aggressive. Items above must be resolved prior to submission. Verifying Monte Carlo spreads will likely take time, and sufficient time should be allocated.

## Slide 6: Reviewer’s comments
DHP
:- Specifications still not concisely presented
:- Cannot put all effort on the ASIC side. System engineering of cabling and interconnects,
and an agreed-upon model for output load is needed.
:- Complexity makes testing difficult
:- Remaining concern is in the verification of the high-speed interfaces.
:- Specifications for output loads and timing are needed for signals in Table 1 of the Manual.
For such a complex device, a more comprehensive document may be required.
:- Finer step TID testing, SEU testing. Channel masking and Overflow handling tests self-identified.
:- Not clear who is doing what to provide further testing and by when.
A detailed model of the cabling needed to complete output driver redesign.
:- A rigorous internal review of the proposed changes should be held prior to release for submission.
Recommendations:
Characterize the electrical properties of the external interconnects and cables.

## Slide 7: Reviewer’s comments
DHP
:- Remaining concern is in the verification of the high-speed interfaces.
:- Specifications for output loads and timing are needed for signals in Table 1 of the Manual.
For such a complex device, a more comprehensive document may be required.
:- Finer step TID testing, SEU testing. Channel masking and Overflow handling tests self-identified.
:- Not clear who is doing what to provide further testing and by when.
A detailed model of the cabling needed to complete output driver redesign.
:- A rigorous internal review of the proposed changes should be held prior to release for submission.
Recommendations:
Characterize the electrical properties of the external interconnects and cables.