## Slide 1: SVD Overview
Christoph Schwanda Institute of High Energy Physics Austrian Academy of Sciences
8th Belle II VXD Workshop September 9-11, 2015 Trieste, ITALY

## Slide 2: Belle II Vertex Detectors
PiXel Detector (PXD)
  Based on DEPFET pixels – see previous talk
Silicon Vertex Detector (SVD)
  Double-sided silicon strip detectors (DSSDs)
PXD
SVD
Fast – to operate in high background environment
Better resolution at IP – to compensate reduction of boost wrt. Belle I
Radiation hard (up to 100 kGy)
Self-tracking capable – to track particles down to 50 MeV in pT
VXD requirements

## Slide 3: Belle II SVD Components
4 Layers double sided silicon strip detectors
2,3,4 or 5 sensors per ladder
Ladders
End rings
Carbon fiber (CF) cone
End flange
PXD (inside SVD  individual sub-detector)
Outer CF shell
Beam pipe

## Slide 4: SVD ladders
L6 Ladder (Kavli IPMU)
L5 Ladder
(HEPHY)
L4 Ladder (TIFR)
L3 Ladder (Melbourne)
FWD module
BWD module
Origami +z
Origami ce
Origami -z
BWD
FWD
Cooling pipe
Cooling pipe
Cooling pipe
BWD module (Pisa)
FWD module
(Pisa)
Layer | Ladders | Sensors / Ladder
6 | 16 | 5
5 | 12 | 4
4 | 10 | 3
3 | 7 | 2

## Slide 5: Ladder anatomy (L5)
Origami hybrids (with APV frontend readout chips)
Airex sheet (insulator)
Sensors
Carbon fiber sandwich ribs

## Slide 6
FW/BW (Pisa)
L3 (Melbourne)
L4 (TIFR)
L5 (HEPHY)
L6 (Kavli IPMU)
All sites have successfully assembled SVD ladders with the final components

## Slide 7: Status at the assembly sites
FW/BW (Pisa)
  Site passed final qualification review on May 29 and is now in production mode
L3 (Melbourne)
  Site assembled two class C ladders (L3.902 and L3.903) and is now moving to the first electrically working ladder (class B)
L5 (HEPHY Vienna)
  Site passed final qualification review on Aug 6
  Very recently completed first production-grade ladder (L5.001) ® origami evaluation
L4 (TIFR)/L6 (Kavli IMPU)
  Both assembled class C and B ladders, close to production readiness
  Main outstanding issue: shift of FW sensor

## Slide 8
Results class C L3 survey

## Slide 9
Ladder survey
Overview of average offsets of each Ladder [µm]
Results class C L5 survey

## Slide 10
Results class C L4 survey

## Slide 11
Results L6 survey

## Slide 13: Ladder parts availability
Sensors
  Three types of DSSD sensors: Micron (trapezoidal), small and large HPK (rectangular)
  After a detailed inventory and sensor grading revision, we conclude that sensors are in hand to produce the detector including 2 spares/layer with a safety factor (~20%)
  Only 5 small HPK sensors for L3 need to be reproduced (available ~end 2015)
Origami
  In autumn 2014 we lost the origami mass production due to cracks in the PA0 lines
  PA0 redesign, origami pre-production, requalification

## Slide 14: Source run with pre-production origami (Aug 28)
Electric functionality of new origami confirmed!

## Slide 15
First samples from the origami mass production expect for the second half of November

## Slide 16: Other issues to follow-up
Ladder mount procedure
  Decision on the concept at the June B2GM (ladder mount from the side)
  But many details to work out (ladder mount adapter – keep or remove, gluing of FOS fibers and NTC sensors, CO2 pipe attachment, …)
Read-out electronics
  Redesign of the FADC board layout
  Trigger latency issue
    Does the L1 trigger arrive within 5 ms to the APV

## Slide 17: Support structure assembly
CMM measurement of assembled FWD-BWD structure (v1): Inoue-san
  will be done in Sep (after VXD meeting). I will show the data as soon as possible.
Second trial of endring+endflange assembly (v2): Katsuro
  Order of modified jigs for FWD was taken place.
  They will appear the middle of Sep.
  We will try to assemble FWD half endrings in Nov.
Support-rod reproduction: Suzuki-san
  We will employ ETP bushings for the new rod. But they will appear the end of Oct.
    Easy to achieve co-axis and squareness, and easy to adjust position in Z.
  Production: by the begin of Nov.

## Slide 18: Ladder Mount Table
Index plate
  Considering cable routing, optimize index plate and fixation mechanism.
  by Oct. B2GM
3D measurement system
  change the stroke of movable stages.
  by Oct. B2GM
Division of half-structure
  Setup rails on table
  Division test
  Storages of half-structure (Toru)
  by Oct. B2GM
Above tasks are managed by Suzuki-san and Maki-san.
Index Plate
Coordinate
Measurement
System
Division
Tool

## Slide 19: FADC Readout System
TRG/CLK signals
x48 FADC
FADC
Zero supp.
Formatter
PXD region of interest gen
Data stream
belle2link
Aurora link
SVD
x4 buffer
FADC-Ctrl
Cu cable
VME
x1748
APV25s
~2m
Repeater
~10m
SVD readout system
Data size reduction
Trigger/
timing
distributor
FADC Ctrl
APV trig gen
Decoder
Central DAQ
“COPPER” board
TX
RX
CPU
to PXD
to HLT
Central TRG
Prototypes of all components have been developed.

## Slide 21: SVD parallel session agenda Thursday morning

## Slide 22: SVD parallel session agenda Thursday afternoon

## Slide 23: Discussion items at this meeting
Discussion time is foreseen during this meeting for a number of items, both in the plenary and in the parallel
Most pressing item: organization of the March/April 2016 combined testbeam at DESY
  date/schedule
  goals and participating sub-systems
  sub-system contact persons and organization
The idea behind the agenda is to discuss these items first within PXD/SVD separately (Thu) and then have a combined discussion (Fri)

## Slide 24: Summary
The SVD ladder production has started although not all assembly sites have been fully qualified
  L5.001 assembled, surveyed and electrically tested
  The origami pre-production has been successful – first mass production samples are expected for the second half of November
The next challenge will be to fully develop and qualify the ladder mount
At this meeting, we need to clearly define what we expect for the DESY testbeam Mar/Apr 2016 and set up the organisation

## Slide 25: backup

## Slide 26: The Belle II detector
CsI(Tl) EM calorimeter: waveform sampling electronics, pure CsI for endcaps
RPC μ & KL counter: scintillator + Si-PM for end-caps
Time-of-Flight, Aerogel Cherenkov Counter → Time-of-Propagation (barrel), prox. focusing Aerogel RICH (forward)
4 layers DS Si vertex detector → 2 layers PXD (DEPFET) + 4 layers DSSD
Central Drift Chamber: smaller cell size, long lever arm

## Slide 27: SVD schedule
Ladder Production schedule still consistent with a start of ladder mount in April 2016

## Slide 28: VXD ( PXD + SVD ) Schedule
High level milestones | 
First mass production ladder (L4-L6) | Oct. 2015
2nd beam test | Jan.-Feb. 2016
Start of ladder mount to support structure | Apr. 2016
SVD readiness in KEK | Feb. 2017
PXD readiness in KEK | Apr. 2017
PXD+SVD integration | Jun. 2017
PXD+SVD combined cosmic ray test | Jun. 2017
PXD+SVD installation | Apr. 2018
Start of physics run | 4Q 2018