## Slide 1: SVD QCG Report
F.Forti

## Slide 2: Outline
Sites Qualification Reviews
Open issues
https://belle2.cc.kek.jp/~twiki/bin/view/Detector/SVD/SvdQCQAGroup

## Slide 3: Site qualification reviews
Site qualification reviews have proven to be a very effective tool to ensure the quality of modules and improve site to site communication.
Quite active summer of update reviews:
May 29, 2015: Pisa qualification update: http://kds.kek.jp/conferenceDisplay.py?confId=18748
Jun 27, 2015: TIFR qualification update: http://kds.kek.jp/conferenceTimeTable.py?confId=18750
Jul 27, 2015: IPMU qualitication update: http://kds.kek.jp/conferenceDisplay.py?confId=19223
Aug 06, 2015: HEPHY qualification update: http://kds.kek.jp/conferenceDisplay.py?confId=18752
Aug 21, 2015: Melbourne qualification update: https://kds.kek.jp/indico/event/19357/
All reports are on the QCG site: https://belle2.cc.kek.jp/~twiki/bin/view/Detector/SVD/SvdQCQAGroup

## Slide 4: Review types
Some naming:
  (PCCQ) Preliminary class C qualification = review of production procedures, but without a fully qualified and satisfactory class C module
  (CCQ) Class C qualification = review a full class C module and authorize production of class B modules
  (CBQ) Class B qualification = review a full class B module, and authorize start of mass production with class A modules
  (CAM) Class A monitoring = regularly review the production quality of class A modules, especially at the beginning of mass production

## Slide 5: Site Qualification current situation (I)
Pisa (SFW-SBW)
  Completed full CBQ qualification on May29  Authorized for class A production
  Need to setup the class A monitoring reviews.
Melbourne (L3)
  DONE: CCQ (21 August 2015): very good progress and minor issues identified.
  Email exchange on-going to finalize issue and start class B production
  TODO: CBQ should be held after the first full class B
TIFR (L4)
  DONE: CCQ (27 June 2015)
    Main issue: shift of the forward assembly, due to vacuum leak accident
    Documentation and DB usage
  The first class B was produced, but has some issues:
    Shift of the forward assembly  probably understood
    Electrical problems in APV readout  needs debugging
  Need to resolve the issue before proceeding.
  TODO: CBQ should be held when a good class B is produced

## Slide 6: Site Qualification Current Situation (II)
HEPHY (L5)
  DONE: CBQ (6 August 2015)  Authorized for class A production
  Fully functional class B module produced
  Very good mechanical accuracy achieved: < 100um shifts
  TODO: Setup class A monitoring reviews
IPMU (L6)
  DONE: CCQ (27 July 2015)
  A class B module had also been produced
  Main issue: shift of the forward assembly  probably understood
    CMM inspection accident  understood
  Procedures should be corrected and one class C should be produced
  Verification of the class C accuracy before next class B construction
  TODO: CBQ should be held after a good class B is produced.

## Slide 7: Shift of forward assembly
Very short PA can carry large forces  do not move hybrid after clamping
Can move several mm’s even vacuum chucking.

## Slide 8: QCG Open issues
Ladder design
  Definition of ladder mechanical tolerances
    L5 shown 100um is possible. Probably too tight.
    Proposal: 100um in xy, 300um in z ? Needs decision
  Verification of thermal (-30 to +60 C) and mechanical properties on ladders (deformations and vibrations)
    Tests performed, analysis to be finalized; no major problem.
  Verification of possible ladders mechanical interference on rings
    Planned for october B2GM

## Slide 9: QCG Open issues
Ladder assembly procedures
  Clear definition of all coordinate systems and survey points
    Done. Need finalization for L3 https://docs.google.com/spreadsheets/d/1_YVu501StrxXufcWm0qn6wgAOasZ15F8WG03tc8utLY/edit?usp=sharing
  Finalization of some assembly procedure details
    Correction of the Shift in the forward assembly to be fully verified
  Streamline the database usage for production checklist and measurements storage and comparison
  Definition of the ladder transport container
  Detailed definition of production ladder thermal tests
    Ideas proposed, but need to be finalized
  Detailed definition of electrical QA during production
    aDefectFinder is the standard tools

## Slide 10: Common comments
The reporting format for the ladder measurements should be standardized for ease of comparison. A uniformly structured spreadsheet should be used
All sites should use the standardized defect finder (aDefectFinder), maybe tuning the cuts for the specifics of the site.
The wire-bonding should be done in full, with a careful visual inspection of each step, but with electrical test only at the end of the wire bonding and prior to gluing.
Modules should be repeatedly inspected throughout the assembly steps to make sure no damage or significant displacements are happening. Pictures should be taken at all steps to document the inspection.
Perform redundant wire bonds for the bias lines.
Common procedures to cut the AIREX should be clarified and finalized, taking into account the needed accuracy for the optical fiber placement and the existing PB2 groove.
Common procedures to glue the SILPAD to the Kokeshi-pin should be clarified and finalized.
The ground wire for the origami needs to be applied by the assembly sites prior to gluing the H-shapes together. The length of the wire should be clearly specified
The electrical functionality of O-Z, OCE, O+Z and SBW and SFW should be verified prior to their usage.
Incoming inspection and tests of received components should be part of the workflow.

## Slide 11: QCG Next Steps
Conclude specification documents signoff (Origami/ H-C Shape)
Conclude sites initial qualification
Set up proper quality monitoring of ladder production
  Collect statistics on production quality
  Spot problems and possibly trigger adjustments of procedures
Start worrying about ladder mount requirements and procedure review

## Slide 12: Communication !
Great progress in communication. Still, communication is difficult and we should apply extra care in making sure we understand each other
  Use good communication equipment for phone meetings !
  Write down conclusions in a clear way !
  Stick to the accepted conclusions, or communicate if we need to change something.
Timid man overboard