## Slide 1: DCD submitted
Conservative version
As now with the following changes: larger LVDS bias current, in ADC layout added dummy structures, antenna diodes
Main version 1
Changed sampling TCK edge
Parallel sampling mode for probe tests at full speed via JTAG, needle pads
Programmable LVDS current (2 levels)
Programmable RefLVDS (2 levels, normal and by ~30mV increased)
Defined power up sequence – VDDD should be turned on as first
Separated bias DACs for up and down (for better LSB uniformity)
IPDAC resized
Gain settings redone
In ADC layout added dummy structures, antenna diodes
Main version 2
As version 1 with larger ADC transistors and uniform orientation for better matching and less missing codes
Main version 3
As version 2 with new digital block – ID-code changed to one with LSB=1, added digital test patterns as proposed by Florian

## Slide 2: DCD submitted
New type
As version 3 with capacitive SAR ADC
Also submitted – wire bond bump bond adapter for standalone DCD tests
Test plan
Use the same PCB design as in Heidelberg with the following redesign: add multiplexer for 64 -> 32 inputs
Three needle “ring” types
Type 1 – for 64++ bump array
Type 2 – for 16 inline bumps + power – JTAG tests – DCD4: tested everything except IO-pads (compatible with present DCD4, the PCB can be used without redesign)
(In the case of new DCD5 also IO pads are tested when type 2 needle ring is used)
Type 3 – for ~20 inline needle pads + power – tested everything – for later tests on wafers

## Slide 3: DCD submission plan (Seeon)
Changes in design (present status):
Change sampling of TDI for global and pixel register to positive edge done
Add fast parallel sampling mode for easier needle card tests (maybe) done
Improve test DAC resolution by adding additional DAC not needed (not done)
Programmable LVDS output current (or just larger) done
Check protection diodes should be on VDDD for digital (done)
Investigate power up problem (mon) (done)
Add transmission switch to monitor (now only PMOS) (not done)
Check the voltage drop on power rail – connect gate of the NMOS sources only in one point done
Reduce RefIn current not needed
Try to connect DAC Dump and SF VDDA to RefIn too complicated (not done)
Separated bias DACs for up and down bias done done
Spare ADCs too complicated not done
Redo protection diode, current drain/split nwell (add PMOS) (left as it is)
Ipdac 60uAfull range (done)
SubIn 4 times or additional DAC not needed? (not done)
Introduce 15k Feedback resistor setting – low gain mode done (done)
Variable digital test patterns done in one version