## Slide 1: DHPT Timing Reference
T. Hemperek

## Slide 2: Synchronization
different startup conditions

## Slide 3: Consequnces
  The acceptance window for recognizing correctly the commands is ~3ns comparing to 12ns before
  The sampling point can change after power up between the chips by ~9ns
    -> requires tuning after every power-up
    This is present since DHP01(2010)

## Slide 4: Design solution
SYNC
Solution (easiest?): Provide GCK based synchronization (SYNC) to the divider
Consequences:
- redo the digital part + better PLL characterization (for SYNC) - it will take time (at the moment I do not know how much will investigate this)
- there is a limited risk something goes wrong

## Slide 5: Other solutions
PROGRAM.
DELAY
SYNC
Does not require changing/charactering PLL
Possibly need some calibration once (like DCD delays) to avoid hold/setup problems since the relationship between GCK and CLK_DES is unknown at this point

## Slide 6: Other solutions
  The acceptance window for recognizing correctly the commands is ~3ns comparing to 12ns before
  Does not require changing/charactering PLL