## Slide 1: Detector Housing: Simulation and Design
Ibrahym Dourki
12.05.2016
Ibrahym Dourki, PhD Student
Max Planck Institute for Structure and Dynamics of Matter, Center for Free Electron Laser Science (CFEL) Luruper Chausee 149 D-22761 Hamburg (Germany)
20th International Workshop on DEPFET Detectors and Applications
11-14 May 2016, Kloster Seeon ( Tagungsraum )

## Slide 2: Outline
Sensor Thickness and Support
Detector Housing Simulation
Mechanical Design of Detector
Spatial Resolution: MTF Calculation
Motivation

## Slide 3
Motivation
Supporting the detector sensitive area:
Provides high mechanical stability for the detector (robustness)
Is needed to integrate an efficient cooling system
BUT!
Support layer increases the noise signal produced by backscattered electrons and thus degrades the detector performance.
A concept of the new design is presented by taking into account the thermo- and mechanical stability of the detector without degrading the detector performance.
Monte Carlo Simulation is used to optimize the detector geometry

## Slide 4
Radiation Source: Electron beam of Ee=300 keV normally incident on the Silicon layer
Thickness of Silicon layer: 50 µm thick
Simulation of 1 mm x 1 mm x 50 um Si layer with Geant4
Sensor Thickness and Support

## Slide 5: Signal Versus Thickness and Energy
50µm Si sensitive layer has high DQE and can detect a single electron

## Slide 6: Signal Distribution: Landau Distribution
e-hole pairs
Counts
https://fr.wikipedia.org/wiki/Lev_Landau
Lev Davidovich Landau 22.01.1908-1.04.1968
Nobel Prize: 1962
- Asymmetric distribution  MPVMV
Long tail extending to high values: Originatingfrom high energy transfer
Most interactions involve little energy deposition
Theory: MPVtheo = 4600 e- Simulation: MPVs = 4824 e-

## Slide 7: Electron Backscattering Investigation
An example of detector beeing simulated
Support layer is needed:
Cooling
Mechnanical stability

## Slide 8
Simulation of the tracks of 500 electrons
of 300 keV in the detector layers.
For 50 µm Si and Ee=300 keV  only 10 % of the electron energy is deposited
Signal generated by backscattered electrons must be reduced as low as possible
Qualitative description of electron backscattering
MV= 265.73 keV
MPV=276.35 keV

## Slide 9
Effet of the backscattering on the signal quality

## Slide 10
Introducing a gap allows to direct the scattered electrons away from the sensitive layer
Substantial improvement in the detector performance.
Detector Optimization: Vacuum Gap

## Slide 11
Black tracks label backscattered and secondary electrons emitted from the support layer.
Vacuum gap between sensitive silicon area and Si support
20 mm vacuum gap
Simulation of the tracks of 500 electrons of 300 keV in the detector layers

## Slide 12
16% noise at 20 mm gap

## Slide 13
Coating the Detector Geometry with Low Z Material
20 mm vacuum gap + extra cavity : Detector stabitiy

## Slide 14
Entrance layers
50 µm sensitive Si layer
900 µm Si
20 mm gap
200 µm Carbon layer
60 µm
140 µm (600 µm)
2.5 mm Si
4.02 mm Si
450 µm
2.5 mm
340 µm
2.02 mm
500 µm
2.5 mm Si
4.02 mm Si
3 mm Si
Extra Cavity (15 mm)
Cross Section of Almost Final Detector Geometry
Notes: 140 µm insensitive layer must be optimized

## Slide 15
Without gap and without coating: ≃ 58 % noise caused by BSE
With vacuum gap and carbon coating: only ≃ 4.2 % noise
≃13 %
≃4.2 %

## Slide 16: Spatial Resolution: MTF Calculation
Modulation Transfer Function (MTF) measures how well a detector is able to transfer signals of various frequencies from the input to the output.
Slanted edge method is used to calculate the MTF
Input Signal: Sin
Output Signal: Sout
1 lp/mm
Object A
10 lp/mm
Object C
Detector
1 lp/mm
Object A
MTF=90 %
3 lp/mm
Object B
10 lp/mm
Object C
MTF=0 %
3 lp/mm
Object B
MTF=50 %

## Slide 18
Example: Imaging of gold and carbon rings (2 line pairs per mm (2lp/mm)
Electron source
FDD
FOD
Object
Magnification:
M=FDD/FOD
Resolution in TEM:
R=pixel size/M
For M=12000 and FOD=20 µm
FDD=240 mm
Width=20.8 nm
Thickness= 2 µm
SF=2lp/mm
2 µm
Gold rings
Cross sectional view
of gold rings
20.8 nm
Detector

## Slide 19
Gold
Carbon
Less electrons reaching the detector

## Slide 20
Gold
Carbon
More electrons reaching the detector

## Slide 21
Mechanical Design of Detector
CAD design (Djordje Gitaric)
very compact design
170 mm
150 mm
Wide and short flex leeds
Cooling plate
PCB inter-
connects
e-
Cavity
Cryo liquid cooling > -40°C
Colling
channels
Poly-Si block
shielding

## Slide 22
HLL ► Ladislaw Andricek ● Martin Hensel ● Christian Koffmane ● Jelena Ninkovic ● Gerhard Schaller ● Martina Schnecke ● Florian Schopper ● Andreas Wassatsch ● Christian Zirr
KIT ► Ivan Peric
USI ► Klaus Gärtner
MPSD ► Ibrahym Dourki ● Sascha Epp ● R. J. Dwayne Miller ● Fabian Westermeier
● Djordje Gitaric
EDET Team: Acknowlegements

## Slide 23
Summary
Detailed detector simulation studies were perfomed.
A new detector design has been developed
The unwanted signal generated by backscatering in the sensitive
layer is reduced by a factor of 13.
The detailed engineering design has just started

## Slide 24
Thank you for your attention