## Slide 1: DePFET Development for the ATHENA Wide Field Imager
P. Lechner, R. Lehmann, J. Ninkovic,
R. Richter, G. Schaller, J. Treis
MPG Halbleiterlabor
A. Bähr, N. Meidinger, J. Müller-Seidlitz,
W. Treberspurg
MPI für extraterrestrische Physik
20th International Workshop on DEPFET Detectors and Applications, Kloster Seeon, 12.05.2016

## Slide 2: ATHENA Mission (Advanced Telescope for High ENergy Astrophysics)
ESA mission
  next large X-ray observatory
  ESA's Cosmic Vision 2015–25 plan
  2nd of three L-class missions
science targets
  theme 'The Hot & Energetic Universe'
    formation of large scale structures
    evolution of black holes
scenario
  launch ~ 2028
  Ariane 5 carrier
  halo orbit around Lagrange point L2
  design life time 5 y (+5 y)
  300 observations per year
status
  phase A (feasibilty study)
ATHENA spacecraft
artist's impression, ESA

## Slide 3: Spacecraft
optics module
  Wolter-I Si pore optics
  effective area 2 m² @ 1 keV
  field of view 40 arcmin
  angular resolution 5 arcsec HEW
  focal length 12 m
instrument module
  moveable platform
  X-ray Integral Field Unit (X-IFU)
    cryogenic transition edge sensor
    highest resolution (2.5 eV @ 6 keV)
    field of view 5 arcmin
    pixels 3840 x (250 µm )
    energy range 0.3 … 10 keV
    temperature < 100 mK
  Wide Field Imager (WFI)
X-IFU
WFI

## Slide 4: ATHENA Wide Field Imager
  rate capability (1 Crab*)
  throughput > 90 %
  pile-up < 1 %
  time resolution
X-ray imaging spectrometer with spectral, position and time resolution
science drivers
specifications
WFI parameters
  point source
  sensitivity
  angular resolution
  ≤ 5 arcsec
  < 0.3 mm
  pixel size
  130 µm 
  survey power
  format
  1024 x 1024 pixels
  14 x 14 cm²
  row / frame time
  ≤ 10 µsec / 5 msec
  field of view
  ≥ 40 arcmin
  ≥ 14 cm Ø
  pile-up limit
combination of
large-area detector
high-rate detector
  line spectroscopy
  energy resolution
  150 keV @ 6 keV
  low electronic noise
  ≤ 10 el. ENC
  quantum
  efficiency
  energy range
  0.1 … 15 keV
  thin entrance window
  thickness 450 µm
  light-curve of bright
  point sources
  transients
  position out of focus
  ~ 35 mm
  4 mm PSF
  frame time
  ≤ 80 µsec
* 1 Crab ≈ 105 cps

## Slide 5: Large Area Detector

## Slide 6: DePFET
Depleted P-channel
Field Effect Transistor
principle
  p-FET on depleted n-bulk
  signal charge collected in potential minimum below FET channel
  transistor current modulation (~ 300 pA/el.)
  unit cell of an Active Pixel Sensor
  X-ray imaging spectroscopy
combined function of sensor & amplifier
  low capacitance (20 fF) and noise
  signal = full – empty internal gate
  charge storage capability
  non-destructive readout
  backside illuminated, fully depleted
DePFET readout sequence
DePFET equivalent circuit
Depleted P-channel Field Effect Transistor

## Slide 7: DePFET
Depleted P-channel
Field Effect Transistor
3D device simulation (POSEIDON)
  integration  DePFET current off
  readout  DePFET current on
  reset  clear structure active
matrix organisation
  common bulk & back contact
   thin homogeneous entrance window
   fill factor 100 %
  row connection of gate, clear, cleargate
  column connection of r/o nodes (drain/source)
   individually addressable pixels
   windowing option
rolling shutter operation
  one active row
  all other pixels turned off
   minimum power consumption
  column parallel processing
Depleted P-channel Field Effect Transistor

## Slide 8: Focal Plane
4 independent & identical quadrants
  format 4 x 512 x 512
  pixel size 130 µm 
  sensitive area 4 x (6.7 cm)²
  two-side buttable DePFET-APS
  front-end electronics
    new SWITCHER-A (3 ports/channel)
    VERITAS readout ASIC
  thermal decoupling
    DePFET @ -60 … -80 °C
    front-end @ -20 °C
  support structure  ~ 7 mm insensitive gap
observation mode
  gap compensation
  Lissajous dithering pattern
    5 arcmin amplitude
    simulation by MPE

## Slide 9: XEUS & IXO Wide Field Imager Prototypes
prototype test
  format 256 x 256 pixels
  area 1.92 x 1.92 cm²
  pixel 75 µm 
  readout 6 µsec / row
  1.5 msec /frame
  temp -5 °C (!)
  resolution 127 eV (singles)
    140 eV (all)
  σ (gain, noise, offset) ~ %
Depleted P-channel
Field Effect Transistor
shadow image,
measurement by
Aline Meuris

## Slide 10: BepiColombo MIXS
Macro Pixel Sensor
  DePFET + Si Drift Detector
  area 1.92 x 1.92 cm²
  pixel 300 µm 
  split frame readout
  source follower (ASTEROID)
  2 instruments:
    MIXS-C (Collimator)
     wide field (5°)
    MIXS-T (Telescope)
     precision mapping < 500 m
status
  fully space qualified
  spacecraft integration
  jan17 launch
  jan24 Mercury orbit
  mission lifetime 1 (+ 1) year
Depleted P-channel
Field Effect Transistor
Mercury Imaging X-ray Spectrometer
300 µm
1.92 cm
MIXS sensor die
microphotograph of pixel structure
planetary orbiter in electromagnetic test facility @ ESTEC

## Slide 11: 1st Prototype Production
2 objectives
  operation of large-scale pixel detectors
   formats representative for flight devices
   homogeneity over large area
   effect of long signal and supply lines
  DePFET evolution
  64 x 64 test vehicle
     variations in layout
     variations in technology
     variations in readout
full width
512 x 64
full height
128 x 512
quarter
256 x 256
prototype
64 x 64

## Slide 12: Layout Variation
  gate shape
  circular, closed
   standard spectroscopy device so far
   compact design, minimum polySi1/2 overlap
   gate geometry not scalable
   long clear time
  50/50 share of both versions
  many flavours with modified details, based on 64 x 64 format
  linear, open
   small gate dimensions possible
   efficient double-sided clear
   less experience in spectroscopy
     complex on-chip wiring

## Slide 13: Layout Variation
  DePFET with internal storage (InfiniPix)
  design similarity to linear gate DePFET
  measured performance
  32 x 32 prototype matrix
  energy resolution (FWHM @ 5.9 keV)
    124 eV (single pixel events)
    128 eV (all valid patterns)
  peak / background ratio
    6500
A. Bähr
measurement by
J. Müller-Seidlitz / MPE

## Slide 14: Technology Variation
   convenient process technology
  all implantations self-aligned w.r.t. polySi
   freedom in choice of operation parameters
   radiation hardness
  gate oxide thickness
   heritage, standard so far
    XEUS, Simbol-X, IXO, BepiColombo MIXS
   amplification
    according to basic DePFET model
    confirmed by experiment
  50/50 share of wafers
e.g. Nordstrom & Gibbon, 1981
thick gate oxide
thin gate oxide ~ 50 %

## Slide 15: Readout Modes
VERITAS readout ASIC  2 input stages
  source follower
  standard so far
  charging of line stray capacitance
   long time constants (~ µsec),
  especially for large area devices
  drain current readout
  commmon operation voltage
   requires homogeneity of DePFETs
  favorised, but insufficient experience
   50/50 split of 1st production
C_stray

## Slide 16: 1st Production Status
production start may15
today
to do
  2nd metal layer top side
  metal layers back side
  passivation
  wafer level test
  dicing
estimated time of arrival sep16
pre-flight production mid17
 final format 512 x 512
microphotographs
of ATHENA DePFET
pixels
round gate
linear gate

## Slide 17: Entrance Window
tradeoff
quantum efficiency
vs.
  optical & UV stray light
  transmittance ≤ 1.e-6 @ 100 nm Al

## Slide 18: High Rate Detector

## Slide 19: Option1: IXO HTRS
multi-channel Si Drift Detector
  format 31 cells
  overall area 4.5 cm², 24 mm Ø
  out-of-focus distance 11.3 cm
predicted performance
  time resolution 10 µsec
  energy resolution 150 eV (BoL)
  300 eV (EoL)
  count rate capability > 10 Crab (170 kcts/sec)
  deadtime & pile-up < 2 % @ 1 Crab
system development
  self-triggering analog readout ASIC SFERA
  (Politecnico di Milano & XGLab)
  alternative digital filtering system
  (CESR Toulouse)
  detector board
  DAQ system
  mechanical/thermal concept
readout side
radiation entrance
window side
High Time Resolution Spectrometer

## Slide 20: Option2: Full Frame Readout APS
full frame readout
  1 amplifier channel / pixel
  large hexagonal pixels, e.g.
  800 µm / 127 cells
  560 µm / 253 cells
  two/four VERITAS readout ASICs
  WFI electronics box
  no SWITCHER
DePFET with internal storage
  2 DePFETs / pixel
  one collecting charge / other in readout mode
  elimination of 'out-of-time' events
127
cells
253
cells
A. Bähr

## Slide 21: Option3: Split Frame Readout APS
'small large-area' WFI detector
  format 64 x 64
  pixel size 130 µm
  split frame readout
   two 64 x 32 'hemispheres'
   two (half) SWITCHER control ASICs
   two readout ASICs
   frame time 32 x 2.5 µsec = 80 µsec
  option:two-row parallel readout
   additional speed-up
   four readout ASICs
no specific production for high-rate detector
  maximum of synergy with large WFI
64 x 64 APS
split frame readout
64 x 64 APS
two-row parallel
split frame readout

## Slide 22: Summary
large-area WFI detector
  samples of 1st production available in summer 16
  large-scale devices
  variations in layout, technology & readout mode
high-rate WFI detector
  no specific activity
  in parallel with large detector development