## Slide 1: Characterization of Pilot Run Modules for the Belle II Pixel Detector
Felix Müller
Max-Planck-Institut für Physik
IMPRS Young Scientist Workshop
Ringberg Castle 2016, June 7, 2016

## Slide 2: Belle II Vertex Detector
Silicon Vertex Detector (SVD)
4 layers of double sided silicon strip detector
R= 3.8 cm, 8.0 cm, 11.5 cm, 14 cm
Pixel Detector (PXD)
2 layers of DEPFET pixels
R = 1.4 cm, 2.2 cm
Beam pipe: R=10mm

## Slide 3: Belle II – PXD Requirements
Occupancy | ~ 1 %
Frame time | 20 µs (rolling shutter mode)
Momentum range | Low momentum (Pt > 50 MeV/c)
Acceptance | 17°-150°
Radiation | ~20 kGy/year, 11010 n/ab-1cm²
Belle II is dominated by low momentum tracks (<P> = 500 MeV/c)
Modest intrinsic resolution (15 μm), dominated by multiple scattering → Moderate pixel size (50 x 75 μm²)
Lowest possible material budget (0.2% X0/layer) [including ASICs]
Increase of background by factor 20-40: irreducible background by 2-photon QED process: Needs to cope with radiation damage, occupancy, fake hits and pile-up noise
100x higher trigger rate (30 kHz) compared to Belle
Silicon strip detector (SVD) close to beam pipe
excluded (too large occupancy): replace by PXD

## Slide 4: DEPFET (DEPleted p-channel Field Effect Transistor)
impinging
particle
Clear
Turn on DEPFET
source
Gate

## Slide 5: DEPFET (DEPleted p-channel Field Effect Transistor)
Clear
A DEPFET is a MOSFET onto a sideward depleted silicon bulk
→ Low noise
→ Low power
→ High signal/noise-ratio
→ Non-destructive readout
internal amplification:
gq  0.5 nA/e-
90 steps fabrication process
9 Implantations
19 Lithographies
2 Polysilicon layers
2 Aluminum layers
1 Copper layer
Back side processing

## Slide 6: Control and readout electronics
SWITCHER
Fast voltage pulses up to 20 V
64 outputs gate and clear
192 electrical rows (6 per module)
Drain Current Digitizer (DCD)
8 bit ADCs
Compensates for pedestal variation
256 input channels (4 per module)
Kapton Flex cable
Power Supply
Data transmission
4 layers, 48 cm
DEPFET
768x250 pixel x 2
Data Handling Processor (DHP)
Pedestal correction
Common mode correction
Data reduction (triggered readout and zero suppression)
Control of DCDs and Switcher
Pixel i,j,v

## Slide 7: Additional steps in module production (1)
From Semiconductor Laboratory:
Silicon:
All implants
Metallization routings
Thinned to 75 µm
Missing:
Assembly of (control and readout) ASICs (@IZM, Berlin)
Assembly of passives (SMD components) (@ Semiconductor Laboratory)
Attachment of Kapton flex (data and power connection) (@ MPP)
End-on gluing of two modules to a self-supporting ladder (@ MPP)

## Slide 8
Additional steps in module production (2)
DEPFETs
Switcher
SMD
DCD
Drain
Current
Digitizer
DHP
Data
Handling
Processor
Sensitive areas:
inner layer: ~ 45 x 13 mm²
outer layer: ~ 61 x 13 mm²
Module sizes:
inner layer: ~ 70 x 15 mm²
outer layer: ~ 85 x 15 mm²
thinned area (75 µm)

## Slide 9: PXD9 Pilot Run
Drain
Current
Digitizer
Data
Handling
Processor
768 x 250 = 192.000
DEPFETs
Switcher
Current
Capacitors & Resistors
SMD 01005, 0201, 0402
careful handling of sensor required, protected by special jig (grounding, cooling, electrical insulation)

## Slide 10: PXD9 – W30-OB1 – Pedestals

## Slide 11: PXD9 – W30-OB1 – Noise
µ=0.60 ADU
µ=0.63 ADU
µ=0.59 ADU
µ=0.60 ADU

## Slide 12: PXD9 – W30-OB1 – Laser scan
Laser signal ~2-4mip, read out at full speed with a noise of ~1.8 ADU (laser instability and system noise)
~105 ns/row, of which ~26ns are used for clear pulse (8 ticks of 32)

## Slide 13: PXD9 – W30-1 – Clear behavior
OB
Consecutive frames are readout
Timing of the laser set to have one laser pulse within 4 frames
Threshold of zero suppression is set to 5 ADU
Laser spot
91ADU

## Slide 14: PXD9 – W30-OB1 – Source Measurement

## Slide 15: TestBeam April 2016 @ DESY (1)
66 registrants from 10 countries for beam test in April 16 at DESY
Complete system integration test (2 layers PXD, 4 layers SVD)
Layer 2
Layer 1
Cool block
(CO2 pipes)

## Slide 16: Test Beam April 2016 @ DESY (2)
1 T solenoid
6 GeV electrons
6 layers telescope,
4 layers SVD,
2 layers PXD
e-
SVD
PXD
e-

## Slide 17: Preliminary TestBeam Analysis – Layer1 Module

## Slide 18: Summary and Outlook
To fully exploit the high luminosity provided by SuperKEKB, a pixel detector close to the beam pipe is mandatory for the precise vertex reconstruction
PXD: Excellent spatial resolution of ~ 15 mm; occupancy ~ 1%, fast readout (50 kHz frame rate), huge number of pixels (~ 8 Mpix) => fits all the requirements for Belle II
Complex DEPFET technology; fully functional; successful demonstration in lab and beam tests
Thinning of sensitive area down to 50µm / 75 mm (0.2% X0), minimizing multiple scattering;
Low power consumption ~ 18 W per ladder
ASICs and Sensors close to final version
Signal to Noise: ~ 40 (including noise from ASICs)
Many aspects not covered in this talk; though in development by the Collaboration
Shows a good clear performance over the entire sensitive area
Shows spectrum of all 24 DCD/Switcher regions with reduced speed
Outlook:
  Optimization of ASIC settings & Supply voltages
  Analysis of beam test data during the next weeks
  Further detector characterization & optimization

## Slide 19: Radiation Tolerance
R&D since 2008:
Reduce tox
Optimize gate dielectric layer
Vt(10Mrad): ~15V  3 V
The remaining small threshold
voltage shift can easily be
compensated by a shift of
the operating voltages
of the DEPFET!
 Safe operation for about 10 years in Belle II

## Slide 20: Radiation Tolerance
Gate Dielectrics: ~ 200nm
Radiation field at Belle II dominated by ~MeV electrons/positrons from QED beam background
Ionizing Radiation - Total Ionizing Dose (TID)
(~2Mrad/a at Belle II)
Positive fixed oxide positive charge  ∆VT
interface trap density 
  reduced mobility (gm)
  higher 1/f noise
Non Ionizing Energy Loss (NIEL)
(1012 neq/cm²/year at Belle II)
Leakage current increase  shot noise
Trapping not considered to be critical
Type inversion expected after 1014 neq/cm²

## Slide 21: Time dependent measurements of CP violation
(Belle: ~200µm)
Y(4S) is the first resonance just above the BB production threshold
Only BB pairs are produced, and are quasi at rest in the Y(4S) frame