## Slide 1: SVD Slow Control Overview and Network
10th VXD Workshop, Santander, Spain

## Slide 2: Introduction
Overview about SVD SC system
Names and purpose of subsystems and IOCs
First draft of network and server configurations
  Intended as starting point for discussion
Manpower

## Slide 3: SVD Slow Control System Overview

## Slide 4: FADC related IOCs (1)
FADC CTRL:
  IOC to configure and control FADC and FADC-Ctrl boards
  HW interfaces:
    CAEN VME controller
    High speed Ethernet to FADC spydaq network
SVDQM:
  Low level quality monitoring (down to APV level)
  Analysis of local run data
    Requires high processing power
    Where to store data  local? KEKCC?
  HW interface: none
  Receives FADC spy data via dedicated local socket
Strongly coupled IOCs  can run on same server

## Slide 5: FADC related IOCs (2)
FADC CM:
  FADC crate monitoring (CM)
  Voltages, currents, fan speed, temperatures, etc.
  Protocol: SMP
  HW interface: Ethernet
SVD CTRL:
  Interface to Belle II RC
  Controls SVD state machine
  HW interface: Ethernet (EPICS)
Can share server with FADC Ctrl and SVDQM

## Slide 6: Power Supply IOCs
SVD_PS:
  To configure and control of CAEN power supplies
  Monitoring of voltages and currents
  Implementation of Belle II PS state machine
  CAEN PS crate monitoring
  HW interface: Ethernet, anything else?
SVD_PSPP:
  IOC to configure and control PS patch panels
  Vsep polarity inversion
  Further “intelligent” functionality?
  HW interface: Ethernet?
Ethernet only?  Can run on any IOC server
Could share server with environmental monitoring system

## Slide 7: Environmental Monitoring IOCs (1)
NTC:
  NTC sensors IOC
  Dedicated interface board required for server?
  HW interface: CANbus, Ethernet?
FOS:
  Fiber optics sensor (FOS) IOC
  Same system as PXD but dedicated HW
  Common IOC with PXD?
  HW interface: Ethernet?

## Slide 8: Environmental Monitoring IOCs (2)
HUM:
  Humidity monitoring
  Common VXD system
  HW interface: Ethernet? / other?
RAD:
  Radiation monitoring, diamonds
  Common VXD system
  HW interface: Ethernet? / other?

## Slide 9: Other IOCs / Systems
SVD CA gw
  Separates belle2epics and SVD epics
  Reduce the amount of process variables (PVs) transmitted to belle2epics
  Do we need this CA gateway or can we just connect the two epics networks?
  If yes, which process variables (PVs) shall be forwarded to belle2epics?
SVD archiver
  Archiver for all relevant SVD PVs
  Can we use the same archiver as PXD?
    Answer from M. Ritzert: rather no
    If yes, do we need to connect pxd epics with svd epics?
    Directly or via CA gateway?

## Slide 10: Databases
Need to interface with several databases
  Configuration DB
  Condition DB
  Archiver
  Error and alarm logging
  other?
At the moment nobody concentrates on this!
Currently we use XML files for configuration

## Slide 11: Responsibilities and Manpower
Number of person working on SC is low
  Hao Yin
    SVD CTRL, FADC CTRL, SVDQM, FADC CM
    incl. CSS for these modules
    Good progress since beam test  see Hao’s presentation
  Szymon Bacher
    SVD_PS, NTC
    HUM?, RAD?, SVD_PSPP?
    Not so much progress since test beam
  Christian Irmler (partly ~10%, still busy with ladder assembly)
    SC group management
    Server and Network configuration

## Slide 12: Poorly Covered Tasks
The following tasks and subsystems are not or just poorly covered
FOS
  Same system as PXD, but can we also share IOC?
  Suppose we can use same IOC, but should run on SVD server
  Need to implement SVD specific CSS
Coordination of SC activities  SC group management
  So far, partly done by myself
  Will be busy with L5 assembly until summer 2017
Databases, archiver, gateways, system and network architecture

## Slide 13: Network Configuration (Draft)
First draft, assuming that IOCs are distributed among 2 servers
  One for FADC related IOCs and a second for the rest (PS, environment, etc.)
To be discussed
Remote connection to our machines via bdaq and access gateway

## Slide 14: SVD Networks
svd epics
  Local SVD EPICS network  all SVD PVs
  Connection to b2epics: directly or via CA gateway?
  Dedicated server or VM for CA gateway?
svd management
  Remote access to our servers and devices
  Used for management and configuration purposes (ssh)
FADC spydaq
  High speed network for GB links of FADC boards
  Two switches at each FADC rack (FW and BW)
  Several optical links between switches and E-hut
  DAQ network for local runs and spy data

## Slide 15: Belle II Networks
bdaq
  Belle 2 DAQ network
  Used to access DAQ servers
  Remote connection to our machines via bdaq?
b2epis
  Belle 2 epics network
  How to connect?
  Directly or via CA GW?

## Slide 16: SVD SC/RC Computing HW
How many servers do we need?
  Need to ensure failsafe operation over several years
So far we have purchased 1 server for FADC system
  Is this sufficient?  Not yet clear.
Need to define computing infrastructure
Can / shall we use virtualization
  Dedicated VM for each IOC or group of IOCs
  Ideal for IOCs, which do not require special HW interface
  Allows to implement nice load balancing and error handling, e.g. if one server fails another can take over IOCs
  Need to verify compatibility with HW interfaces
  Probably requires to duplicate some HW interfaces

## Slide 17: Summary
Number and tasks of SVD SC sub-systems well defined
Manpower is marginal
  Some tasks are not well covered, e.g. databases, management
  Need to define / assign work packages and schedule
Computing and network infrastructure
  First ideas exist, but nothing decided
  Many questions open?