## Slide 1
Overview
MPI for Physics: 100 Year Anniversary
Detector and Technology Developments for Particle Physics (and beyond)
(or: Excellent Science needs Excellent Scientists + Excellent Detectors)
  Introduction
  HYBUC: the hyperon bubble chamber
  Fixed-target spectrometer experiments
  Large volume tracking detectors: TPC
  Liquid argon calorimetry and associated electronics
  Solid state detectors for particle physics and X-ray astronomy
  Photo detectors and Cherenkov telescopes for TeV photon astronomy
  GERDA: neutrino-less double -decay
  Summary
In this talk
- I look back on some of the beautiful detectors developed and built at the MPI-Physik for astro particle- and particle physics, and on the experiments in which they were used.
- These developments have allowed the MPI-Physik to play a lead role in many experiments, which have shaped and are shaping particle and astro-particle physics.
- These developments also found applications in other science fields and commercial products.

## Slide 2
Introduction
Precision measurements, Max Planck and the beginning of Quantum Mechanics
  ~ 1880: Street and home lightning by gas and electricity  need for a standard light normal
  Physikalisch-Technische Reichsanstalt Development of black body + bolometers
  Oct. 1900 Rubens + Kurlbaum + others: Precision results of black-body spectrum  conflict with theoretical predictions
  Max Planck 14. Dec. 1900: “Akt der Verzweiflung”
  MPI-Physik: Innovative detectors  excellent experiments  original theoretical ideas

## Slide 3
HYBUC: Hyperon bubble chamber - MPI-München, Vanderbilt-University (1970-1973)
HYBUC – dedicated hyperon bubble chamber
Physics: magnetic moment mS of S+ (uus)  does simple quark-model describe structure of baryons ?
Method: K- p  p- + S+ (↑)  p p0 S+ precesses in B-field; decay (10-10 s) measures mS
Challenges: 11.5 Tesla field ! high statistics: (2 Mio. pictures  70 000 S+-decays)
Results: 10 physics publications
Highlight: mS = (2.30 ± 0.14) mN: an impressive early confirmation of the simple quark model and a very beautiful experiment !
the „typical“ event
S+
K-
p-
p

## Slide 4
Albert Einstein: 1st director of the Kaiser Wilhelm Institut für Physik
Albert Einstein and magnetic moments
Ampère 1820: Molecular currents postulated  Magnetism linked to angular momentum
Einstein–de Haas 1915: Experimental demonstration  Agreement with theory (at that time!)
Improved measurements  Einstein’s only experi-ment off by factor 2 !  explained by electron spin
Understanding the spin of hadrons remains a puzzle
  Shall we believe experiments by theoreticians if they know already the result?

## Slide 5
Fixed target spectrometer experiments: CERN-Munich (PS)  ACCMOR SPS (1970-1989)
Fixed target spectrometer experiments
Physics studied:
  - Hadron (meson) spectroscopy: unflavoured, strange and charmed hadrons
  Hadronic production mechanism (model independent analyses, meson exchange and soft diffraction)
   More than 100 publications
Challenges:
  - Large acceptance  large tracking detectors
  Precision measurement of angles and momenta
  Particle identification  large, multicell C-detectors
  High statistics  selective trigger + state-of-the-art DAQ
  (for the time) very complex analyses
17.2 GeV/c beam
CERN-Munich Spectrometer
8 m
30 m
WA-3 SPS-W-hall  NA12/32 SPS-N-hall
up to 220 GeV/c

## Slide 6
Fixed target spectrometer experiments
(up to) 80 huge high precision spark chambers (in NA32 drift chambers):
  Largest chambers: 4m x 2m – simple but effective and reliable design (lived for 15 years!)
  Electronics (magnetostrictive) read-out with inductive pick-up coils
  Position resolution: 200 mm ! + precision overall alignment of detector components
  Elegant + precise set-up allowing for easy servicing and change of spectrometer geometry!
+ Large multi-cellular Cernkov counters  expertise later used in HEGRA MAGIC CTA
  After 1980: Si-detectors with ~ 5 mm resolutions were pioneered in NA-32 (CCDs+Si-strips), which made extension of program to charm possible
large spark chambers of the CERN-Munich experiment

## Slide 7
Fixed target spectrometer experiments
CERN-Munich +: E-hall of the CERN-PS ↓
WA3: W-hall of the CERN-SPS 
  Pioneered fixed target spectrometers  template for many experiments

## Slide 8
E-, B-field
particle
Large volume gas tracking detectors: streamer chambers and TPCs
Large volume gas tracking detectors
Aim: (for study of high-multiplicity events at colliders and fixed target (heavy ion) experiments)
- Complete and precise 3-dimensional reconstruction of complex high-multiplicity events with minimal material
- Charged particle identification using ionization (dE/dx)
MPI: development to perfection of streamer chamber and time projection chamber (TPC)
Principle of operation of TPC:
Charged particles ionize chamber gas
Electrons drift (up to 2.5 m) in uniform E- and B-field to chambers on end plates
Chambers measure pulse shape  from position and time  3-dimensional position measurement
Resolution (ALEPH) sr,f = 170 mm
sz = 750 mm
for wire- or other chamber

## Slide 9
Large volume gas tracking detectors: TPC
Large volume gase tracking detectors
TPC: LBL – Pep4: pioneering work – but still lots of understanding and improvement needed
MPI: Development to perfection of time projection chamber (TPC) + leading role in construction and exploitation for physics of a number of TPCs
1983: TPC 90  working horse for an in-depth understanding of a large volume TPC:
- Diffusion of drifting electrons
- Gas amplification in strong E/B-fields
- “Laser tracks” ionisation
- Gas chemistry and purity
- Response function + electronics
- Optimization and test place
for read-out chambers and
read-out electronics
- …
A “Musterbeispiel” how to syste-
matically solve a complex
experimental problem and train
excellent students and post-docs
1.2 Tesla field
90 cm
TPC 90: entirely built in MPI-workshop

## Slide 10
TPC 90: R&D on gaseous detectors
 Much of the work found its way into textbooks:
Large volume gaseous tracking detectors
TPC 90: entirely built at MPI-workshop

## Slide 11
 ALEPH TPC
after connecting 47000 cables!
Large volume gaseous tracking detectors

## Slide 12
 ALEPH TPC: some events at LEP (e+e-interactions up to 209 GeV centre-of-mass energy), which demonstrate the impressive performance and pattern recognition abilities
91 GeV
200 GeV
161 GeV
161 GeV
Physics results:  for precision electro-weak physics  talk by D.Schlatter
3 jets at Z0
3 jets at W+ W- threshold
m + 2 jets at W+ W- threshold
4 jets at the highest LEP energies
Large volume gaseous tracking detectors

## Slide 13
 CERN NA49: TPC for fixed target heavy ion interactions
NA49 TPC: field cage
NA49 charged tracks from heavy ion collision
Large volume gaseous tracking detectors

## Slide 14
 NA49 TPC  STAR TPC  ALICE TPC: most impressive tracking performance
Large volume gaseous tracking detectors
Au + Au @ 140 AGeV
  A development which has shaped experimental particle physics

## Slide 15
 NA49 TPC  STAR TPC  ALICE TPC: most impressive tracking performance
Large volume gaseous tracking detectors
Au + Au @ 140 AGeV

## Slide 16
 STAR TPC: most impressive tracking and particle identification performance
+
 R&D for further improved TPC for ILC
Large volume gaseous tracking detectors

## Slide 17
Calorimetry and associated electronics: liquid argon CELLO  H1 ATLAS (+ 4p calorimetry for fixed target experiments (NA5), low T calorimeters for WIMP-searches, crystal calorimetry with Si-sensor read-out, non-hep applications and many more)
Liquid argon calorimetry
At the heart of every collider detector: tracking ∙ calorimetry
Challenges and requirements:
- Energy and position measurement of electrons, charged and neutron hadrons over entire solid angle + missing energy “measurement”
- Uniformity of response (%); stable calibration and reliable operation in hostile environment
- Particle identification: e/g – hadrons – m’s
- Timing (adapted to bunch crossing rate of collider: 100 ns@HERA and 25 ns@LHC
- Fast signal for trigger decision – to select the rare interesting events
Technology chosen at MPI: liquid Ar (LAr) sampling calorimeters
Challenges of LAr:
- Pulse shaping (speed) ↔ electronics noise (capacitance!)
(+ large number of channels + complex el. connections
 ATLAS: “cold GaAs electronics !)
- Purity (electron life time) need << ppm
- Mechanical tolerances + HV stability
- But: LAr is intrinsically radiation hard
with CELLO (PETRA)  H1 (HERA)  ATLAS (LHC)
I (t)
Q(T) = ∫I (t)dt
after pulse-shaping with tp=50 ns
no pulse-shaping
25 ns bunch crossing of LHC
MPI world-leading centre to master such challenges

## Slide 18
LAr calorimetry@MPI:
CELLO LAr calorimeter
H1 LAr calorimeter
H1 LAr calorimeter
ATLAS end-cap
Liquid argon calorimetry

## Slide 19
Solid state detectors: NA11/32  ALEPH  ATLAS  Röntgen Astrophysics  BELLE II  …
Silicon detectors
After discovery of charm (1974), t-lepton (1975) and beauty (1977) with lifetimes ct ~100 mm: need fast (ns), and precise (mm) electronic tracking detectors
1980 J.Kemmer (TUM): highly developed Si-technology transferred to detector-grade (kcm) material
“Miniaturized” low-noise amplifiers in thick field hybrid technology available (at MPI electronics workshop!) and hep groups started with VLSI design
1980: NA11 collaboration (NB first Ringberg meeting!)
20 mm
 develop Si detectors (micro-strips (MPI) and CCDs)

## Slide 20
1981: first detectors in beam:
24 x 36 mm, 1200 strips
20 mm strip pitch
60 mm readout pitch
- Area Si telescope: 0.01 m2
 5.4 mm accuracy
 100 % efficiency
- Built at the MPI-workshop a high resolution vertex detector (6 beam + 6 vertex detectors) with a total of 2000 channels running in early 1982
Silicon detectors
A major break-through in electronic detectors

## Slide 21
p+
K+
K-
production + decay
DS p+ F( K+K-)
NA11/32 results on charm:
- Precision mass measurements: D0, D, D*(2010), DS, Lc, c+, c0 (in several cases best mass values and first identified decays)
Lifetimes D0, D, D*(2010)+, DS, Lc, c+, c0, and branching fractions,
Hadronic production of charmed particles at (relatively) low energies (QCD)
MPI+TU have been the starting point of the success story of silicon detectors now used in all collider experiments
and
MPI (HLL) continues to play a leading role
and
major impact on novel applications of silicon detectors in many fields
Silicon detectors

## Slide 22
MPI became the leading semiconductor detector laboratory in the 80-ies
1983: 3rd European Symposium on Semiconductor Detectors at Munich
Silicon detectors

## Slide 23
Solid state detectors: NA11/32  ALEPH  ATLAS an impressive development
Aleph silicon detector (version 0  exhibited here at MPI !)
version 0: operating in ALEPH 1990-1991
73 728 channels; d = 12 mm x 12 mm,
first “double-sided” vertex detector at collider,
lifetime Bs and t; -mixing + much more
Silicon detectors

## Slide 24
Silicon detectors: NA11/32  ALEPH  ATLAS an impressive development
ATLAS silicon tracker
15 552 sensors – 61 m2
~80 mm pitch, 5 mm alignment accuracy
rad. tolerant for > 10 y LHC operation
Silicon detectors

## Slide 25
Silicon detectors: Si-drift chambers and further developments
Position resolution using laser spot
using beam particles
Principle of Si-drift chamber (Gatti+Rehak)  shaping the E-field inside of detector
3 mm -
n+ anode
p+ field
shaping
electrodes
3 mm resolution
Silicon detectors
MPI attracted leading Si detector experts
n+

## Slide 26
Solid state detectors: Cylindrical drift chamber for high resolution X-ray spectroscopy
- Low capacitance (~ independent of area) + on-detector FET  energy resolution: 121eV@6keV (-10°C)
- Back irradiation  ultra-thin “window”  low Eg !
Applications in industry, research, art, ….
 portable XRay-fluorescence system
X-rays
55Fe X-ray source
Silicon detectors

## Slide 27
Solid state detectors: DEPFET pixel detector
50-500mm
- Sideward depletion (Si-drift chamber)
- Potential minimum for e- ~1mm underneath transistor channel by “deep” n-implant
- Transistor channel steered by external gate and by internal gate
- Very low C (~fF)  low noise (<1e for circular structure, 10 e for linear structure)
- Achieved amplifications ~400pA/e (int. gate)
“Outstanding” performance  R&D and sensor production for:
  - vertex detectors  BELLE II in Japan
  - X-ray astronomy
  - Photon-research
  - Bio-medical applications, …
Matrix readout (e.g. ILC 13x100mm2 25mm2 pixels-5W):
- connect gates/clears horizontally to select/clear signal rows
- connect drains(+sources) vertically and amplify I or V  no shift of charge !!!
- sequence: enable row  read (Isig+Iped)  clear  subtract (Iped)  next row
- read 10x2048 rows in 50 ns (20 MHz)
Silicon detectors

## Slide 28
Solid state detectors: fully depleted npCCDs for X-ray science (astrophysics  SR-research)
Principle of operation (pnCCD)
(CCD = Charged Coupled Device)
Charge from entire detector depth stored below electrodes  Sensitive to high E X-rays
Thin back contact + low noise  Sensitive to low E X-rays Clocking of shift-registers  transfer charge to anodes of low capacitance = low noise (at close to ambient temperature)
 Superior performance
particle or X-ray
XMM-Newton observatory
 deep X-ray sky
deep X-ray sky: 106 sec observation  - distant galaxies with massive black holes
“colours”  info on black holes + surround.
most “blue objects” XMM-N. discoveries
Silicon detectors

## Slide 29
Fully depleted CCDs for X-ray science: view of chemical composition of Tycho supernova remnant
Silicon detectors

## Slide 30
Since > 50 years: One of the leading labs for improving and developing novel photo-detectors for low-light application in collaboration with industry and research labs
Low-light photo detectors
Detector types:
“Classical” vacuum photomultipliers
APD arrays
(avalanche photodiodes)
SiPMs
(silicon photmultipliers)
Major improvements:
  Photo-detection efficiency
  Wavelength range
  Noise by cross-talk
Major progress in understanding  Enabling novel applications
1440 pixel SiPM camera “FACT”

## Slide 31
Low-light photodetectors used in Cherenkov telescopes for GeV/TeV g astronomy: HEGRA  MAGIC  CTA  pioneering role of MPI in this field of research, but also with major impact on medical applications, calorimetry, sensing, …
High energy g -astronomy
Calibration and alignment
of MAGIC C-telescope at Las Palmas
17 m telescope Ø
g-energy threshold ~25 GeV

## Slide 32
Can one measure a decay with without background ?
GERDA: Neutrino-less double β decay
Yes, they can! (die schaffen das!)
  Is the neutrino its own anti-particle? (since > 50 years a most fundamental question!)
  Isotopes with forbidden β decay: e.g. 76Ge
  76Ge enriched crystals + pulse-shape analysis
  Ultra-clean materials + shielding + vetos
H2O
LAr
Ge
-veto
enriched 76Ge detector

## Slide 33
100 years MPI-Physik ≡ (also)
Excellence in detectors and their use in innovative experiments
Apologies to all the excellent work, which I did not mention – thank you for providing me with information
Summary I

## Slide 34
Many thanks to the visionary founding fathers of the Kaiser-Wilhelm-Institute for Physics 100 years ago
Summary II
Karikatur auf die Gründung der Kaiser-Wilhelm-Gesellschaft.
Untertitel: “Beim Friedensfürsten.
Die drei Könige aus dem Morgenland bringen ihre Weihnachtsgeschenke”
(aus A. Hermann, Die Geschichte der Deutschen Physikalischen Gesellschaft 1899–1945)