## Slide 1: DAQ system design.
Overview
Introduction.
EDET. Data flow.
DAQ tasks.
Questions & Solutions.
Resources overview.
Hardware & Software + time*manpower.

## Slide 2: DAQ system design.
What is EDET aiming for?
80 000 Hz
1 Hz
Large molecules interaction,
Substance structural changes.

## Slide 3: DAQ system design.
How does should it look like?
Detector FPA consisting of 4 individual, independent modules.
Each quarter consists of DEPFET ASM together with electronics and mechanical support
DEPFET matrix 512 x 512 pixels
1 Mpixel = 4 x 512 x 512 pixels
Real-space imaging in the focal plane of a TEM
Grey-scaled image
512x512 pixels
Shielding
e-
Switcher
DCD
DMC

## Slide 4: DAQ system design.
DAQ. Initial approach datapath overview.

## Slide 5: DAQ system design.
DAQ. Actual approach datapath overview.
Point of the most interest for today‘s topic.

## Slide 6: DAQ system design.
All-silicon module (ASM).
DCD x 8
Matrix
512x512
DMC(DHPT) x 8
SRAM buffer
for 102 frames;
LVDS driver;
8 x 8
digital
lines
Analogue
lines

## Slide 7: DAQ system design.
DAQ. Actual approach datapath overview.
DLSP(pcb)
LVDS buffering
Simulation shall give us an answer, whether to use the buffer or painlessly bypass it (ChK).
8 x DMC
(DHPT)
8 x 8
LVDS lines or
(8 x CML lines)
Notes: A candidate to be removed from the design.

## Slide 8: DAQ system design.
DAQ. Actual approach datapath overview.
MIC(+MIC Service Module(MSM))
DLSP
64 x 320 Mb/s LVDS pairs
20,48 Gb/s
Notes: We have entrusted the data handling to a high-end Xilinx SoC populated on a very compact PCB with and I beleive we made a right choice. By the next slides I‘ll show you why I think so.

## Slide 9: DAQ system design.
DAQ. Actual approach datapath overview.
Network and Storage array
MIC
2 x 10GBASE-SR
Requirements:
Write rate 8GB/s
Capacity enough for 1 hour

## Slide 10: DAQ system design.
EDET backend firmware tasks.
Provide data path from the sensor to the storage (excluding new bottlenecks if possible);
Metadata encapsulation;
Configuration data delivery to every part of the system in vertical direction;
Inter-module link communication:
  Trigger and clock distribution to the neighboring tiles;
  Configuration data delivery in horizontal direction and monitoring data transition;
Houskeeping:
  Power module;
  DLSP;
Operator UI;
Trigger signal generation(!)
Notes: Splitting the DAQ system into several independent tasks.

## Slide 11: DAQ system design.
Programmable logic
High speed data path. Test mode.
DHPT data generator/checker
Aurora IP 1,6Gb/s
8b10b
AXI interconnect
16
16
Loopback
64
XG Ethernet
UDP/IP/MAC
Loopback
64
PCS/PMA
16
1
2
3
5
7
8
9
64
64
1
2
3
4
4
5
6
7
8
9
6
Notes: Splitting the DAQ system into several independent tasks.

## Slide 12: DAQ system design.
Programmable logic
Metadata encapsulation.
Aurora IP 1,6Gb/s
8b10b
AXI interconnect
8
64
XG Ethernet
UDP/IP/MAC
PCS/PMA
SFP+
+
Meta
+
Meta
+
Meta
16
16
16
16
16
16
XG Ethernet
UDP/IP/MAC
PCS/PMA
64
SFP+
Image reshaping,
Metadata generation and incapsulation
Notes: Splitting the DAQ system into several independent tasks.

## Slide 13: DAQ system design.
Programmable logic
Vertical configuration
AXI interconnect
IP
Processing system
IP
IP
JTAG
Linux Kernel
User software
File system
DCD: >80
DHPT: ~60
DMC: ~50
1. Where to keep configuration data(MIC or Network)?
2*. How to configure the tool? (SSH, xUI)
3*. How and where to keep track of state changes? (text log, CSV, EMACS/CS Studio)
4. Where to keep the filesystem? (Locally or NFS)
Notes: That section gives me more questions than answers.

## Slide 14: DAQ system design.
PL
Inter-module link communication (ILC)
Summary
1G/10G Ethernet link between adjacent tiles;
Wired connection for clock and trigger.
PL
AXI interconnect
PS
Linux Kernel
User software
File system
Aurora OR
USXGMII
MGT
Aurora OR
USXGMII
MGT
Aurora OR
USXGMII
MGT
Aurora OR
USXGMII
MGT
G
M or S
AXI interconnect
PS
Linux Kernel
User software
File system
G
M or S
Notes: That section gives me more questions than answers.

## Slide 15: DAQ system design.
Housekeeping
Command line interface?
eXtended UI (xUI)
Programmable logic
AXI interconnect
I2C
Processing system
Linux Kernel
User software
File system
I2C
I2C
DLSP
MPM
Functionality:
  Configuration,
  Current device state reading,
  State tracking,
  Reports generating.
Notes: That section gives me more questions than answers.

## Slide 16: DAQ system design.
Operator UI.
Processing system
User software
File system
Command line
Graphical
DCD: 83
DHPT: 59
DMC: ~50
Total order ~4,4*103

## Slide 17: DAQ system design.
PL
G
M or S
Filmed time | Blind time
1,28ms (11%) | 10,24ms (89%)
Read-out (Blind) time
F
Blind time
F
Blind time
F
Blind time
Trigger signal generation.

## Slide 18: DAQ system design.
Resources overview.
Hardware
Software
SoC board
MIC service module (in design)
Xilinx devkit
Xilinx synthesis EDA + simulator
GCC cross-compiler
Chart: 
| 1. Passed | 2. Left
Time | 100 | 265

## Slide 19: DAQ system design.
Summary.
High speed data path. Simulated. Ok.
Image reshaping and metadata generation.
Configuration:
  Storage: local initial configuration(RO), local user modified(RW) and Network.
  Type: Database.
Instrument state data:
  Monitor current state with xUI(CS Studio).
  Log past events (EMACS).
Intelligent trigger system.
  Metadata generation.

## Slide 20: DAQ system design.
To be continued…
Thanks for your attention.