PicoScale Interferometer
Stefan Knirck
for the MADMAX working group
Max-Planck-Institut für Physik, München
all information from SmarAct GmbH

---
PicoScale Accuracy
λ ≈ 1550 nm
modulated at
ω ≈ 30MHz, i.e. λmod ≈ 10m
Demodulation gives S(ω), S(2ω)
→ quadrature signal
→ up to pm accuracy
but:	absolute distance accuracy
~ 1mm

---
Sonsor Head
“Sensor Head C02”
low angular acceptance
high working distance
→ Retro-reflector needed
David
Kittlinger
→ reduced accuracy still better than ~1µm

---
Implementation
Retroreflectors

---
Implementation
Retroreflectors
need:
ability to rotate laser heads around beam axis
without displacement in beam direction
Δz ~ few µm

---
Conclusion
Attractive Features:
- high accuracy even at large distance
- 3 channels → measure tilt
- automatic feedback system
  Main Drawback:
- Absolute distance measurement not accurate enough