## Slide 1: Irradiation status & plans
Mitja Predikaka
Edet session @ Kloster Seeon
28/05/2019

## Slide 2: Devices – availability
4 wafers in PXD10:
W09 (50 μm SOI)
W10 (30 μm SOI)
W11 and W12 (450 μm)
6 devices per wafer:
4 without backside imp – TL, TR, BR, BL
2 with backside – ML, MR
none of the devices are backthinned

## Slide 3: Devices - structure
4 quarters: 2 x 80k (of interest) + 2 x 1k
Contacts per quarter:
Gate (sweep)
Clear Gate (sweep)
Drift (not connected)
Source (static)
Clear (static)
PT (not connected, therefore you bias it through 1k Drift contact – common)
Cutting Edge (common)
All Drain (two voltages)
8 x drain for PXs with G length of 3.8 μm
8 x drain for PXs with G length of 4.8 μm
8 x drain for PXs with G length of 5.8 μm
Connections per device: 59!

## Slide 4: Devices – area of interest
300 μm
5000 μm
5000 μm
Area of interest: 800x100 μm2
Area to be irradiated: 1000x300 μm2
1000 μm
800 μm
100 μm
1500 μm

## Slide 5: Setup for Irr. S. (v1)

## Slide 6: Setup for Irr. S. – inside of the Vacuum Box
Device carrier PCB @ HLL
HD DSUB 78 pin male @ HLL (tested with Allectra HD DSUB 78 pin female)
Terminal blocks @ HLL
Coarse positioning of the electron beam

## Slide 7: Setup for Irr. S. – inside of the Vacuum Box
DUTs @ HLL
Ceramics @ in production with A.L.L Lasertechnik
Screws @ HLL (has to be checked, planned is that the ones from SPIX setup fit here as well)
Cold plates @ in production with Thomas Markl GmbH
Due to the Terminal Block connector above
For precise positioning of the electron beam on the edges of DUT

## Slide 8: Setup for Irr. S. – inside of the Vacuum Box
DUTs @ HLL
Ceramics @ in production with A.L.L Lasertechnik
Screws @ HLL (has to be checked, planned is that the ones from SPIX setup fit here as well)
Cold plates @ in production with Thomas Markl GmbH
Due to the Terminal Block connector above
Alignment holes
for precise positioning of the electron beam on the edges of DUT

## Slide 9: Setup for Irr. S. – inside of the Vacuum Box
Peltier elements @ HLL (test of cooling/heating capabilities still pending)
For fastening to the PCB (creation of a sandwitch (CP, Peltier, Ceramics, PCB)
For attaching of ”cold fingers” and temperature sensors (8 x M3)

## Slide 10: Setup for Irr. S. – inside of the Vacuum Box
Peltier elements @ HLL (test of cooling/heating capabilities still pending)
For attaching of ”cold fingers” and temperature sensors (8 x M3)

## Slide 11: Setup for Irr. S. – inside of the Vacuum Box
1 to 1 cable from Allectra
  2 x Peek UHV Female HD DSUB 78 pin
  0.5 m Kapton ribbon cable
  @ to be ordered (production time on the order of 3 weeks)

## Slide 12: Setup for Irr. S. – outside of the Vacuum Box
Breakout PCB:
  6 layer rigid part (19 mm x 70 mm) with 78 pin HD DSUB Female connector
  2 layer flexible part (48 mm x 70 mm)
  6 layer rigid part (160 mm x 100 mm) with
    DUT quarter selection jumpers,
    LEMO connectors for drains,
    TRIAX/Terminal Block connectors for common terminals
    Terminal Block connectors for temperature sensors and Peltier element
  @ PCB to be ordered (asking for quotes – 1 offer from Beta LAYOUT with production time of 16 WD), all other components already at HLL

## Slide 13: Setup for Irr. S. – PSU + DAQ
PSU @ HLL
Keithley 4200A-SCS (9x SMU) @ HLL
Sw. Mat. rack (2x Keithley 708B) @ HLL
Sw. Mat. (2x Keithley 7174A) @ HLL
40k € shipment from yesterday

## Slide 14: Setup for Irr. S. – PSU + DAQ
PSU @ HLL
Keithley 4200A-SCS (9x SMU) @ HLL
Sw. Mat. rack (2x Keithley 708B) @ HLL
Sw. Mat. (2x Keithley 7174A) @ HLL
Simple cable connections to
terminal blocks. GND shared from Keithley over the Breakout PCB.
Triax cables to Breakout PCB; Afterwards only Force line over the PCBs and Kapton cable in vacuum.
Triax cables to the Switching Matrix
40k € shipment from yesterday

## Slide 15: Setup for Irr. S. – PSU + DAQ
PSU @ HLL
Keithley 4200A-SCS (9x SMU) @ HLL
Sw. Mat. rack (2x Keithley 708B) @ HLL
Sw. Mat. (2x Keithley 7174A) @ HLL
Triax –> BNC –> Lemo adapter, Lemo cable, PCBs and Kapton cable.
Triax Cables to the Keithley 4200
40k € shipment from yesterday

## Slide 16: Setup for Irr. S. – PSU + DAQ
PSU @ HLL
Keithley 4200A-SCS (9x SMU) @ HLL
Sw. Mat. rack (2x Keithley 708B) @ HLL
Sw. Mat. (2x Keithley 7174A) @ HLL
Triax –> BNC –> Lemo adapter, Lemo cable, PCBs and Kapton cable.
Triax Cables to the Keithley 4200
40k € shipment from yesterday

## Slide 17: Setup for Irr. S. – Peltier controller
Temperature sensors
4 wire PT1000 for the DUT
2 wire 10kOhm Thermistor for the cold plate
Peltier potentials
Power suppy (12 V)
Computer interface
Controller board (TEC-1089-SV-PT1000) @ HLL
Thermometers @ HLL
Cables for Thermometers @ ordered

## Slide 18: Setup for Irr. S. – hybrid for preparations
Breakout PCB
connector
Already populated and tested devices for the SPIX setup

## Slide 19: Irradiation procedure
  Only 1 device (2 quarters) per Device carrier PCB due to large distances
  2nd quarter more or less safe when 1st is irradiated
  While irradiation:
    all potentials applied to the DUT to mimic real life operation
    gate potentials in the OFF state (4/512 rows are in OFF state during the imaging)
    DUT kept at the fixed temperature: TBD
  Dose rate:
    Ideally we should aim for the same dose rate as in real life operation: 100 e–/px @ 10 kHz; if too slow we will speed it up
  Max Dose: TBD
  Dose step: should be extrapolated from Martin’s thesis
  Measurements between dose steps:
    1st device: frequent measurements to observe the transient behaviour of self annealing(?) until plateau is reached
    2nd device: trying to speed up the transient behaviour through heating (~50 °C) with Peltier element
    rest: 1 measurement after plateau has been reached
From my point we could do 1st irradiation session in the first half of June 2019(?)

## Slide 20: Components provided by MPSD
  Mechanical
  vacuum feedthrough flange – Allectra
  holder for the Device holder PCB – Djordje(?)
  copper braids – Djordje(?)
  copper braids connection sandwitch – Djorjde(?)
  heat sink flange – Djordje(?)
  2D moving stages + software for the control – Djordje and Sascha(?)
  mechanical holder for the breakout board – Djordje(?)
  mechanical holder for the Peltier controller – Djordje(?)
  mechanical holder for feedthrough flange with connected Kapton cable and Breakout PCB for when it is not in use
  Simulations
  dose absorbed by silicon oxide for 450 um thick devices – Ibrahym(?)
Please give me an estimation about timeline.

## Slide 21: Annealing studies
    ?
regular studies with heating of the DUTs in the oven
modification of planned laser annealing system (timeline?)

## Slide 23: Setup for Irr. S. – Keithley connections
Keithley Model 4200A-SCS Parameter Analyzer
Reference Manual Jan. 2019
page 2-7 (38/1606)
Keithley - Low Level Measurements Handbook
7th Edition
page 2-18 (56/244)
20/5/19 … Daniel tasked with checking the possibility of floating SMUs … you can bring grounding plane closer.

## Slide 24: Setup for Irr. S.– Vacbox feedthrough v1
High density Sub-D 78 pin from Allectra:
3 A/pin
Cable made by Allectra:
1st end: SUB-D 78-WAY PEEK
Cable: Kapton Ribbon cable 0.5m
2nd end: SUB-D 78-WAY PEEK
Connections (not actual pin numbers):
01 – 60 … for the device
61 – 68 … for the temperature sensors
69 – 78 … for the Peltier element