## Slide 1: The Data Handling Hybrid
TUM Physics Department E18
I.Konorov

## Slide 2: Overview
DHH functionality
Proposal for DHH architecture based on SODA -Time Distribution system for PANDA
DHH design
Project time estimate

## Slide 3: DHH

## Slide 4: Proposal for DHH
Based on our prototype development of Time Distribution System for PANDA
FPGA based, commercial components
Not radiation hard
Anticipated location : DOCK ~2m away from half ladder
*SVD group measured radiation dose in the DOCK recently and within few weeks they accumulated 5 kRad

## Slide 5: DHH functionality
Voltage regulators
Slow control support:
  Provision of JTAG interface to configure PXD
  Provision of slow control interface to configure DHH cards
  Monitoring voltages, currents, temperature
CLOCK synthesis from COMMON clock and distribution
DAQ functionality
  Synchronous distribution of TRIGGER, RESET(?), … signals
  Data buffering : 4x1Gb/sec
  Sub event building : merging 4 data blocks into one
  Transmission of merged data to DAQ via high speed optical serial link

## Slide 6: SODA serial interface
Optical network with STAR topology using passive optical splitters
125 MHz or 1.25 Gb/s now, in future may go up to 2.5Gb/s
Bidirectional link :
  Controller -> Receivers full bandwidth of 125 MB/s
    Broadcast synchronous commands with fixed latency, 32 bit long:
      RESET, Start/Stop data taking, Start/End of burst
    Asynchronous commands , 32 bit long
      Scanning connected modules
      Control
    Packets up to 1kB
  Receivers -> Controller
    Time sharing principle, similar to common bus
    Only one receiver can send data at a time
    Controller schedules Receivers access
    Switching from one receiver to another takes 400 ns
      Laser OFF - Laser On – Relock SERDES to new receiver
    Heartbeat packet
    Status packet
CNTR
RCV
RCV
RCV

## Slide 7: SODA –PANDA time distribution system
SODA controller :
  Provision of 155.52 MHz reference clock, 10ppm or better
  Provision of RESET, Burst, SuperBurst, Start/Stop
  PC interface for configuration and status information
  Lattice FPGA with SERDES
Optical splitter :
  1x8; 1x16; 1x32
SODA receiver:
  Mounted directly on Data Concentrator/Multiplexer module
  155.52 MHz
  RESET, SOB, EOB, Start/Stop
Passive splitter
1x8, 1x16
SODA
controller
PCI-e
HESR
SODA
receiver
Multiplexer/
Data Concentrator
  155.52 MHz
  Reset
  Burst
  Start/Stop

## Slide 8: SODA interface
8/10 bit encoding
Command(packet) transmission/handshake
IDLE status
Synchronous command:
  RESET, SOB, EOB, SuperBurst, Start, Stop, Trigger, 3 spare bits
Asynchronous commands
0
10 bits
ECC(5b)
K28.7
K28.7
K28.7
K28.7
K28.7
K28.7
1
8 bits
ECC(7b)
K28.7
K28.7
K28.7
K28.7

## Slide 9: Test setup
Lattice PCI-e evaluation card
Optical splitter 1:8
2x SODA receivers mounted on evaluation cards
Reference Clock vs Recovered Rx Clock
10ps/div
RMS 15ps

## Slide 10: Proposal: DHH card design
to DAQ
to DHH Controller
DHH design based on commercial components :
  FPGA(Lattice/Xilinx)
  Optical transceivers

## Slide 11: Proposal: DHH system architecture
FPGA
PCIe , USB, Ethernet
JTAG
Trigger
Clock
DHH Controller
Reset
Ackn
Belle
Trigger
Distr.
System
RJ45

## Slide 12: DHH  Trigger interface
Belle II Trigger Distribution System provides:
  LVDS: Common clock – 127 MHz (508.87 MHz/4)
  LVDS DDR Serial link 254 Mb/s: Trigger, Hard Reset, Soft Reset, Event number(8 bits)…
DHH :
  Trigger Acknowledge LVDS within 30 us after trigger
*@PXD-DAQ work shop Japanese colleagues proposed to come with trigger copper cable directly to DHH cards
  Issues to be addresses:
    Grounding
    Additional interfaces for Slow Control and JTAG
  No final decision yet, although advantage of optical network solution was acknowledged

## Slide 13: DHH  DHP
DHH generates two clock signals
  Frame clock: 508.87 MHz/10240 = 49.69 kHz (~20 μs period)
  Switcher clock: 508.87 MHz * 5/32 = 79.5 MHz or 508.87 MHz * 3/20 = 76.3 MHz
Propagate Soft/Hard RESET signal ?
Convert pulsed trigger signal to level trigger signal
Belle Trigger
DHP Trigger

## Slide 14: DHHDAQ
Compute
Node
Compute
Node

## Slide 15: PXDDHHDAQ interface
PXD => DHH
  4 copper serial links, 1.5 Gb/s each
  Aurora protocol, 8/10 bit encoding
  One data block is one or more events
  Data format defined
  Average network bandwidth utilization – 80-90%
DHH => DAQ
  6 Gb/s or 2x3 Gb/s
  “Sub event” building

## Slide 16: PXD frame timing
Trg M
T
Rows
Part of frame N
Event M
Frame N+2
Event M+1
Part of frame N+1
Event M
Frame N+2
Event M+1
Frame N+2
Event M+2
Trg M+1
Trg M+2
Belle II dead time:
  in current scenario SVD requires not more than 5 triggers in 125us – 18% dead time
  PXD: data block combines up to 5 events 
  Due 18% dead time more probable scenario for SVD is 10 events in 125 us
  Probability for 10 triggers within 180us is 2.6%
  PXD data block is not limited by any number of events

## Slide 17: New collaborator
Ricard Aquilué, from La Salle Engineering – Universitat Ramon Llull, Barcelona
Experience in FPGA designs, High Speed Serial Links
Expressed interest to participate in development of DHH system
Contribution:
  Implementing precise time distribution functionality using Xilinx FPGAs
  Slow Control Functionality by employing soft μP core in FPGA and Linux OS

## Slide 18: Time lines (preliminary)
Requirements and specification - 09.2010
Prototype development - 03.2011
Test, debugging, final specification - 01.2012
Final prototype - 03.2012
Final production - 09.2012

## Slide 19: Summary
DHH location to be defined
Radiation conditions to be clarified
Trigger interface specified - OK
Trigger distribution scheme to be defined
  via DHH controller
  Directly to DHH card
Maximum number of events per data block is not limited
Introduce PXD dead time to limit number of events ?
DHP DHH interface in progress
Goal:
Fix DHH specification by September 2010 !!