## Slide 1
Project 200
Technical Meeting
Overview
Dagmar Kreikemeyer
Jan 24th 2022

## Slide 2
Mechanics Prototype: Project 200
  Purpose: verifiy feasibility of 3 piezo motors moving one disk along a 200 mm rail at cryogenic temperatures in a vacuum volume. Study the temperature distribution along the hardware. First tests with absolute position interferometer.
1
2
3
4
5
6
530 mm
300 mm
1- Cu mirror (fix position)
2- Sapphire disk (adjustable position)
3- P200 backbone structure
4- (3x)piezo motors
5- interferometer incoupler
6- interferometer outcoupler
Weight < 20 kg

## Slide 3: Timeline
Design  2020
Production of the parts  June to September 2021
Assembly in Hamburg  September 2021
Purchase of Attocube interf. as back-up system  November 2021
Modifications  November/December 2021
First tests of the motors inside the setup  January 2022
Installation of Attocube Interferometer  January 2022
Programming of an interface between Attocube and JPE  Nov 2021 to Jan 2022
NEXT STEPS:
Tests of three motors together  January /February 2022
Test setup at 4 K (Cryolab, CERN) using Attocube interf.  Feb/March 2022
RF measurements with P200 (Antonios, Stefan)  Spring/Summer 2022
Test setup at 4 K (Cryolab, CERN) using HighFinesse interf.  Autumn 2022
Test setup in a B-field (MORPURGO)  March 2023

## Slide 4: Meeting schedule
 |  | Topic | Speaker | Time
1 | 09:00 | Intro + Overview | Dagmar | 10‘
2 | 09:10 | Project 200 – Status | Christoph | 30‘
3 | 09:40 | Mechanical parts | Barthel | 15‘
4 | 09:55 | Disc support ring | Stephan | 5‘
5 | 10:00 | HighFinesse Interferometer | Christian | 15‘
10:15 |  | BREAK |  | 10‘
6 | 10:25 | Temperature simulations | Antonios | 5‘
7 | 10:30 | Tests in CERN cryostat | Dagmar | 40‘
8 | 11:10 | General discussion | all | 60‘
 | 12:10 | End of meeting |  |