## Slide 1: Data Handling Processor v0.1 First Test Results
Tomasz Hemperek

## Slide 2: DHP01 Overview
Technology
  IBM 90nm – 9 metal layer
  1.2 core / 1.8 IO voltage
Interface
  32 (4x8) 400 MHz inputs from DCD (HSTL18)
  LVDS control signals (clock, trigger, sync)
  CMOS JTAG
  Hi-speed CML output
Internal Blocks
  Common mode correction
  Pedestal subtraction (static and dynamic*)
  Zero suppression (threshold)
  Channel framing and serialization
  DCD offset correction
  Raw data storage up to (2048 rows)
  Sequencer for switcher
  Configurable delays
  Clock generation (PLL)
  Configurable trigger latency (up to 1024 rows)
  Slow control (JTAG)
  ADC & DAC

## Slide 3: Slow control - JTAG
Boundary scan
  EXTEST
  SAMPLE
  PRELOAD
  INTEST
Configuration
  BYPASS
  IDCODE
  USERCODE
  ADC
  BG
  CORE_READBACK
  CORE_REG
  DAC
  DACENC
  GLOBAL_REG
  MEM_ADDRESS
  MEM_DATA
  OFFSET_MEM_ADDR
  OFFSET_MEM_DATA

## Slide 4: DHP – Signal Rates & Data Flow

## Slide 5: DHP Overview

## Slide 6: DHP Processing
Deserializer (1 to 4)
Common mode correction
Buffering for latency
Pedestal correction
Hit Pairing
Readout
Output framing
Processing algorithms are very simple in current version and need to be adjusted

## Slide 7: Operating modes
MEMORY ACCESS
  Allows to access memory block through JTAG interface for pedestal and offset correction.
RAW DATA RECORD
  Storing raw data to memory (support for trigger).
RAW DATA SEND
  Sending through fast output link all memory contents.
AQUSITION
  Normal operation mode where data are going through all processing stages. Support for trigger and latency buffering.
TEST
  Like AQUSITION but new data are not being recorded.

## Slide 8: Common mode
7bit+8bit
=
8bit
8bit
8bit
+ … +
0
1
127
CM
8bit
8bit
0
-
8bit
1
…
-
8bit
127
-
=
0
8bit
=
8bit
=
8bit
1
…
127
store to memory
n
8bit
n
8bit
n
8bit
=
-
to output
Pedestal subtraction

## Slide 9: Hit Pairing
suppressed data
1
3
2
4
5
column | row | orientation | val 0 | val 1
5 bit | 10 bit | 1 bit | 8 bit | 8 bit
pairs are send out
Parallel pair search (2 rows at a time)
Output data format (24 bits)

## Slide 10: DHP01 - Layout
Prototype with 32 input chip
OFFSET
MEORIES
OUT FIFO MEORY
ANALOG
CML TX
2xPLL
HSTL RX
RAW DATA
MEMORIES
RAW DATA
MEMORIES
LVDS RX
~5.5mln transistors
2mm
4mm

## Slide 11: DHP01 – Bump bonding

## Slide 12: DHP01 + DCDB

## Slide 13: Test Setup
Xilinx XUPV5-LX110T
Ethernet
TCP/IP
GPIO
SMA/Coax
Ethernet
UDP/IP

## Slide 14: FPGA System Overview
Microprocessor responsible for receiving commands (TCP/IP) and controlling chips
Independent high-speed (UDP/IP - close to 1Gbit/s) for data

## Slide 15: Simple Application

## Slide 16: Testing till now
Working:
LVDS Input
HSTL like Input (from DCD)
Slow control (JTAG)
Memories read/write
CML Hi-speed link (tested up to 1.555 GHz) data transition
Input readout
Patter generator
DAC
Bend Gap
To Do:
Processing (different configurations)
DCD communication and synchronization
More High Speed testing

## Slide 17: Power
Measurement conditions:
  1.2 V, 400MHz (100MHz Core)
Current consumption:
  CML TX - ~25 mA
  2xPLL - ~5mA
  digital core - ~60mA

## Slide 18: PLL and CML
1.5552 GHz – data transmission (random 8b10b)
WB + ~5 cm PCB + SMA +~40cm coaxial cable + SMA
100 ps/div
100 mV/div

## Slide 19: Problems till now
Looks like CMOS output pads can work till ~100MHz (200MHz when bump bonded?) so unable to test with DCD at 400 MHz
Configuration of one PLL output (slow one) not fully accusable (simple bug known from submission) there is a workaround
Wrong input data format

## Slide 20: Timeline
Finish test setup to be ready for hi-speed data accusation
Prepare setup with DCDB
Radiation tests
DHP 0.2:
  still half size
  add custom I/O and bias
  Redesign serializer to final version
Need to develop “final” processing algorithm

## Slide 21: Thank to
Bonn:
  Hans Krüger
  Andre Kruth
  Mikhail Lemarenko
  and others
Barcelona:
  Albert Comerma
  Angel Dieguez
  Lluıs Freixes
  Eva Vilella
  and others

## Slide 22: Extra slides

## Slide 23: Performance

## Slide 24: Embedded Development Kit

## Slide 25: Our system

## Slide 26: Transmition