## Slide 1: DHH architecture: outcome of DXP-DAQ workshop and few other topics
Igor Konorov
TUM Physics Department E18

## Slide 2: DHH architecture
PXD-DAQ workshop : to choose one of two DHH architectures:
  TUM proposal based on optical distribution system
  KEK Trigger group proposal with direct Trigger interface to DHH module

## Slide 3: Proposal for DHH system architecture
DH Hybrid
DHH Controller
Belle II
Trigger
FPGA
USB ,
Ethernet
RJ45
DHH design :
  FPGA(Lattice/Xilinx)
  Optical transceivers
  Power module
DHH functions:
  Optical network: Trigger, DAQ, Control
  Power
Giessen Box
Power Supplies

## Slide 4: Alternative DHH architecture
Belle Trigger group(KEK) proposed:
  trigger interface directly to DHH module
Possible scenario:
Belle II Trigger
Box
FPGA
SFP
RJ45
Ladder’s flat
cable connector
PIGGY-BACK
Power Module
POWER
CONNECTOR
JTAG
Slow Control
DAQ
Slow Control
Box
Copper
interfaces

## Slide 5: New feature of Trigger Dist.System

## Slide 7: Nakao-san’s proposal
RJ45, Trigger
RJ45, JTAG

## Slide 8: DHHDAQ links
1 x 6 Gb/s or 2 x 3 Gb/s
Agreed 2 x 3Gb/s !!!

## Slide 9: CLOCK requirements
Belle II Trigger distribution provides:
  127 MHz = 508.87 MHz/4
Clock for DHP serial links
  101 MHz = 508.87 MHz/5
  Can be asynchronous ?
Clock for Switchers: GCK = F0 · SW_channels/1280:
Virtex 5 DCM capability (Fclkfx):
Fout = Fin · M/D
M any integer : 2-33
D any integer : 1-32 To be tested
192/1280 = 3/20
224/1280 = 7/40
216/1280 = 27/160
210/1280 = 21/128
204/1280 = 51/320
168/1280 = 21/160

## Slide 10: Starting prototype design
Specification to be defined
  DHP  DHH interface
  Power connectors
  Internal features
    Memory

## Slide 11: DHH location
First scenario:
2-3 m away
In Dock
Passive Patch Panel
High neutron flux
Too high SingleEventUpset rate
Loss of configuration information
Second(current) scenario
10 m away
No radiation
Patch panel
  Passive ?
  Active I: signal conditioner for Serial Links
  Active II: radiation hard laser drivers and optical transceivers (GBT components)
30-50 cm
Kapton
Flat cable
2 m
Patch
Panel
30-50 cm
Kapton
Flat cable
10 m
Patch
Panel
1 Gb links just enough for 1% occupancy
Do we want to have more safety margin?
With passive patch panel it will not be possible

## Slide 12: DHH  DHP
  Probability for 10 triggers within 180us is 2.6% =>
Convert pulsed trigger signal to level trigger signal
Belle Trigger
DHP Trigger
one frame
HEADER
TRAILER

## Slide 13: Questions: external memory for buffering
Does DHH needs memory ?
  4x1 Gb/s incoming links
  2x3 Gb/s outgoing links
  No need memory
How to merge data ?
  Sub frame wise
DHP
DAQ
DHP
DAQ

## Slide 14: Prototype design
Flexible design compatible with optical, active and passive Patch panel
Objectives
  Hardware for development internal DHH interfaces, firmwares for trigger distribution and clock synthesis
  Provide more compact card for DHP readout
  Provide card for evaluation DHP  DHH interfaces

## Slide 15: Summary
DHH architecture
  mixed , compatible with both proposals
Switcher frequency
  no real limitations but still to be tested
  options with odd multiplication coefficient > 21 to be excluded
Flexible prototype design