FPGA firmware development overview
Synergies between projects
vision of the future
Ringberg, December 2022

---
Agenda_clipboard0
generalization of tasks (daq system)

---
Hardware candidate
Highlights
Built around Xilinx's Zynq Ultrascale+™ MPSoC
DDR4 SDRAM with Error Correction Code (ECC)
19.2 GByte/sec memory bandwidth
Offers PCIe® Gen2 x4, 2x USB 3.0 and 2x Gigabit Ethernet interfaces
Available in industrial temperature range
Three 168-pin Hirose FX10 connectors with 294 user I/Os
Linux BSP and tool chain available
Powerful and compact FPGA board

---
FPGA: Tool chain & workflow
Chosen set
SystemVerilog
Vivado HLS
Cadence Xcelium
Vivado NPM (tcl flow)
Git
PL requirements
Reproducibility
Fast simulation
VCS

---
IP cores
High speed links
Aurora
UDP/IP XG Ethernet
JESD204B (upto 12.5Gbps)
Interconnect
AXI(S,L) switch
AXI-SRAM interface converters
SRAM-register array (Xilinx primitive ports and PL settings)
SRAM-DRP(Xilinx primitives DRP)
PL to PS’ DDR
Data handling
CDC
AXIS data remap
Slicing
Meta data encapsulation
Header handling
Data processing
Dark/Offset correction
Common mode correction
CTI correction
Linearity correction
Stacking of up to N frames
Data reduction for spectroscopic application
Peripherals
SPI
GPIO
Version footprint
S7 sequencer
DHPT/DMC TRG sequencer
Debug
JTAG over TCP/PS
Registers and DP memory
*No proprietary solution used, no license fee paid

---
EDet80k firmware brief
Data path
Scalable
Reusable
data
dummy
gen
data
dummy
gen
1. Filtering
2. Remapping
3. Header handling
4. Slicing
5. Sending

---
FSP+TNG firmware brief
Data path
Scalable
Reusable

---
Edet and FSP+TNG IP cores utilization
EDET only	Common	FSP+TNG only
Peripherals: DHPT/TRG sequencer	Interconnect	Peripherals:SPI
HSL: Aurora	Peripherals	Peripherals:S7 sequencer
	HSL: UDP/IP XG Ethernet	Data processing
	Debug	HSL: JESD204B
	Data handling

---
project hierarchy: fsp & edet

---
Processing system
Unified for projects
Centralized network boot
SDRAM based filesystem
Rich package set

---
Future steps
Workflow related:
- Update Vivado tool version (used 19.2, latest 22.2)
- Increase verification coverage
- Automate verification/build process
  (day: HDL, night: verification and build if success)
Project oriented:
- EDET:
  - Improve TRG sequencer to meet DMC capabilities
  - Enable second 10G link
- FSP+TNG
  - Improve JESD204B to rev. C
  - Implement data processing block (HLS)
- Common
  - Update Linux filesystem (add requested packages)
  - Switch to a newer kernel(?)

---
PS PL firmware
Thank you for your attention
Questions, suggestions, remarks are welcomed.

---
EDet80k block scheme
Data path
Firmware

---
Tasks and challenges
- Boot up (QSPI, DHCP, FSBL, UBOOT, Linux, filesystem, device tree, drivers, etc.)
- Configure the firmware, know the status
- Simulation
- Get, process and transmit the data
- Debug
- Transfer knowledge (how to use)

---
Firmware debug
Old

---
Firmware debug
Less cables – less problems
HW: TCP
PS: Linux + Driver + Software
PL: IP core

---
FPGA utilization

---
Tools used
- HDL: (System)Verilog, VHDL
- Scripting: Shell, TCL
- Software: Xilinx Vivado, Cadence Xcelium
- Packages: Linux, Buildroot, Uboot, etc.
- Paradigm: command line interface, scripting

---
TESTBENCH
Add-on

---
documentation
Wiki pages / git repositories
https://fsteam.hll.mpg.de
http://persei.hll.mpg.de:3000/