## Slide 1: Overview: Data Archiving & Version Control
Project Review 2022 – Martin Hensel

## Slide 2
Outline
Archiving vs. Version Control
Different kinds of Data
Accessibility
Version control systems
Product Life Cycle Management solutions
Options, so many options ...

## Slide 3: Archiving versus Version Control
  Backup the data, possibly on multiple locations (redundancy).
  Control accessibility (user access control).
  Timestamped (time of archivation/file creation)
  May reduce data size (compression)
  Can accomodate all data types.
  Track how data changes over time.
  Track who changes the data (commiter).
  Define snapshots (commits).
  Acts as a time machine for data.
  Allow diverging timelines (branching).
  Allow converging timelines and provide ways to integrate changes from different timelines into one (merging).
  Best used for text data, most functionality not usable or not optimized for binary files.
Archiving
Version Control

## Slide 4: Different kinds of Data
Versioning
Archiving
  Compiled applications
  Documentation images (png, pdf)
  Schematics
  Board and wafer layouts
  CAD files (3D construction data)
Binary Data
Human Readable Data
  Measurement raw data (xls, xlsx, npy, hd5)
  Analyzed measurements (npy)
  Generated plots (png, pdf)
  Communications (pdf)
  Measurement raw data (csv, txt)
  Communications (e.g. mails, chat)
  System/Client specifiactions
Proprietary
Collaborative
  Source Code, Scripts (py, cpp, hpp, ...)
  Documentation text
  DRC/LVS definitions
  Calibration data
  Step files (finished 3D models)

## Slide 5: Data accessibility
Proprietary Data:
  Wafer design files
  Technology related measurements
  Software & Firmware development
Collaborative Data:
  ASIC design/tests
  System specifications
In between:
  Software releases
  PR plots/measurements
  Documentation
Who can access?
How to gain access?
How to transfer?
Who can transfer?

## Slide 6: Version control systems
  We employ the industry standard: git
  Other tools are available as well, e.g. SVN
  The differences are mostly in administration style and where the data is stored.
On top: Usablility
  User interface to work with the basic system
  A way for collaborators to interact with the data and each other
  Process automation (CI/CD)
  Documentation
  Every binary file type is different.
  Data comparison almost impossible.
  Most version control tools are proprietary
  and handle only a small subset of all possible binary data types.
  E.g. Cadence Design Entry HDL:
  Version control of PCB schematics (HDL) via MS SharePoint server.
  But no support for PCB layouts (boad files), although created with the same software suite.
Human readable files: Industry standard
Binary files: It‘s complicated

## Slide 7: Product Life Cycle Management
  Project planning and time tracking
  Work force deployment and load optimization
  Manufacturing process tracking
  EDM integration (e.g. SAP orders from BOM)
  Management sugar: colorful plots about nothing
  Issue tracking
  After-production: marketing, rollout
  Knowledge bases and documentation
  Efficiency scoring (e.g. yield analysis)
  And many more
  it may be the only solution that encompasses a good chunck of a development task, e.g. PCB design from schematic, via simulation to layout.
  it can be used as a common interface between several individual version control systems and bridge the gaps left by them.
  that may be true, it can be a total waste of time and man- power to manage such a system.
Many tools provide much more functionality:
This sounds like a lot, but ...

## Slide 8: Disclaimer
The following slides can only show a small part of the available products that can be used to perform the described tasks. The presented lists cannot – and are not intended to – be complete representations of the market.
I have worked with some of the tools in the past. That introduces an inherent selection bias for some tools over others, based on previous experiences and ignorance about possibly superior alternatives and recent developments.

## Slide 9: Options – Firmware and Software
 | Gitea | Gitlab | Stash (Atlassian)
Location | Self-hosted | Hosted (GWDG) | Hosted (tbd)
Administration | mhe + vtravalja | GWDG + HLL | Hoster + HLL
Repo Structure | Organization, Project | Group, Sub-group(s), Project | Group, Project
User Structure | Organization, Team | Group, Permission | Group, Permission
Issue tracking | Integrated | Integrated | JIRA (Atlassian)
Documentation | Project wiki | Group wiki, Project wiki | Confluence (Atlassian)
Automation | Possible, but no experts available on site | Implemented, runners on HLL machines TBD | Implemented (bamboo), runner location TBD
Collaboration | Only internal | GWDG members and external via guest account | Everyone is external anyways
Price tag | Free (+ mhe & vtravalja) | Basic version free | TBD
For firmware and software development on git basis:

## Slide 10: Options – 3D Modeling and CAD
  Design workflows and automation steps (e.g. fill out drawing blocks with revision data).
  Manage revision and approval permissions and requirements.
  Document history and access to old versions.
  Check-out-check-in system to lock files.
  Branching and merging of designs for prototyping and experiments.
  But no coworking on the same file, no merging of changes from different users on the same file at the same time.
  https://www.solidworks.com/de/product/solidworks-pdm
  https://www.autodesk.com/products/vault/overview
Solidworks – Solidworks PDM
Autodesk – Autodesk Vault

## Slide 11: Options – Wafer Schematics and Layouts
ClioSoft SOS7 – Available from Europractice:
  Complete version tracking, branching and merging of design files.
  Check-in-check-out based editing: Lock the file you are working on so no other users can change it until your edits are done.
  Visual differences view to compare versions of layouts and schematics.
  Seamlessly integrates into Cadence Virtuoso and Library Manager and extends some functionalities like working on multiple files.
  Integrates into issue and bug tracking systems e.g. Atlassian JIRA.
  https://www.cliosoft.com/products/sos/
  https://www.europractice.stfc.ac.uk/tools/cliosoft.html

## Slide 12: Options – Cadence PCB design Suite
  Included in Europractice package 17.2
  Has to be set up for our group with a central server instance.
  Check-out-check-in system to lock files, pages or hierarchy groups for editing.
  Revision tracking.
  Link for more information
  Available since 16.6 even better in 17.2
  Server based or individual system.
  Open a session for several people to collaborate on the same layout.
  No direct version control.
  Link for more information
PCB Schematics:
Allegro EDM
PCB Layout:
Symphony Team Design
  Work in progress by our new expert Sharif.
Footprints and Symbols:
Central Library
Allegro Pulse
  Version control, product life cycle management
Link for more Information

## Slide 13: So many options – Which one to take? – Discuss!

## Slide 14: Thank you for your attention For questions please contact:
Max Planck Society – Semiconductor Laboratory
  Martin Hensel
  Otto-Hahn-Ring 6
  81739 München
  Tel.: +49 (0)89 839400-0 Fax: +49 (0)89 839400-11
  E-Mail: hll-info@hll.mpg.de Internet: www.hll.mpg.de