## Slide 1: Towards an automatic mode of operation of the MAM subsystem of MAGIC
Angela Bautista
Presentation for the DPG SMuk Spring Meeting
23 Mar 2023

## Slide 2: Ground-based Gamma-ray Astronomy

## Slide 3: Ground-based Gamma-ray Astronomy
Atmosphere
Cherenkov radiation
Extensive air shower
Very High Energy gamma-ray produces shower of secondary particles
Cherenkov radiation: Light emitted when charged particles exceed the speed of light in a medium
Credits:https://tenor.com/view/

## Slide 4: Imaging Atmospheric Cherenkov Telescope (IACT)
Adapted from W. Hofmann
≈ 10 km
Cherenkov light
rayo gamma

## Slide 5: IACT array
gamma-ray direction

## Slide 6: The MAGIC Telescopes
Two 17-m diameter Imaging Atmospheric Cherenkov Telescopes (IACTs)
Detect gamma rays in the Very High Energy range, 20 GeV to 100 TeV
Cherenkov photons used to estimate the energy of the incident gamma-ray
Credits: https://ipa.phys.ethz.ch/research/ResearchProjects/magic.html

## Slide 7: Very Large Zenith Angle (VLZA) Observations
Only the most energetic gamma-rays reach the detectors
Detect gamma-rays with energies above 100 TeV with MAGIC
We can probe particle acceleration up to the PeV range with gamma-rays with energies in the UHE range (above 100 TeV)
The hunt for PeVatrons!
What are they?
We are looking for them with MAGIC!
Credits: van Scherpenberg, J. (2023) Very Large Zenith Angle Observations with MAGIC
Notes: There is a special mode of observation in MAGIC, ZA, image, when the shower develops at ZA higher than 70deg,(vlza), with vlza observations we are getting closer in this search

## Slide 8: Calibration Subsystems
Light Detection and Ranging System
(LIDAR)
Atmospheric corrections using backscattered light from a laser
LIDAR measures atmospheric transmission up to 70 deg zenith angle
NO LIDAR :(
MAGIC Atmospheric Minion (MAM)
Atmospheric corrections for VLZA observations
solution
Credits: Schmuckermaier, F. (2023) Correcting MAGIC Telescope data with the LIDAR
Notes: For the correct analysis of MAGIC data

## Slide 9: The MAGIC Atmospheric Minion (MAM)
Subsystem to correct VLZA MAGIC data
Task: monitor the atmospheric transmission (AT) in real time in the pointing direction of MAGIC using photometry and spectroscopy
11-inch telescope
5-inch telescope
CCD camera
spectrograph
Credits: Pihet, M (2023) MAM Technical Operation Manual

## Slide 10: Plan automatic mode of operation of MAM
How? MAM will track a star in the close vicinity of a MAGIC target and measure the Atmospheric Transmission
Photometric mode:
- Focus on VLZA MAGIC targets
- Identify bright stars for each target
- Calibration of stars selected (we need this to measure transmission)
Requirement: magnitude at airmass zero
Notes: Say what is airmass

## Slide 11: Plan automatic mode of operation of MAM
How can we measure the magnitude at airmass zero?
Repeat this process, we should obtain the same magnitude at airmass zero.
Next step, calculate atmospheric transmission.
More VLZA targets.
Spectroscopic mode, take a spectra and measure the atmospheric transmission
Credits: Pihet, M (2020) Calibration of a photometric filter system with a 5-inch telescope susbsystem of the MAGIC Telescopes
1
2
Measure the magnitude at different zenith angles
Notes: Spectroscopic mode implemented once photometry is ready to use

## Slide 12: Take Home Message
MAM installed at the MAGIC site to correct for the atmospheric effects during VLZA observations
It will measure the atmospheric transmission in real time in the pointing direction of MAGIC
MAM subsystem will be crucial for the hunt of PeVatrons with MAGIC!
Credits: Pihet, M (2023) MAM Technical Operation Manual

## Slide 13: Backup

## Slide 14: Atmospheric Transmission
Flux observed F:
: total flux of a star in units of , number of det. photons per second
: optical depth of the atmosphere, : airmass
Atmospheric transmission T: Fraction of starlight reaching the observer
Atmospheric transmission:

## Slide 15: Flux Measurement
Aperture photometry
Total flux of a star:
-S: total electron count of the star
-n_pix: total number of pixels in the aperture
-Ns: total number of sky electrons per pixel
-F: total count inside of the inner aperture

## Slide 16: Flux Measurement
Aperture photometry with growing curve correction